## Slide 1: Way forward for NR UE URLLC performance requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #96-e
E-meeting, 17 – 28 August, 2020
Agenda Item: 7.8.1.2
R4-2012648

## Slide 2: FR1 High reliability (1)
      Background (Agreed parameters from #94e, #94e-Bis and #95e)
  SCS/CBW: ​
    FDD: 15 kHz/10 MHz​
    TDD: 30 kHz/40 MHz​
  TDD pattern: 7D1S2U, S=6D: 4G: 4U for 30 kHz SCS.​
  PDSCH configuration:
    Mapping type A, symbol length 12, starting symbol 2.​
    Aggregation level: 2 for FDD and TDD
    Max number of HARQ transmissions: 4​
    FDD: No scheduling in slots 0 and 1 (or 19) within 20ms.
    TDD: No scheduling in D slots i, where mod(i, 10) = 0, and S slots
  Antenna configuration: 2x2 and 2x4, ULA low​
  Propagation condition: TDLA30-10​
  Target BLER: 1%​ (BLER is calculated after all transmission​)
  Target Confidence level: 99%​

## Slide 3: FR1 High reliability (2)
HARQ process number: 2 for FDD and 4 for TDD
MCS:
  Option 1: MCS13
  Option 2: MCS16
  Option 3: MCS19
Methodology for MCS selection
  Higher or equal to -4 dB for final 4 Rx requirement definition (average ideal SNR alignment result + IM)
BLER calculation method
  BLER = NpacketFail/NpacketTx, where NpacketFail is the number of packets with CRC fail after all transmissions (initial and retransmissions), NpacketTx is the total number of packets transmitted during the test.

## Slide 4: FR2 High reliability
      Introduce test cases with PDSCH repetition in FR2 with 1% BLER as test metric
      Test applicability rule for FR2
  The performance requirements are only applicable for UE supporting FR2 operating bands
      Test applicability rule for FR1 and FR2 if UE support both
  UE should be tested for both FR1 and FR2 if UE support FR1 and FR2
Companies are encouraged to provide view on detailed test parameters in the next RAN4 meeting:
  Aggregation factor, MCS, Channel bandwidth, SCS, Channel model, TDD pattern, PDSCH Mapping type etc.

## Slide 5: FR1 PDSCH mapping Type B and processing capability 2 (1)
Background (Agreed parameters from #94e, 94e-bis and 95e)
  SCS/CBW:
    FDD: 15 KHz/10 MHz
    TDD: 30 KHz/ 40 MHz
  TDD pattern (30KHz SCS): DDDSU, S=10:2:2
  Slots to be scheduled:
    FDD: All DL slots with K1=0
    TDD: S slots with K1=0
  PDSCH configuration:
    Starting symbol: 2
    Symbol length for FDD and TDD: 2os only
    Slot aggregation level: 1
    Max number of HARQ transmissions: 1
    Number of HARQ process for FDD: 2
  Channel model: TDLA30-10
  Antenna configuration: 2x2 and 2x4, ULA Low.
  Test metrics: 70% throughput

## Slide 6: FR1 PDSCH mapping Type B and processing capability 2 (2)
      Number of HARQ process for TDD: 2
      MCS: Only MCS 4

## Slide 7: FR2 PDSCH mapping Type B
Test applicability rule for FR2: No need to define the applicability rule.
Test applicability rule for FR1 and FR2: No test applicability rule is needed.
SCS/CBW: 120 kHz/100 MHz
TDD pattern: DDDSU with S = 10D:2G:2U
PDSCH Configuration
  Scheduling: No PDSCH in slot 0 within 20 ms
  MCS: [MCS4] from table 1. Confirming the MCS depends on the simulation results to ensure a proper SNR value.
  Start symbol: 1
  Symbol length: 2
  Max number of HARQ transmissions: 4​
  Number of HARQ process: 8
Antenna configuration: 2x2, ULA low
Channel model:
  Option 1: TDLA30-75
  Other options are not precluded
Test metrics: 70% throughput

## Slide 8: Pre-emption indication (1)
      Background (Agreed parameters from #94e, 94e-bis and 95e)
  No URLLC PI performance requirements
  Time frequency set: 14x1
  Number of symbols to be pre-empted: 2
  Starting symbol to be pre-empted: 3
  Pre-emption scheduling: Fixed scheduling
  Test applicability for eMBB UE PI requirements: optional with UE capability signalling
  Antenna Configuration: 2x2 and 2x4, ULA low

## Slide 9: Pre-emption indication (2)
      Background (Agreed parameters from #94e, 94e-bis and 95e)
  Use the following parameters for eMBB PDSCH configuration
Parameter |  | Value
Duplex mode |  | FDD, TDD
Active DL BWP index |  | 1
PDSCH configuration | Mapping type | Type A
 | k0 | 0
 | Starting symbol (S) | 2
 | Length (L) | 12
 | PDSCH aggregation factor | 1
 | PRB bundling type | Static
 | PRB bundling size | 2
 | Resource allocation type | Type 0
 | RBG size | Config2
 | VRB-to-PRB mapping type | Non-interleaved
 | VRB-to-PRB mapping interl bundle size | N/A
PDSCH DMRS configuration | DMRS Type | Type 1
 | Number of additional DMRS | 1
 | Maximum number of OFDM symbols for DL front loaded DMRS | 1
Number of HARQ Processes |  | FDD: 4, TDD: 8
Maximum HARQ transmission |  | 4
The number of slots between PDSCH and corresponding HARQ-ACK information and TDD pattern |  | FDD: 2 TDD: FR1.30-1
CBW/SCS |  | FDD: 10/15, TDD: 40/30
RB allocation |  | Full bandwidth
MIMO layer |  | Rank 1
Propagation condition |  | TDLA30-10

## Slide 10: Pre-emption indication (3)
      The assumption of UE behaviours for buffer flushing and decoding
  If UE cannot decode the PDCSH correctly, UE feeds back NACK to gNB. Then UE flushes the buffer and waits for the next re-transmission for LLR combing to decode the PDSCH.
      URLLC interference modelling
  SNR: Same as for eMBB transmission
  Structure: Some random data
      Pre-emption probability
  Option 1: 10% within 1 radio frame
  Option 2: 20% within 1 radio frame
      eMBB MCS
  Option 1: MCS13 in Table 1
  Option 2: MCS4 in Table 1
      Test metric
  Option 1: 70% of max T-put
  Other options are not precluded
      Companies are encouraged to prepare comparison analysis of UE with and without HARQ buffer flushing of pre-empted bits to decide on options above

## Slide 11: Test applicability
      Background (Agreement from 95e meeting)
  Test applicability for Rel-15 URLLC UE feature:
    The corresponding test applicability rules for the following features needs to be specified:
      PDSCH repetition (pdsch-RepetitionMultiSlots)
      PDSCH mapping type B (pdsch-MappingTypeB)
      PDSCH processing capability 2 (pdsch-ProcessingType2)
      new 64QAM MCS table for PDSCH (dl-64QAM-MCS-TableAlt)
      CQI table with target BLER of 10^-5 (cqi-TableAlt)
Agreement for 96e meeting
  FFS whether UE URLLC requirements for Rel-15 features are release independent from Rel-15
  No additional features and capability needed for URLLC Demod and CSI requirements introduced for Rel-15 feature under Rel-16 URLLC WI.

## Slide 12: CR work split for UE
Specification | Requirements title | Frequency range | CR work | CR Responsibility
UE demodulation and CSI (38.101-4) | Test applicability for all cases | FR1 | Test applicability | Huawei, HiSilicon
 |  | FR2 | Test applicability | Huawei, HiSilicon
 | FRC for all cases | FR1 | FRC | Intel
 |  | FR2 | FRC | Intel
 | Requirements for PDSCH with ultra-low BLER target (10-5) | FR1 | Requirements | Ericsson
 | Requirements for PDSCH with aggregation factor configured | FR1 | Requirements | Huawei, HiSilicon
 |  | FR2 | Requirements | Apple
 | Requirements for PDSCH for mapping Type B and processing capability 2 | FR1 | Requirements | Qualcomm
 | Requirements for PDSCH for mapping Type B | FR2 | Requirements | Ericsson
 | Requirements for PDSCH for pre-emption indication | FR1 | Requirements | Ericsson
 | CQI reporting test for table 3 | FR1 | Requirements | Apple

## Slide 13: Requirements for Rel-16 URLCC feature
Requirements for Multi-TRP URLLC transmission schemes are covered by Rel-16 e-MIMO WI, no discussion in URLLC thread.
Rel-16 features need to be discussed
  PDCCH enhancement
  Other features not precluded.