## Slide 1: 3GPP TSG-RAN WG4 Meeting #96-e R4-2012649 Electronic Meeting, 17th - 28th Aug, 2020
Huawei, HiSilicon
Way forward on NR URLLC BS performance requirements

## Slide 2: Background
The following WFs were approved:
  R4-1915913: Way forward on NR URLLC demodulation and CSI requirements, RAN4 #93
  R4-2002429: Way forward for NR BS URLLC performance requirements, RAN4 #94-e
  R4-2005528: Way forward for NR BS URLLC performance requirements, RAN4 #94bis-e
  R4-2008810: Way forward for NR BS URLLC performance requirements, RAN4 #95-e

## Slide 3
Agreements:
BS demodulation requirements of high reliability for FR1
  PUSCH aggregation factor for TDD 15 kHz SCS with pattern DDDSU: Configure n2 for FDD and n8 for TDD with note.
    Note: The intention of this configuration is to have two effective transmissions of the transport block. To achieve this for the standard TDD pattern captured in this table, a value of n8 is necessary, while for FDD a value of n2 is necessary.
  RV sequence with 4 HARQ transmission：{0,3,0,3} with note
    Note: The effective RV sequence is {0,2,3,1} with slot aggregation
BS demodulation requirements of high reliability for FR2
  Test applicability rule for FR2 for different SCS: Only 1 SCS need to be tested
  Test applicability rule for FR1 and FR2: If BS declare to support both FR1 and FR2, the tests shall be done both.
  Antenna configuration: 1x2, ULA low
  SCS/BW for FR2: 60 kHz/50MHz, 120 kHz/ 50MHz
  Mapping type: Type B
  MCS: MCS5 from table 3
  Start symbol: 0
  Symbol length: 10
  DM-RS Type: Type 1
  DM-RS duration: Single-symbol DM-RS
  Bandwidth allocation: Full bandwidth
  Maximum number of HARQ re-transmissions: 4
  Test metric: 1% BLER (Calculated after all re-transmissions)
PUSCH BS demodulation requirements of high reliability:

## Slide 4: BS demodulation requirements of high reliability for FR1:
Applicability rule for FDD and TDD
    Option 1: The requirement with PUSCH aggregation level n8 for TDD with 15 KHz SCS can be applied with FDD or TDD 30 KHz SCS with PUSCH aggregation level n2.
    Option 2: The requirements for PUSCH with aggregation for 15kHz can be tested either by configuring n8 and the DDDSU TDD pattern or by configuring FDD with aggregation level n2.
Whether to clarify the safety statement
  Option 1: No need to specify any safety statements in specification
  Option 2: Yes
    Option 1a: Since the URLLC features of 5G NR will potentially be used in safety critical applications, the ultimately chosen statistical testing methodology for testing of these features must be verified by an independent body of experts/statisticians, before requirements and test can be used as basis for safety critical implementations. All statistical analysis and discussions provided in this meeting are to be taken as a best effort and is not to be taken as due diligence
    Option 1b: If the URLLC features of 5G NR would be used in safety or mission critical applications, the ultimately chosen statistical testing methodology for testing of these features must be verified by an independent body of experts/statisticians. It is also important to bear in mind that the demodulation requirements do not take account of all aspects of system operation (for example RF, transmitter, internal interfaces, higher layer protocol software etc.).

## Slide 5: BS demodulation requirements of high reliability for FR2:
TDD pattern
  Option 1: DDDSU, S=10:2:2
  Option 2: DSUU, S=12:2
Aggregation factor for TDD
  Option 1: n8 for DDDSU
  Option 2: n2 for DSUU
  Option 3: n8 for DDDSU with note
    Note: The testing can be performed with a different TDD pattern
Channel model
  Option 1: TDLA30-300 Low
  Option 2: TDLA30-75
DM-RS
  Option 1: 1+0 and 1+1.
  Option 2: 1+1

## Slide 6: Simulation assumptions for PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level for FR1
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Antenna configuration |  | 1x2, ULA Low
PUSCH configuration | Mapping type | Type A and Type B
 | Starting symbol (S) | 0
 | Length (L) | 14
 | PUSCH aggregation factor | n2 for 30 kHz SCS n2 for FDD and n8 for TDD[note 1]
PUSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Propagation condition |  | TDLB100-400
MCS Table |  | Table 3, MCS 5
SCS and BW |  | 15 kHz for 5/10 MHz 30 kHz for 10/40 MHz
Frequency domain resource |  | Full Bandwidth
TDD pattern |  | 15 kHz SCS: 3D1S1U, S=10:2:2 30 kHz SCS: 7D1S2U, S=6:4:4
Maximum number of HARQ transmissions |  | 4
Testing metric |  | Target BLER: 10-2 (Calculate the target BLER after all transmission)
Note 1: The intention of this configuration is to have two effective transmissions of the transport block. To achieve this for the standard TDD pattern captured in this table, a value of n8 is necessary, while for FDD a value of n2 is necessary. |  | 

## Slide 7: PUSCH demodulation requirements for low latency for FR2
BS FR2 URLLC demodulation requirements for PUSCH mapping Type B
Agreements:
  Test applicability rule for FR1 and FR2 if both are supported by BS: Tests shall be done for both, and only 1 SCS will be tested for each frequency band with test applicability rule.
  SCS/CBW for FR2: 60kHz/50 MHz, 120 kHz/ 50 MHz
  TDD pattern: DDDSU, S=10:2:2
  Aggregation factor for TDD: n1
  Channel model：TDLA30-300
  Antenna configuration：1x2, ULA low
  Bandwidth allocation：Full bandwidth
  Maximum number of HARQ re-transmissions: 1
  DM-RS Type: Type 1
  DM-RS duration: Single-symbol DM-RS
  Start symbol: 0
  Test metric: 70% TP
  Section numbers and title for TS38.104: (TS 38.141-1/2 will follow the agreements.)
    8.2.6 Requirements for PUSCH 0.001% BLER
    8.2.7 Requirements for PUSCH repetition Type A
    8.2.8 Requirements for PUSCH mapping Type B with non-slot transmission
  FRC numbers in Annex A for TS38.104: (TS38.141-1 and TS38.141-2 will follow the agreements.)
    A.3A Fixed Reference Channels for performance requirements (QPSK, R=99/1024)
    A.3B Fixed Reference Channels for performance requirements (QPSK, R=308/1024)

## Slide 8: PUSCH demodulation requirements for low latency for FR2
BS FR2 URLLC demodulation requirements for PUSCH mapping Type B
MCS
    Option 1: MCS10 from table 3
    Option 2: MCS 5 or MCS 2 from table 3
DM-RS
    Option 1: 1+0 and 1+1.
    Option 2: 1+0
    Option 3: 1+1 if symbol length larger than 4
Symbol length
    Option 1: 2
    Option 2: 4
    Option 3: 7

## Slide 9: Rel-16 URLLC BS features
Features need to be discussed
  PUSCH repetition type B
  Inter-UE multiplexing
  Other features not precluded.
Whether to define performance requirements for PUSCH repetition type B
  Option 1: Yes
  Option 2: No
Whether to define performance requirements for Inter-UE multiplexing
  Option 1: Yes
  Option 2: No

## Slide 10: PUSCH demodulation requirements CR work split
Specifacation | Requirements title | CR Specifacation | Frequency range | CR work | CR Responsibility
BS demodulation (38.104/38.141-1/38.141-2) | FRC for all test cases | 38.104 | FR1 | FRC | Nokia
 |  |  | FR2 | FFS | Samsung
 |  | 38.141-1 | FR1 | FRC | Ericsson
 |  | 38.141-2 | FR1 | FRC | Huawei
 |  |  | FR2 | FRC | Samsung
 | Test methodology | 38.104? | N/A | Test methodology | Nokia
 |  | 38.141-1 | N/A | Test methodology | Ericsson
 |  | 38.141-2 | N/A | Test methodology | Nokia/Huawei
 | Test applicability for all test cases | 38.141-1 | FR1 | Test applicability | Huawei
 |  | 38.141-2 | FR1 | Test applicability | Ericsson
 |  |  | FR2 | Test applicability | Ericsson
 | Requirements for PUSCH with ultra-low BLER target (10-5) | 38.104 | FR1 | Requirements | Nokia
 |  |  | FR2 | FFS | Samsung
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Ericsson
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | Ericsson
 |  |  | FR2 | N/A | N/A
 | Requirements for PUSCH with aggregation factor configured | 38.104 | FR1 | Requirements | Huawei
 |  |  | FR2 | FFS | Samsung
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Huawei
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | DoCoMo
 |  |  | FR2 | Requirements / Measurement of Performance requirements Annex C.3 | Huawei
 | Requirements for PUSCH for mapping Type B with low number of symbols | 38.104 | FR1 | Requirements | Nokia
 |  |  | FR2 | FFS | Samsung
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Huawei
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | DoCoMo
 |  |  | FR2 | Requirements / Measurement of Performance requirements Annex C.3 | Intel