## Slide 1: Way Forward for general and PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes (eMBB)
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #96-e
Electronic Meeting, 17th – 28th Aug. 2020
Agenda item: 7.9.3.1
R4-2012662
Document for: Approval

## Slide 2: Background
Agreed WF in the previous meetings:
  R4-2002419 WF on demodulation and CSI requirement for NR eMIMO, RAN4#94-e
  R4-2002420 WF on PDSCH demodulation requirements based on multi-TRP transmission for NR eMIMO, RAN4#94-e
  R4-2005529 WF on PDSCH demodulation requirement and General aspects for NR eMIMO, RAN4#94-e-Bis
  R4-2008813 WF for general and PDSCH requirements with single-DCI SDM scheme and Multi-DCI transmission schemes (eMBB), RAN4#95-e

## Slide 3: Performance requirements for multi-panel/TRP in FR1

## Slide 4: General test set-up for PDSCH requirements
Reference for timing offset/frequency offset
  Using TP1 is Reference to define timing and frequency offset
    Timing offset = time offset among TP2 and TP1
    Frequency offset = frequency offset among TP2 and TP1
Baseline receiver assumption for FFT window timing
  It’s up to UE implementation for FFT windowing timing adjustment strategy;
  Define performance requirements in receiver agnostic manner.
  Meanwhile define RAN4 performance requirements based on the assumption of UE sets FFT timing based on TCI state #0 (TP1 i.e. SSB only transmitted from TP1).

## Slide 5: General test set-up for PDSCH requirements
Timing offset among multi-panel/TRP (FR1 only)
  FR1 FDD with 15kHz
    Positive timing offset: 2us
    Negative timing offset: -0.5us
  FR1 TDD with 30kHz
    Positive timing offset: 1us
    Negative timing offset: 0.25us

## Slide 6: General test set-up for PDSCH requirements
TRS/CSI-RS configuration
  Introduce the test cases with only non-colliding TRS/CSI-RS in multi-TRP/panel

## Slide 7: Multi-DCI based PDSCH requirements
Resource allocation
  Introduce only non-overlapping cases
Antenna configuration per each TRP
  Only 2T2R, 2T4R

## Slide 8: PDSCH requirements
Number of test cases for single-DCI/multi-DCI
  Test 1b Single- DCI with positive time offset and overlapping scheduling.
  Test 2a Multi- DCI with frequency offset and negative time offset and non-overlapping scheduling
  FFS on Test 1a Single-DCI with frequency offset and negative time offset and overlapping scheduling.
  Applicability rule:
    Option 1 (If Test 1a will be defined):
      If UE only supports single-DCI based multi-TRP transmission for eMBB, it should be tested with test case 1a and test case 1b
      If UE can support both single-DCI and multi-DCI for eMBB, it should be tested test 2a and test 1b
  Interested companies are encouraged to provide simulation results next meeting for tests 1a, 1b and 2a.

## Slide 9: Performance requirements for multi-panel/TRP in FR2

## Slide 10: Performance requirements for multi-panel/TRP in FR2
No PDSCH demodulation requirements with multi-Panel/TRP transmission schemes under single Tx/Rx beam with same QCI Type-D in FR2 for Rel-16
Considering current OTA Test limitation for demodulation test cases, no test cases for multi-TRP transmission with multi-Tx beams in TDM manner (URLLC TDM scheme) in Rel-16; and further discuss in future release with consideration of test ability issue