## Slide 1: WF for PDSCH requirements with Single-DCI based multi-TRP/Panel transmission schemes (URLLC)
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #96-e
Electronic, 17th – 28th August 2020 Agenda Item: 7.9.3.1
R4-2012663

## Slide 2: Background
      Agreed WFs for demodulation requirements for NR eMIMO WI in previous meetings
        R4-2002419 WF on demodulation and CSI requirement for NR eMIMO, RAN4 #94-e
        R4-2002420 WF on PDSCH demodulation requirements based on multi-TRP transmission for NR eMIMO, RAN4 #94-e
        R4-2005529 WF on PDSCH demodulation requirement and general aspects for NR eMIMO, RAN4 #94e-Bis
        R4-2008813 WF for general and PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes(eMBB), RAN4 #95-e
        R4-2008814 WF for PDSCH requirements with Single-DCI based multi-TRP/Panel transmission schemes (URLLC), RAN4 #95-e
        R4-2008815 Simulation assumption for PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes, RAN4 #95-e
        R4-2008816, WF on PMI Reporting Test Cases with Rel-16 Type II Codebook, RAN4 #95-e

## Slide 3: Candidate schemes
URLLC single-DCI based multi-TRP/panel repetition transmission schemes (see Annex)
  FDM scheme A (2a)
  FDM scheme B (2b)
  TDM scheme A (3)
  Inter-slot TDM scheme (4)

## Slide 4: PDSCH requirements introduction
      Define performance requirements only for FDM scheme A and inter-slot TDM scheme with the following applicability rule:
        FDM scheme is skipped if UE passes the multi-DCI based multi-TRP Tx requirements and TDM scheme is skipped if UE passes URLLC slot aggregation requirements and anyone of the other multi-TRP Tx requirements.

## Slide 5: Number of test cases
      Two test cases per duplex mode:
        Option 1:
          Test 1a: Single-DCI based FDM scheme A with frequency offset and negative time offset
          Test 1b: Single-DCI based inter-slot TDM with positive time offset
        Option 2:
          Test 1a: Single-DCI based FDM scheme A with frequency offset and positive time offset
          Test 1b: Single-DCI based inter-slot TDM A with frequency offset and positive time offset
        Other options are not precluded

## Slide 6: PDSCH configuration
      Option 1: Reuse parameters (TDD configuration, SSB and CSI-RS configuration, PDCCH setup, Propagation conditions and TO/FO) from single-DCI based SDM Tx scheme test case
        MCS:
          Option 1: MCS 13
          Option 2: MCS 19
          Other options are not precluded
        Resource configuration (see table 1)
 | FDMSchemeA | Inter-slot TDM
Mapping type | Type A | 
Resource allocation type | Type 1 | 
DMRS configuration | Type 1, 1+1 | 
Antenna port index | {1000} for TCI#1 and {1001} for TCI#2 | 
Start symbol and time duration | PDSCH#1: 2, 12 PDSCH#2: 2, 12 | 
FDD PRB allocation | PDSCH#1: PRB#0 to PRB#25 PDSCH#2: PRB#26 to PRB#51 | PDSCH#1: PRB#0 to PRB#51 PDSCH#2: PRB#0 to PRB#51
TDD PRB allocation | PDSCH#1: PRB#0 to PRB#52 PDSCH#2: PRB#53 to PRB#105 | PDSCH#1: PRB#0 to PRB#105 PDSCH#2: PRB#0 to PRB#105
Table 1.

## Slide 7: Test metric
      Test metric for requirements definition
        Option 1: 1 % BLER which is more suitable for URLLC service
        Option 2: 70 % @ max throughput as in eMBB related test cases

## Slide 8: Annex
URLLC transmission schemes
  Single-DCI based FDM repetition scheme A
    Single RV in a slot, ~equally divided PRGs across TRPs, common TDRA, single CDM group, single PTRS port
  Single-DCI based FDM repetition scheme B
    RV pair in a slot, ~equally divided PRGs across TRPs, common TDRA, single CDM group, single PTRS port
FDM A
FDM B

## Slide 9: Annex (cont’d)
URLLC transmission schemes
  Single-DCI based TDM repetition scheme A
    RV pair in a slot, same FDRA, same symbol length of each Tx occasion, single CDM group, limited TBS
  Single-DCI based inter-slot TDM repetition scheme
    Single RV in a slot, common SLIV, common FDRA, number of Tx occasions 2-16, single CDM group, limited TBS
TDM A
Inter-slot TDM (2 Tx occasions)