## Slide 1: Way Forward on PMI Reporting Requirement for NR eMIMO
Qualcomm, Ericsson
3GPP TSG-RAN4 Meeting #96-e
Electronic Meeting, Aug 17th – Aug 28th 2020
Agenda item: 7.9.3.3
R4-2012665
Document for: Approval

## Slide 2: Enhanced Type II Test Setup
Test setup:
  Option 1: Only use SU-MIMO test setup, i.e., one tested UE
  Option 2: MU-MIMO based test setup, i.e., one tested UE + one co-scheduled UE (generated by TE)
  Option 3: Using SU-MIMO set-up to Introduce PMI test cases. Meanwhile a MU-MIMO setup based demodulation test with test metric of either follow PMI based or random PMI based throughput can be introduced
The baseline receiver assumption is UE without interference cancellation capability with/without co-scheduled UE.
Under the baseline UE receiver assumption, the PMI calculation processing will not change with and without co-scheduled UE.
The test purpose of such requirements is to verify UE PMI reporting accuracy following NW configuration with RAN1 feature: enhanced type II codebook
  There is no restriction for gNB scheduling with such requirements.
  RAN4 need to ensure UE reporting PMI follow Type II codebook other than Type I codebook under proper test set-up either with MU-MIMO set-up or SU-MIMO set-up.
  We need to ensure the performance requirements with proper test set-up as receiver implementation agonistic manner i.e. no punishment for advanced receiver with inference cancellation capability.

## Slide 3: Test Parameters for SU-MIMO Test Setup - I
Number of CSI-RS ports:
  16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4)
Number of PMI Sub-bands per CQI Sub-band
  R = 1
Codebook parameter configuration
  paramCombination-r16: 6, with L =4, pν =1/2, β=1/2
Sub-band Size:
  4 for FDD with 15kHz SCS, 10MHz CBW
  8 for TDD with 30kHz SCS, 40MHz CBW

## Slide 4: Test Parameters for SU-MIMO Test Setup - II
Channel Model
  TDLA30-5
MIMO Correlation
  XP Medium
MCS and Rank
  MCS 20 (64QAM Table), Rank 2

## Slide 5: Test Parameters for SU-MIMO Test Setup - III
Beam-Steering Model
  How to specify beam steering model into specification.
    Same as specified in B.2.3B.4A of TS 36.101

## Slide 6: Simulation Assumptions for SU-MIMO Test Setup
For initial simulations:
  Use the parameters listed in previous slides.
  The remaining parameters will be same as for Rel-15 Type II codebook simulation assumptions in R4-2012690.
  Interested companies are encouraged to provide the simulation results in the next meeting.

## Slide 7: MU-MIMO Test Setup: Scheduling Model - I
Transmitted signal modelling
  It’s not excluded to further extend the model which can be applied for rank2 transmission, if needed.
  Further discuss for the details on
    NZP-CSIRS configuration for each UE : colliding or not colliding
    IMR configuration
    DMRS configuration for each UE
    Rank assumption for each UE
    baseline UE receiver: MMSE or MMSE-IRC
    Interference estimation assumption

## Slide 8: MU-MIMO Test Setup: Scheduling Model - II
Option 1: W = XH*(X*XH + λI)-1diag(p)-1/2
  λ = 0.001 as baseline assumption
    λ should be kept a small positive scalar to keep zero-forcing properties
Option 2: ,
  where is the orthogonalized and normalised and is the normalized projection of the co-scheduled PMI on the null space of
    Note: Option 2 does not require matrix inversion to generate Xb
One TE vendor questions the feasibility of the proposed test setup

## Slide 9: MU-MIMO Test Setup: Scheduling Model - III
How to generate Xb (channel for co-scheduled UE)
  Option 1: PMI reporting from co-scheduled UE
    The reported PMI is generated from a different channel realization of the same channel model as DUT
    Not feasible from one TE vendor perspective.
  Option 2: Random PMI
    The PMI is selected at random, given the size of type II codebook set, the PMI used may with a very low probability be equal to the PMI reported from the DUT
  Option 3: Fixed PMI
    The PMI is generated once at the start of the simulation and kept in memory to be used in the ZF precoder algorithm when a new PMI from DUT is reported.
  Option 4: True Channel
    The true channel may be obtained by generating a channel which is not restricted by the quantized type II PMI reports, direction may be obtained by a different channel realization of same channel model as DUT
    Not feasible from one TE vendor perspective.

## Slide 10: MU-MIMO Test Setup: Scheduling Model - IV
Beam Steering Model
  Option 1: No beam steering model applied in MU-MIMO test set-up
  Option 2: Yes

## Slide 11: Test Parameters for MU-MIMO Test Setup - I
Number of CSI-RS ports:
  Option 1: 16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4) as baseline
  Option 2 : 32 ports with (N1,N2) = (4,4) and (O1,O2)=(4,4)
Number of PMI Sub-bands per CQI Sub-band
  R = 1
Codebook parameter configuration
  paramCombination-r16: 6, with L =4, pν =1/2, β=1/2

## Slide 12: Test Parameters for MU-MIMO Test Setup - II
Sub-band Size:
  4 for FDD with 15kHz SCS, 10MHz CBW
  8 for TDD with 30kHz SCS, 40MHz CBW
Channel Model
  Option 1: TDLC300-5
  Option 2: TDLA30-5
  Other options are not precluded
MIMO Correlation
  Option 1: XP Medium
  Other options are not precluded
MCS and Rank
  Option 1: MCS 7 (64QAM Table), Rank 1
  Other options are not precluded

## Slide 13: Test Parameters for MU-MIMO Test Setup - III
Test Metric
  Option 1: Relative Throughput ratio between following PMI for Rel-16 enhanced Type II and Rel-15 Type I single-panel codebook.
  Option 2: Relative throughput ratio between following PMI and random PMI.