## Slide 1: WF on UE demodulation and CSI reporting requirements for FR2 DL 256QAM
China Telecom
3GPP TSG-RAN4 Meeting #96e
Electronic Meeting, 17 Aug - 28 Aug, 2020
Agenda item: 7.10.3
R4-2012666
Document for: Approval

## Slide 2: Background: WFs in previous meetings
RAN4 #94e-Bis
  WF: R4-2005531
RAN4 #95e
  WF: R4-2008817

## Slide 3: PDSCH Demodulation: Main Parameters
  Rx impairment modelling and band agnostic requirements
  Not explicitly model Rx impairment
  Rank
  Rank 1 only
  MCS
  Keep the agreement in the last meeting, i.e., use MCS 20
  Propagation condition
  Use fading channel
  In the next meeting, companies are encouraged to provide ideal and impairment results for both option 1A and option 1B, and down select one of the two options based on simulation results.
    Option 1A: TDLA30-300
    Option 1B: TDLD30-75
      Note: extra effort on TDLD channel model simplification is needed.

## Slide 4: Maximum testable SNR for PDSCH demodulation requirements (for information)
  22.0dB for FR2 bands including n260 with 50MHz CBW.
  Anritsu: Note that according to R4-2006352 the maximum ΔMBP,n is 0.75 dB , using the demodulation spreadsheet in TR 38.810 we estimate that under this scenario SNRs up to 22.0dB at baseband could be tested under 50MHz scenario.

## Slide 5: Agreed simulation parameters in previous meetings #1
Parameter | Value
Tx EVM | 3%
Rx impairment modelling and band agnostic requirements | The following scenarios can be considered for band agnostic requirements definition: Static channel mode: MCS 20-23, rank 1 TDL-D channel mode: MCS 20-21, rank 1 TDL-A channel mode: MCS 20-21, rank 1
SCS | 120 kHz
Channel bandwidth and PRB allocation | 50MHz CBW with full PRB allocation
TDD Configuration | DDDSU, S=10D:2G:2U
SSB configuration | Periodicity 20 ms, Allocated in first slot within 20ms
PDCCH duration | Symbol #0 in each slot
PDSCH configuration | Full DL slots: Start symbol 1, Duration 13 Special slots: Start symbol 1, Duration 9
PDSCH mapping type | Type A

## Slide 6: Agreed simulation parameters in previous meetings #2
Parameter | Value
PRB bundling size and Precoding model | PRB bundling size: 2 Precoding model: Random Precoding, per slot , WB granularity
DM-RS configuration | Type 1 single symbol front loaded, 1 additional DMRS
PT-RS configuration | per 2PRB in frequency domain per symbol in time domain
TRS configuration | 20 ms periodicity, 2 slots, Offset 10 ms
Overhead for TBS determination | 6
HARQ RV sequence | {0, 2, 3, 1}
HARQ process number | 8
Receiver assumption | MMSE-IRC
MIMO configuration | 2Tx 2Rx ULA low
Test metric | 70% of max TP

## Slide 7: SDR Requirements
Whether to define SDR requirements for FR2 256QAM
  Option 1: Add 256QAM (modulation format of 8) to FR2 SDR requirements
  Option 2: Not to define FR2 SDR requirements for 256QAM
  If it is agreed to define SDR requirements, consider the following test parameters:
  MCS and rank
    Option 1:Add MCS indexes 26, 21, 20 and 11 in MCS table 2 for both 1 and 2 MIMO layers in the Table 7.5A.1-3. Run simulations to derive the required SNR at 85% throughput for MCS 20 to MCS 26 in MCS table 2, with both 1 layer and 2 layers.
    Other options are not precluded.

## Slide 8: CQI reporting Requirements
Whether to define FR2 CQI reporting requirements for CQI table 2
  In the next meeting, decide whether to introduce the requirements for AWGN and/or fading conditions based on the simulation results under 50MHz CBW:
    For AWGN condition, companies are encouraged to simulate the required SNR for achieving median CQI of [11, 12 and 13] in CQI table 2.
    For fading condition, companies are encouraged to simulate the required SNR where CQI indices corresponding to 256QAM (i.e., 12 and higher) in CQI table 2 can be reported with at least [10%] probability.
  If it is agreed to define FR2 CQI reporting test for CQI table 2, use channel bandwidth of 50MHz.
  If it is agreed to define FR2 CQI reporting for CQI table 2, consider the following test applicability:
  If UE passes the test with CQI Table 2, then it can skip the corresponding test with CQI Table 1
  Note: Similar to the existing CQI table 1 test, the test for CQI Table 2 will cover both lower SNR and higher SNR.

## Slide 9: CQI reporting Requirements cont’d
If it is agreed to define FR2 CQI reporting for CQI table 2, consider the following test parameters:
  SNR testing point for the higher SNR:
    For AWGN condition:
      Option 1: 19/20 dB
      Other options are not precluded.
    For fading condition:
      Option 1: 17/18 dB
      Other options are not precluded.
    Decide in the next meeting based on more simulation results.
  Other parameters
    Reuse the other parameters in Rel-15 FR2 CQI tests