## Slide 1
3GPP TSG-RAN WG4 Meeting #96-e R4-2012668
Electronic Meeting, 17-28 Aug., 2020
Agenda Item: 7.15.3.1
WF on UE demodulation for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1910050 WF on demodulation for UE NR HST, RAN4#92
  R4-1912808 Way forward on NR HST UE demodulation, RAN4#92BIS
  R4-1915926 WF on UE demodulation for NR HST, RAN4#93
  R4-2002418 WF on UE demodulation for NR HST, RAN4#94-e
  R4-2005532 WF on UE demodulation for NR HST, RAN4#94bis-e
  R4-2008820 WF on UE demodulation for NR HST, RAN4#95-e

## Slide 3: Test case for DPS
Whether to introduce test cases for DPS transmission scheme 1b
  Introduce DPS transmission scheme 1b test cases with test applicable rules which can be further discussed among below options
    Option 1:
      If UE declared supporting > 1 TCI states, UE will pass scheme 1b and skipped HST single tap test cases and scheme 1a test cases
      If UE only support 1TCI state, UE need to pass both scheme 1a and HST single tap test cases and skip scheme 1b test cases
    Option 2:
      If UE pass HST-SFN test cases, then UE can skip HST-DPS scheme 1a/1b

## Slide 4: Test setup for DPS 1a
Two RRH s of RRH#(2k) and RRH#(2k+1) are assumed, and SSB#0 is transmitted from both TRPs, where k is the RRH number with k=0,1, 2, …
  UE is configured with TCI#(k mod 2) and TCI#(k+1 mod 2) that are associated with TRS#(k mod 2) and TRS#(k+1 mod 2) transmitted from RRH#(2k) and RRH#(2k+1) respectively by RRC signalling tci-StatesToAddModList in the PDSCH-Config and tci-PresentInDCI is not configured;
  All the configured TCI states are known to UE. UE is configured with NZP-CSI-RS resource for L1-RSRP measurements by RRC signaling nzp-CSI-RS-ResourceSet within the CSI-ResourceConfig and periodic CSI reporting by setting reportConfigType to periodic and reportQuantity to cri-RSRP (Note: reported L1-RSRP mesurements are not tested)
TE actives TCI #0 for PDCCH by “TCI State Indication for UE-specific PDCCH MAC CE”;
PDSCH associated with TCI #0 is transmitted during the slots from 0 to (n-1) + HARQ needed time + 3ms + first TRS + TRS processing time;
In slot n TE start triggering TCI state switching command to TCI #1 by “TCI State Indication for UE-specific PDCCH MAC CE”;
PDSCH associated with TCI #1 is transmitted in slots from n + HARQ needed time + 3ms + first TRS + TRS processing time to N.
PDSCH associated with TCI #(k mod 2) (k=0,1,2,…) is transmitted in slot from max((2k-1)n, 0) to ((2k+1)n-1) + HARQ needed time + 3ms + first TRS + TRS processing, where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH. And k is the RRH number in the channel model.

## Slide 5: Test parameters for DPS
Transmission scheme 1a
  Rank 2
  PDSCH is scheduled in DL, FFS for special slots
  TRS processing time: 2ms
  MCS
    Option 1: MCS 13 based on 64QAM table (same as HST-SFN)
    Option 2: MCS 17 based on 64QAM tables
  HARQ timing
    FDD 15kHz SCS: 2 slots
    TDD 30kHz SCS with TDD pattern 7D1S2U: {8,7,6,5,5,4,3,2} slots

## Slide 6: Open issues for DPS
  Number of active TCI states in DPS transmission scheme 1b
    Option 1: with 2 active TCI states.
    Option 2: with 2 and more than 2 active TCI states.
  FFS Test setup of DPS 1b
  Statistics during the switching time for both DPS 1a and 1b
    Option 1: The switch command is transmitted via MAC CE, the corresponding PDSCH carrying that MAC CE should be ensured to be decoded successfully and lower MCS should be used, such as MCS 4.
    Option 2: PDCCH/PDSCH are DTXed from the time gNB indicates MAC CE TCI state switch to the time UE receive the first TRS from the new TRP.
    Option 3: Use same SNR point for all DPS Tx schemes requirements definition:
      Skip PDSCH allocation on slots with TRS transmission
      Skip PDSCH allocation on slots from n to m, where n slots are equivalent to time that needed to pass middle point between two RRH and m is a slot which corresponds to HARQ needed time on MAC CE command in DPS scheme 1a.
    Other options are not precluded.

## Slide 7: Test setup of DPS 1b
Test setup for transmission scheme 1b
  Use following as baseline for DPS transmission scheme 1b test setup (agreement in last meeting)
    for scenario with 2 active TCI states
      (total 2 active TCI states): PDCCH TCI state switching delay caused by MAC CE, but less than DPS 1a with pre-tracking of second TCI state and only HARQ needed time + 3ms delay is needed, UE tracks 2 active TCI states in advance so that UE can quickly get better Doppler shift estimation for the second TRP compared to DPS 1a.
      UE is configured with two different TCI states (TCI #0 and TCI #1) associated with two different RRHs by RRC signalling tci-StatesToAddModList in the PDSCH-Config and tci-PresentInDCI is not configured;
      TE activates TCI #0 and TCI #1 for PDSCH at the same time by “TCI States Activation/Deactivation for UE-specific PDSCH MAC CE” and activates TCI #0 for PDCCH by “TCI State Indication for UE-specific PDCCH MAC CE” command with the field of CORESET ID set to 0;
      TE transmits PDCCH and PDSCH associated with TCI #0 from TRP#1 from slot 0 to n-1;
      In slot n TE start triggering TCI state switching command to TCI #1 by “TCI State Indication for UE-specific PDCCH MAC CE”;
      TE transmits PDCCH and PDSCH associated with TCI #1 from TRP#2 from slot n [+ HARQ needed time + 3ms] to N.
      where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH

## Slide 8: Test setup of DPS 1b cont.,
Test setup for transmission scheme 1b
  Use following as baseline for DPS transmission scheme 1b test setup (agreement in last meeting)
    for scenario with 3 active TCI states
      (Total 3 active TCI states): No PDCCH TCI state switching delay by using MAC CE, but 3 active TCI states to track, UE needs to report supporting of maxNumberActiveTCI-PerBWP = n4
      UE is configured with three different TCI states (TCI #0, TCI #1 and TCI #2) associated with two different RRHs by RRC signalling tci-StatesToAddModList in the PDSCH-Config;
      TE activates TCI #0 and TCI #1 for PDSCH at the same time by “TCI States Activation/Deactivation for UE-specific PDSCH MAC CE” and activates TCI #2 for PDCCH by “TCI State Indication for UE-specific PDCCH MAC CE” command with the field of CORESET ID set to 0;
      TE transmits PDCCH associated with TCI#2 from TRP#1 and TRP#2 from slot 0 to N
      DCI contains pointer to TCI#0 from slot 0 to n-1 and pointer to TCI#1 from slot n to N
      TE transmits PDSCH associated with TCI #0 from TRP#0 from slot 0 to n-1
      TE transmits PDSCH associated with TCI #1 from TRP#1 from slot [n or n+1] to N
      where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH

## Slide 9: Applicability rule
Test applicability between HST-SFN and HST single tap
  Do not test UE under HST single-tap, if UE passes the requirements for HST-SFN.
    Option 1: Skip the Rel-15 HST single tap test, if UE passes the requirements for HST-SFN
    Option 2: Skip both Rel-15 and Rel-16 HST single tap test, if UE passes the requirements for HST-SFN
Test applicability between HST-SFN and HST multi-path fading
  Option 1: Do not test UE under HST multi-path scenarios, if UE passes the requirements for HST-SFN.
  Option 2: Do not define any applicability rules between HST-SFN and HST multi-path fading performance test cases

## Slide 10: Applicability rule
Test applicability between different Doppler frequencies for the same channel model
  For FDD
    Define applicability rule for TDLB100-400
      Rel-15 multi-path fading with TDLB100-400 (Table 5.2.2.1.1-3 Test 1-1 and Table 5.2.3.1.1-3 Test 1-1) is not applicable for UE that passes Rel-16 multi-path fading tests TDLC300-600 for FDD
    FFS whether to define applicability rule for TDLC300-100
      Option 1: no applicability rule
      Option 2: Rel-15 multi-path fading with TDLC300-100 (Table 5.2.2.1.1-3 Test 1-2 and Table 5.2.3.1.1-3 Test 1-2) is not applicable for UE that passes Rel-16 multi-path fading tests TDLC300-600 for FDD

## Slide 11: Applicability rule
Test applicability between different Doppler frequencies for the same channel model
  For TDD
    Not define any applicability rule for TDLB100-400 multi-path fading tests between Rel-15 and
    FFS whether to define applicability rule for TDLC300-100
      Option 1: no applicability rule
      Option 2: Rel-15 multi-path fading with TDLC300-100 (Table 5.2.2.2.1-3 Test 1-2 and Table 5.2.3.2.1-3 Test 1-2) is not applicable for UE that passes Rel-16 multi-path fading tests TDLC300-1200 for TDD

## Slide 12: Release independent
Rel-16 HST-SFN requirements are released independent from Rel-15
HST-DPS test is release independent from Rel-15

## Slide 13: Simulation assumption for DPS transmission scheme
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2x2; 2x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, FFS whether PDSCH is scheduled in special slots | 
MCS | Option 1: MCS 13 based on 64QAM table Option 2: MCS 17 based on 64QAM table | 
Propagation condition | HST-DPS (Assume two TRPs for HST-DPS transmission scenario) | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 870Hz | 1667Hz
HARQ needed time/slots | 2 | 8,7,6,5,5,4,3,2
TRS processing time | 2ms | 
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15 |  | 

## Slide 14: Simulation assumption for HST-SFN
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2x2; 2x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 13 based on 64QAM table | 
Propagation condition | HST-SFN | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 870Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 15: Simulation assumption for HST-single tap
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 1x2; 1x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
MCS | MCS 17 based on 64QAM table | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
Propagation condition | HST-single tap | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds= 300m, Dmin=2m | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 972Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 16: Simulation assumption for multi-path fading channel
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2x2; 2x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 13 based on 64QAM table | 
Propagation condition | TDL-C 300ns | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 600Hz | 1200Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15