## Slide 1: WF on Rel-16 NR HST BS demodulation requirements
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, 17 – 28 Aug., 2020
Agenda: 7.15.3.2
R4-2012676
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
Agreed WFs for General/PUSCH/PRACH in previous meetings
  R4-1910128 Way forward on NR HST BS demodulation requirements, RAN4#92.
Agreed WFs for PUSCH in previous meetings
  R4-1912809 Way forward on NR HST PUSCH demodulation requirements, RAN4#92Bis.
  R4-1915886 Way forward on NR HST PUSCH demodulation requirements, RAN4#93.
  R4-2002405 WF on Rel-16 NR HST BS demodulation requirements, RAN4#94e. (The content in WF R4-2002405 except slide 16 is agreed; see meeting minutes.)
  R4-2005534 WF on Rel-16 NR HST PUSCH BS demodulation requirements, RAN4#94-e-bis.
Agreed WFs for PRACH in previous meetings
  R4-1912729 WF on NR HST BS PRACH demodulation requirements, RAN4#92b.
  R4-1915871 Way forward on NR HST PRACH demodulation requirement, RAN4#93.
  R4-2002405 WF on Rel-16 NR HST BS demodulation requirements, RAN4#94e. (The content in WF R4-2002405 except slide 16 is agreed; see meeting minutes.)
  R4-2005535 WF on Rel-16 NR HST PRACH BS demodulation requirements, RAN4#94-e-bis.
Agreed WFs for UL TA in previous meetings
  R4-2002405 WF on Rel-16 NR HST BS demodulation requirements, RAN4#94e. (The content in WF R4-2002405 except slide 16 is agreed; see meeting minutes.)
  R4-2005536 WF on Rel-16 NR HST ULTA BS demodulation requirements, RAN4#94-e-bis.
Agreed WFs for PUSCH/PRACH/UL TA in previous meetings
  R4-2008821 WF on Rel-16 NR HST BS demodulation requirements, RAN4#95-e.
Corresponding Email summary in RAN4#96-e
  R4-2012739 Email discussion summary for [96e][323] NR_HST_Demod_BS, RAN4#96-e.

## Slide 3: PUSCH

## Slide 4: PUSCH - 1T1R requirements
1T1R requirements for the tunnel scenario - MCS configuration
  Only have MCS 2 requirements

## Slide 5: PUSCH - Multi-path fading channel models with high Doppler values
Multi-path fading scenarios under consideration
  The following models are under consideration:
    TDLC300-600 FO=0Hz TDLC300-1200 FO=0Hz
Multi-path fading scenario typicality
  Do not further pursue consensus.
Specification of multi-path fading channel under high Doppler
  Introduce PUSCH requirements for HST multi-path fading channel under high Doppler, with configuration
    TDLC300-600 FO=0Hz (15kHz), TDLC300-1200 FO=0Hz (30kHz)
    MCS: 2
    Waveform: CP-OFDM
    DM-RS: 1+1+1
    Antenna: 1T2R
    Bandwidth: 5MHz for 15kHz SCS, 10MHz for 30kHz SCS

## Slide 6: PUSCH - Multi-path fading channel models with high Doppler values
Specification drafting of multi-path fading requirements
  Option 2: Introduce multi-path fading channel requirements with high Doppler value into the section “8.2.1 Performance requirement for PUSCH with transform precoding disabled”
  Option 3: Introduce multi-path fading channel requirements with high Doppler value in a separate table under section “8.2.4 Requirements for PUSCH for high speed train”

## Slide 7: PUSCH - DFT-s-OFDM Requirements
Include requirements for DFT-s-OFDM waveform
  Do not introduce PUSCH HST requirements for DFT-s-OFDM.

## Slide 8
Simulation assumptions for PUSCH (Informative)
Parameter | Value |  |  |  | 
 | v = 350km/h |  | v = 500km/h |  | 
Transform precoding | Disabled |  | Disabled |  | 
Number of Tx | 1 |  | 1 |  | 
Number of Rx | Tunnel: 2, 1 Open space: 2, 8 |  | Tunnel: 2, 1 Open space: 2, 8 |  | 
Number of layers | 1 |  | 1 |  | 
SCS | 15kHz, 30kHz |  | 15kHz, 30kHz |  | 
Reference signal | DMRS type 1 with 1+1+1 |  | DMRS type 1 with 1+1+1 |  | 
l0 | l0 = 2 or 3 |  | l0 = 2 or 3 |  | 
symbols length | 14 |  | 14 |  | 
start symbol index | 0 |  | 0 |  | 
Time domain resource allocation type | type A |  | type A |  | 
Frequency domain resource | Full applicable test bandwidth |  | Full applicable test bandwidth |  | 
MCS index | Tunnel: MCS 2 and MCS 16 Tunnel 1T1R: MCS 2 Open space: MCS 2 and MCS 16 |  | Tunnel: MCS 2 and MCS 16 Tunnel 1T1R: MCS 2 Open space: MCS 2 and MCS 16 |  | 
Maximum Doppler shift | 15kHz SCS: 1340Hz | 30kHz SCS: 2334Hz | 15kHz SCS: 1740Hz |  | 30kHz SCS: 3334Hz
Carrier frequency (GHz) | 15kHz SCS: 2.1GHz 30kHz SCS: 3.6GHz |  | 15kHz SCS: 1.8GHz (Band n3) 30kHz SCS: 3.6GHz |  | 
Propagation condition | HST single-tap channel model: Tunnel: Ds=300m, Dmin=2m Open space: Ds=700m, Dmin=150m Multi-path fading channel under high Doppler value 15kHz: TDLC300-600 FO=0Hz; 30kHz: TDLC300-1200 FO=0Hz |  |  |  | 
SCS and BW | 15kHz: 10MHz/5MHz; 30kHz: 40MHz/10MHz for HST single tap channel model 15kHz: 5MHz; 30kHz: 10MHz for multi-path fading channel under high Doppler value |  |  |  | 
Number of HARQ transmissions | 4 |  |  | 4 | 
Testing metric | SNR @70% of maximum throughput |  |  | SNR @70% of maximum throughput | 

## Slide 9: PRACH

## Slide 10: PRACH - TDLC300-100 propagation conditions for long preamble formats
TDLC300-100 propagation conditions for long preamble formats
  Introduce TDLC300-100 FO= 0Hz for PRACH with restricted set type A and B.
  In Rel-16, no additional test cases for PRACH besides what we already agreed test case.
  The test cases applied for BS if BS declared supporting corresponding restricted set A/B.

## Slide 11: PRACH - Manufacturer declaration
PRACH high speed support declaration for HST
  HST PRACH support should be covered by the same declaration entry for HST PUSCH and UL TA, and one declaration entry for short and long preamble format is enough:
D.10X | High speed train | Declaration of high speed train scenario support.
D.10Y | PRACH format for high speed train | Declaration of supported PRACH format(s) for high speed train scenario, i.e. format 0 restricted set type A, format 0 restricted set type B, format A2, format B4, format C2. This declaration is applicable to HST PRACH only if BS declares to support high speed train in D.108.

## Slide 12: PRACH - Test applicability for short PRACH formats
Test applicability for short PRACH formats
  Do not specify an additional test applicability rule for HST short PRACH, i.e., all short PRACH format declared to be supported need to be tested.

## Slide 13: UL TA

## Slide 14: UL TA - Additional scenario “X”
Addition of scenario “X”
  RAN4 agree to introduce scenario X requirements under rel-16 HST WI, adding it in non-HST sections/tables to avoid misleading.
    A BS, which declares to support HST and passes scenario Y or scenario Z, can assume implicit test passing of scenario X.
    Scenario X parameters:
  .
Parameter | Scenario X
Channel model | Stationary UE: AWGN Moving UE: TDLC300-400
UE speed | 120 km/h
CP length | Normal
A | 15 kHz: 10 us 30 kHz: 5 us
Δω | 15 kHz: 0.04 s-1 30 kHz: 0.08 s-1

## Slide 15: UL TA - Additional scenario “X”
SCS/CBW combinations
  Option 1: Have requirements for
    15kHz: 10MHz/5MHz; 30kHz: 40MHz/10MHz.
  Option 2: Have requirements for
    15kHz: 5MHz; 30kHz: 10MHz.
  Option 3: Have requirements for all Rel-15 non-HST PUSCH bandwidths.
  Other options not precluded.
Applicability rules concerning SCS/CBW
  Option 1: Re-use non-HST PUSCH applicability rules.
  Option 2: Re-use HST PUSCH applicability rules.
  Other options not precluded.

## Slide 16: UL TA - Manufacturer declaration w.r.t. scenario X
Scenario X manufacturer declaration
  No manufacturer declaration for scenario X.
Scenario X implicit test passing
  Merged into <Addition of scenario “X”> agreemement

## Slide 17: UL TA - Specification writing
Organization of requirements for 500kph in specifications
  Capture the 500kph UL TA scenario in the same table as the 350kph UL TA scenario. Title includes “for high speed train”.

## Slide 18: UL TA - Minimum CBW FDRA and SRS configuration
Minimum CBW FDRA and SRS configuration
  Use the following configurations:
    FDRA
      5MHz CBW/15KHz SCS: 12 contiguously allocated RBs for each UE
      Start RB index
        Moving UE: 0
        Stationary UE: 12
      10MHz CBW/30KHz SCS: 12 contiguously allocated RBs for each UE
      Start RB index
        Moving UE: 0
        Stationary UE: 12
    SRS
      5MHz CBW/15KHz SCS: 20 contiguously allocated RBs starting from PRB index 0
      10MHz CBW/30KHz SCS: 20 contiguously allocated RBs starting from PRB index 0
      C_SRS = 5, B_SRS =0, for 20RB with 15 KHz SCS and 30 KHz SCS

## Slide 19: UL TA - Minimum CBW FDRA and SRS configuration
Minimum CBW simulation template
  Add the cases for 5MHz CBW/15kHz SCS and 10MHz CBW/30KHz SCS for UL TA to the simulation result summary template
Minimum CBW FRC
.
Reference channel |  | 
Subcarrier spacing [kHz] | 15 | 30
Allocated resource blocks | 12 | 12
Data bearing CP-OFDM Symbols per slot (Note 1) | 11 | 11
Modulation | 16QAM | 16QAM
Code rate (Note 2) | 658/1024 | 658/1024
Payload size (bits) | 4032 | 4032
Transport block CRC (bits) | 24 | 24
Code block CRC size (bits) | - | -
Number of code blocks - C | 1 | 1
Code block size including CRC (bits) (Note 2) | 4056 | 4056
Total number of bits per slot | 6336 | 6336
Total data bearing resource elements per slot | 1584 | 1584
NOTE 1: DM-RS configuration type = 1 with DM-RS duration = single-symbol DM-RS and the number of DM-RS CDM groups without data is 2, Additional DM-RS position = pos2, and l0 = 2 or 3 for PUSCH mapping type A, as per table 6.4.1.1.3-3 of TS 38.211 [5]. NOTE 2: Code block size including CRC (bits) equals to K' in subclause 5.2.2 of TS 38.212 [15]. |  |