## Slide 1: Way forward on PDSCH CA normal demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #96-e
E-meeting, 17 – 28 August 2020
Agenda Item: 7.16.1.1
R4-2012688

## Slide 2: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      Pcell configuration for the test
  The test coverage can be considered fulfilled if UE passes any one of scenario with one of the CC as PCell for FDD 15 kHz + TDD 15 kHz
  If Pcell in both carriers are supported for FDD 15 kHz + TDD 30 kHz, configure TDD cell as Pcell
  If Pcell in both carriers are supported for TDD 15 kHz + TDD 30 kHz, configure
    Option 1: 15 kHz SCS cell as Pcell
    Option 2: 30 kHz SCS cell as Pcell

## Slide 3: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      HARQ process number
      K1 values
 |  | CCs with the same duplex mode & SCS with Pcell | CCs with different duplex mode / SCS with Pcell
FDD 15 kHz + TDD 30 kHz CA | FDD PCell | 4 | 8
 | TDD PCell | 8 | 8
FDD 15 kHz + TDD 15 kHz CA | FDD PCell | 4 | 4
 | TDD PCell | 8 | 8
TDD 15 kHz + TDD 30 kHz CA | 15kHz PCell | 8 | 12
 | 30kHz PCell | 8 | 8
 |  | CCs with the same duplex mode & SCS with Pcell | CCs with different duplex mode / SCS with Pcell
FDD 15 kHz + TDD 30 kHz CA | FDD PCell | {2} | {2}
 | TDD PCell | {8,7,6,5,5,4,3,2} | {7,5,4,11,9}
FDD 15 kHz + TDD 15 kHz CA | FDD PCell | {2} | {2}
 | TDD PCell | {4,3,2,6} | {4,3,2,6,5}
TDD 15 kHz + TDD 30 kHz CA | 15kHz PCell | {4,3,2,6} | {4,4,3,3,2,2,6,6}
 | 30kHz PCell | {8,7,6,5,5,4,3,2} | {7,5,4,11}

## Slide 4: Test applicability rule
      Categorizing of CA capabilities
  Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.
      Test of different CA capabilities
  Option 1: Test intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with the largest number of bands.
  Option 2: Test all the supported CA capabilities, including intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.
  Option 3:
    Intra-band CA: test intra-band contiguous CA, and intra-band non-contiguous CA
    Inter-band CA: test inter-band CA with the largest number of bands and inter-band CA with the largest aggregated CBW
      The details are to be discussed
      If the selection of “inter-band CA with the largest number of bands” and “inter-band CA with the largest aggregated CBW” results in the same CA configuration(s), only one inter-band CA configuration will be tested; otherwise, two inter-band CA configurations will be tested.
  Other options are not precluded

## Slide 5: Test applicability rule
      Selection of CA configuration(s) and CBW combination
  Agreement from RAN4 #95e
    Further discuss by taking into account:
      The supportedSubCarrierSpacingDL, maxNumberMIMO-LayersPDSCH and supportedModulationOrderDL are reported for each CC and scalingFactor are reported per band for FR1 and FR2.
      The testable SNR for FR2.
  Options for further discussion
    Option 1: Proposal 7 in R4-2009579
    Option 2: Proposal 6 in R4-2011010
    Option 3: Proposals 5 and 6 in R4-2009730
    Other options are not precluded
  Way forward
    Companies are encouraged to provide the comments on the following questions:
      Whether to consider maxNumberMIMO-LayersPDSCH, supportedModulationOrderDL and scalingFactor, since only 16QAM and rank 2 are used?
      If yes for the above bullet, align the understanding of these capability based on 38.306, such as, applied per CC, per band or in the final data rate calculation?
      Which option is better to accommodate the FR2 testability?