## Slide 1: WF on NR MIMO OTA
vivo, CAICT, Spirent
3GPP TSG-RAN WG4 Meeting #96-e R4-2012707
Electronic Meeting, 17-28 Aug., 2020
Agenda item: 12.1.1
Document for: Approval

## Slide 2: NR MIMO OTA
WI management
  Detailed Work Plan in [R4-2012710] for NR MIMO OTA WI is agreed. Future update based on the actual progress of RAN4 is not precluded.
  Keep the agreed WID as it is, the MU aspects will be handled in RAN WG5, and the performance requirement with head/hand phantoms is 2nd priority.
Down-selecting of parameters for NR MIMO OTA requirements
  For FR1 MIMO OTA performance requirements:
    Adopt 40MHz bandwidth and associated other parameters in Table 8.2-2 and Table 8.2-5 in TR 38.827 v16.0.0 as the only FR1 TDD RMC for FR1 MIMO OTA requirements.
    Adopt FR1 UMi CDL-A for 4Rx bands, and FR1 UMa CDL-C for 2Rx bands.
  For FR2 MIMO OTA performance requirements:
    Further discuss the down-selection of FR2 RMC, feasibility of 64 QAM for FR2 will be checked, and final conclusion will be made next meeting.
      Technical input from companies is encouraged to analyze SNR range and feasibility of 64QAM
    Further discuss the down-selection of FR2 channel model for defining FR2 MIMO OTA requirement
      keep both InO CDL-A and UMi CDL-C at this stage, the goal is to select one for final requirement

## Slide 3: NR MIMO OTA
Figure of Merit for NR MIMO OTA requirements
  For FR1 MIMO OTA performance requirements:
    Only one outage point of TP@ 70% is selected for the final performance metric
      This agreement is based on LTE TRMS analysis
    Further check whether how many PMODE can reach TP @ 90% or 95% could be an additional FoM
      Option 1：TP@90% can pass 11 of total 12 rotations
      Option 2：TP@95% can pass 10 of total 12 rotations
      Other options are not precluded
  For FR2 MIMO OTA performance requirements:
    Select averaging all the values better than [50%] percentile of CCDF as the Figure of Merit for FR2 MIMO OTA requirement
    Further check whether [50%] percentile value of the CCDF curve should also be a FoM of FR2
    Analysis on number of test points vs uncertainty of FR2 MIMO OTA performance is encouraged

## Slide 4: NR MIMO OTA
NR MIMO OTA requirements framework
  Clear requirements framework should be defined prior to measurement campaign
    Agreement was reached that a Lab alignment activity is required before labs/vendors can submit data for the performance requirements definition (similar to LTE MIMO OTA)
      Detailed work plan for alignment activity will be discussed
  For FR2, simulation approach to define performance requirement is not precluded
    Workplan including detailed simulation assumptions for FR2 simulation campaign need to be defined

## Slide 5: MIMO OTA test methodology
Channel model validation
  Channel model validation procedure
    Time domain approach for FR1 spatial correlation validation is agreed as the alternative method
      Detailed procedure can be added in the TR38.827 next meeting
    Spatial correlation validation based on either frequency-domain or time-domain is sufficient
      pass/fail limit of spatial correlation should consider both approaches
    Further check whether vertical polarization is sufficient for FR1 Spatial Correlation validation
      Simulation or measurement results are encouraged
    5cm PSP validation for performance requirements work as baseline for FR2
      Companies are encouraged to provide procedures, concrete test points, and impact on test time for a 10cm PSP validation approach
      Companies to analyze if test system with 5cm radius PSP validation can be used to measure DUT with larger antenna size such as 10cm radius
  Pass/fail criteria of channel model validation
    Simulation analysis and measurement results from CE vendors and Labs are encouraged to specify the pass/fail limit as soon as possible.

## Slide 6: MIMO OTA test methodology
UE orientations clarification in 3D-MPAC system
  UE orientation will keep as 3D scan with agreed 36 points in TR38.827
  Probes Configuration
    Rotate the probes towards the z axis direction, which probe is along z axis will be decided next meeting
    CE vendors encouraged to discuss probe configurations, blocking, re-positioning, impact on channel model realization w.r.t. 38.901 and 38.827 and harmonize on a joint probe configuration proposal prior to the next RAN4 meeting
    Detailed position of probes will be decided next meeting
  FR2 QoQZ validation procedure optimization
    Based on TR 38.810 [or TS 38.521-2]
    Updates to the procedure to be finalized next meeting (pending the final probe locations)

## Slide 7: Next step
Key work for next meeting
  FR1 channel model validation analysis
  Discuss detailed FR1 Lab alignment activity work plan
  UE orientations clarification