## Slide 1: WF on the polarization mismatch objective
Samsung
R4-2012714
3GPP TSG-RAN WG4 Meeting #96-e
Online Meeting, Aug 2020
Agenda: 13.1.2

## Slide 2: Background
EIRP measurement enhancement
  Methods identified in RAN4#93 meeting [1]
    Method 0: No change to the measurement procedures in TR38.810
    Method 1: “H&V simultaneous operation with 2-port CSI-RS beam management by TE” [8]
    Method 2: “Keep H&V non-simultaneous operation by TE, but change test procedure to Link_V → Link_H → UE_Beam_Lock → Measurement_V → Measurement_H” [8]
    Method 3: “H&V non-simultaneous operation by TE with additional 45 deg link” [8]
    Method 4: Different approach for calculating total EIRP [10]
    Method 5: Polarization sweep of the DL signal [R4-1911503]
    Method 6: The use of CP for the DL signal and UL signal measurement [R4-1911503]
    Method 7: Test mode for certification purpose to force the UE to transmit on both polarizations
    Method 8: The use of Elliptical Polarization for the DL [11]
    Other methods are not precluded
  Method identified in the informal email discussion and offline conference call meeting [2]
    Method based on TPMI
  New method proposed in RAN4#96e meeting [3]
    Method by using power up command to trigger TX diversity
Enhancement on demodulation of UL by test equipment (e.g. EVM measurement)
  Whether FR2 test equipment topology shall be enhanced by adopting dual polarization coherent receivers [1][2][3]

## Slide 3: WF on EIRP measurement
Focus on following techniques to enhance EIRP measurement, and it is agreed to propose to add them into SID scope explicitly in Sep. RAN plenary :
  Option 1: TPMI side condition method
    TPMI side conditions are applicable to Rel-16 (and higher) UEs
  Option 2: DL polarization scan method
    Further clarify whether it can reliably force UE to transmit simultaneously with dual polarization for all UEs
    How to address the concern on test time and the concern on difference between test and field
  Option 3: test mode to trigger TX diversity
    Test mode can reliably force UE to transmit simultaneously with dual polarization for all UEs
    How to address the concern on difference between test and field
FFS on feasibility of power up command to trigger TX diversity
FFS on feasibility of 2-port CSI-RS method as an extra enhancement

## Slide 4: WF on UL demodulation
Whether FR2 test equipment topology shall be enhanced by adopting dual polarization coherent receivers
  The dual polarization coherent receiver topology is taken as a starting point
  Companies are encouraged to contribute in future meetings with test setup descriptions, impact on test time, preliminary MU, and the method’s feasibility

## Slide 5
[1] | R4-1916177 | WF on FR2 test methodology enhancement | Apple, CAICT
[2] | R4-2009959 | FR2 test method enhancement informal email discussion summary | Apple
[3] | R4-2012561 | Email discussion summary for [96e][330] FR2_enhTestMethods | Moderator(Apple)
References