## Slide 1: WF on IAB-MT Tx requirements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting # 96-e Electronic Meeting, 17-28 Aug. 2020
R4-2012745

## Slide 2: Background
The following contributions were provided and discussed in RAN4#96e
  R4-2011031, IAB-MT Transmit signal quality, Ericsson
  R4-2010951, Futher discussion on IAB-MT transmitted signal quality, ZTE
  R4-2010296, IAB-MT transmit modulation quality, Nokia, Nokia Shanghai Bell
  R4-2009789, TP for TR 38.809: IAB-MT Transmit signal quality, CATT
  R4-2010912, IAB MT Tx Requirements, Qualcomm
  R4-2011297, IAB-MT Tx emissions, Huawei
  R4-2011033, IAB-MT unwanted emission for FR2 and FR1, Ericsson
  R4-2010952, Further discussion on IAB-MT unwanted emission, ZTE
  R4-2010298, TP to TR 38.809: IAB-MT unwanted emission requirements, Nokia, Nokia Shanghai Bell
  R4-2009793, Discussion on IAB-MT unwanted emissions, CATT

## Slide 3: WF on transmit signal quality
Do not specify spectrum flatness, in-band emission, LO leakage and IQ-imbalance requirements for IAB-MT
EVM measurement procedure will be included in the core specification, but only during performance part of the WI
No further discussion in Rel-16 WI of IAB-MT as synchronization source impact on network performance and possible further work

## Slide 4: WF on unwanted emissions requirements
Scaling factor for LA IAB-MT type 1-O: NTXU,counted = min(NTXU,active , 8×Ncells) (agreement in R4-2012616)
FR1 LA IAB-MT re-uses BS relative ACLR, absolute ACLR, OBUE, OOB boundary and general spurious emissions
FR2 LA IAB-MT re-uses BS absolute ACLR, OBUE, OOB boundary and general spurious emissions. Relative ACLR was already agreed previously (24 dB)
WA IAB-MT shall re-use WA gNB absolute ACLR, both category A and B
gNB requirements are adopted for co-existence and co-location requirements, further clarifications are needed for co-location, to be included in the TP
Transmission in DL timeslot requires meeting gNB requirements, Will be captured in TP for TR and TS
Additional emission requirements will be specified based on gNB requirements, further revise the requirements if needed pending on RAN2 responses