## Slide 1: Way Forward on PMI Reporting Requirement for NR eMIMO
Qualcomm, Ericsson
3GPP TSG-RAN4 Meeting #96-e
Electronic Meeting, Aug 17th – Aug 28th 2020
Agenda item: 7.9.3.3
R4-2012761
Document for: Approval

## Slide 2: Enhanced Type II Test Setup
Test setup:
  Option 1: Only use SU-MIMO test setup, i.e., one tested UE
  Option 2: MU-MIMO based test setup, i.e., one tested UE + one co-scheduled UE (generated by TE)
  Option 3: Using SU-MIMO set-up to Introduce PMI test cases. Meanwhile a MU-MIMO setup based demodulation test with test metric of either follow PMI based or random PMI based throughput can be introduced
The baseline receiver assumption is UE without interference cancellation capability with/without co-scheduled UE.
Under the baseline UE receiver assumption, the PMI calculation processing will not change with and without co-scheduled UE.
The test purpose of such requirements is to verify UE PMI reporting accuracy following NW configuration with RAN1 feature: enhanced type II codebook
  There is no restriction for gNB scheduling with such requirements.
  RAN4 need to ensure UE reporting PMI follow Type II codebook other than Type I codebook under proper test set-up either with MU-MIMO set-up or SU-MIMO set-up.
  We need to ensure the performance requirements with proper test set-up as receiver implementation agonistic manner i.e. no punishment for advanced receiver with inference cancellation capability.
Make final agreements among SU-MIMO vs. MU-MIMO set-up in RAN4#97e
  Companies are encouraged to bring simulation results for both Type II and Type I codebook under the same simulation assumption for comparison purpose.

## Slide 3: Test Parameters for SU-MIMO Test Setup - I
Number of CSI-RS ports:
  16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4)
Number of PMI Sub-bands per CQI Sub-band
  R = 1
Codebook parameter configuration
  paramCombination-r16: 6, with L =4, pν =1/2, β=1/2
Sub-band Size:
  4 for FDD with 15kHz SCS, 10MHz CBW
  8 for TDD with 30kHz SCS, 40MHz CBW

## Slide 4: Test Parameters for SU-MIMO Test Setup - II
Channel Model
  TDLA30-5
MIMO Correlation
  XP Medium
MCS and Rank
  MCS 20 (64QAM Table), Rank 2

## Slide 5: Test Parameters for SU-MIMO Test Setup - III
Beam-Steering Model
  How to specify beam steering model into specification.
    Same as specified in B.2.3B.4A of TS 36.101

## Slide 6: Simulation Assumptions for SU-MIMO Test Setup
For initial simulations:
  Use the parameters listed in previous slides.
  The remaining parameters will be same as for Rel-15 Type II codebook simulation assumptions in R4-2012690.
  Interested companies are encouraged to provide the simulation results in the next meeting.

## Slide 7: MU-MIMO Test Setup: Scheduling Model - I
Transmitted signal modelling
  It’s not excluded to further extend the model which can be applied for rank2 transmission, if needed.
  Details
    NZP-CSIRS configuration for each UE : Not colliding
    IMR configuration: No IMR configuration
    DMRS/Rank configuration for each UE:
      DUT = 3 with DMRS seed=0, co-scheduled UE=5 with random DMRS seed (Rank 1, DMRS antenna port mapping 1000 for DUT, 1002 for co-scheduled UE)
Notes: QC: Then Under MU-MIMO, we have different interference levels in data and CSI-RS; will this impact overall performance.
Nokia/E//: We didn’t assume that UE need to apply special interference handing, UE assumption and behavior among SU-MIMO and MU-MIMO as it’s transparent to UE.
Huawei: IMR used to measure interference and apply whiting . NO need to IMR needed assuming no specific interference.
QC/Apple: This is not match with real deployment and will degrade the performance.
Nokia: With proper Zero forcing in MU-MIMO, such interference ignorable in receiver side.
QC: We will see low SNR.

## Slide 8: MU-MIMO Test Setup: Scheduling Model - II
,
  where is the orthogonalized and normalised and is the normalized projection of the co-scheduled PMI on the null space of
    Note: Option 2 does not require matrix inversion to generate Xb
One TE vendor questions the feasibility of the proposed test setup

## Slide 9: MU-MIMO Test Setup: Scheduling Model - III
How to generate Xb (channel for co-scheduled UE)
  Option 1: Random PMI
    The PMI is selected at random, given the size of type II codebook set, the PMI used may with a very low probability be equal to the PMI reported from the DUT
  Option 2: Fixed PMI
    The PMI is generated once at the start of the simulation and kept in memory to be used in the ZF precoder algorithm when a new PMI from DUT is reported.

## Slide 10: MU-MIMO Test Setup: Scheduling Model - IV
Beam Steering Model
  Option 1: No beam steering model applied in MU-MIMO test set-up
  Option 2: Yes

## Slide 11: Test Parameters for MU-MIMO Test Setup - I
Number of CSI-RS ports:
  Option 1: 16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4) as baseline
  Option 2 : 32 ports with (N1,N2) = (4,4) and (O1,O2)=(4,4)
Number of PMI Sub-bands per CQI Sub-band
  R = 1
Codebook parameter configuration
  paramCombination-r16: 6, with L =4, pν =1/2, β=1/2

## Slide 12: Test Parameters for MU-MIMO Test Setup - II
Sub-band Size:
  4 for FDD with 15kHz SCS, 10MHz CBW
  8 for TDD with 30kHz SCS, 40MHz CBW
Channel Model
  Option 1: TDLC300-5
  Option 2: TDLA30-5
  Other options are not precluded
MIMO Correlation
  Option 1: XP Medium
  Other options are not precluded
MCS and Rank
  Option 1: MCS 7 (64QAM Table), Rank 1
  Other options are not precluded

## Slide 13: Test Parameters for MU-MIMO Test Setup - III
Test Metric
  Option 1: Relative Throughput ratio between following PMI for Rel-16 enhanced Type II and Rel-15 Type I single-panel codebook.
  Option 2: Relative throughput ratio between following PMI and random PMI.