## Slide 1: Way forward on PMI reporting requirements for Tx ports larger than 8 and up to 32
Ericsson, Samsung
3GPP TSG-RAN4 Meeting #96e
Electronic Meeting August 17 – August 28, 2020
Agenda item: 7.16.1.2
R4-2012762
Document for: Approval

## Slide 2: Timeline of previous agreements
#92
  WF: R4-1910017
#92bis
  WF: R4-1912834
  simulation assumptions: R4-1912811
#93
  WF: R4-1915858
  Simulation assumptions: R4-1915859
#94e
  WF: R4-2002393
  Simulation assumptions: R4-2002394
#94e-Bis
  WF: R4-2005549
  Simulation assumptions: R4-2005550
#95e
  WF: R4-2008846
  Simulation assumptions: R4-2008847

## Slide 3: Simulation assumptions
Detailed simulation assumptions:
  R4-2012690

## Slide 4: PMI tests SP Type I page 1
Further check gain requirements and alignment results
 | CTC, HW, Ericsson | Samsung, Intel | Intel, CTC | QC | Apple
16T2R | 2.5 | 2.0 | 2.5 | 2.0 | 2.6
16T4R | 3.5 | 2.0 | 2.5 | 3.0 | 2.6
32T2R | 5.0 | 4.5 | 5.0 | 4.5 | 
32T4R | 8.0 | 4.5 | 5.0 | 8.0 | 

## Slide 5: Type II test setup
Test setup:
  Option 1: Only use SU-MIMO test setup, i.e., one tested UE
  Option 2: MU-MIMO based test setup, i.e., one tested UE + one co-scheduled UE (generated by TE)
  Option 3: Using SU-MIMO set-up to Introduce PMI test cases. Meanwhile a MU-MIMO setup based demodulation test with test metric of either follow PMI based or random PMI based throughput can be introduced
The baseline receiver assumption is UE without interference cancellation capability with/without co-scheduled UE.
Under the baseline UE receiver assumption, the PMI calculation processing will not change with and without co-scheduled UE.
The test purpose of such requirements is to verify UE PMI reporting accuracy following NW configuration with RAN1 feature: enhanced type II codebook
  There is no restriction for gNB scheduling with such requirements.
  RAN4 need to ensure UE reporting PMI follow Type II codebook other than Type I codebook under proper test set-up either with MU-MIMO set-up or SU-MIMO set-up.
  We need to ensure the performance requirements with proper test set-up as receiver implementation agonistic manner i.e. no punishment for advanced receiver with inference cancellation capability.

## Slide 6: Parameters for SU-MIMO Type II page 1
Codebook construction
  16Tx ports (N1,N2) = (4,2), (O1, O2) = (4,4)
L (numberOfBeams)
  2
Npsk (phaseAlphabetSize)
  8
SubbandAmplitude
  Option 1: False
  Option 2: True
PMI-FormatIndicator
  Option 1: Wideband
  Option 2: Subband
Propagation condition
  TDLA30-5
MIMO correlation
  Option 1: XP High
  Option 2: XP Medium

## Slide 7: Parameters for SU-MIMO Type II page 2
MCS and rank
  MCS 20, rank 2
Beam steering model
  For Rel-15 Type II codebook test:
    Configure only two beams in beam steering model for Rel-15 Type II codebook test.
  specifying beam steering model into specification:
    Reuse the agreement from Rel-16 eMIMO demod.
Test metric
  TP ratio between following PMI and rand PMI
Subband size
  Option 1: 4 for FDD and 8 for TDD
  Option 2: 8 for FDD and 16 for TDD

## Slide 8: Parameters for SU-MIMO Type II page 3
Implementation of Random Type II PMI
  Proposal 1: A common way of doing random PMI for Type II codebook simulation might need to be agreed in order to reach sufficient randomization and meanwhile avoid uncertainty and unexpected results brought by infinite random parameters.
    Beam randomization:
      Option 1: Randomly select a beam combination from a set which include all possible beam combinations
      Option 2: Limit the set of possible beams to the possible beams under the configuration of following PMI
    Amplitude and phase coefficient randomization:
      Option 1: For each weighting coefficient, independently and randomly chose an amplitude quantization gear and a phase quantization gear. To at least ensure one of the weighting coefficients is quantized as the highest grade, phase quantization is 0 gear and its position at 2L is randomly generated.
    Note: The set is limited due to the limitation of quantization gears.

## Slide 9: Parameters for MU-MIMO Type II page 1
Test metric
  Option 1: TP ratio between following PMI and random PMI
  Option 2: TP ratio between following Type II codebook and following SP Type I codebook
  Other options are not precluded
codebook construction
  Option 1: 32Tx ports (N1, N2) = (4,4), (O1, O2) = (4,4)
  Option 2: 16Tx ports (N1, N2) = (4,2), (O1, O2) = (4,4)
Npsk (phaseAlphabetSize)
  8

## Slide 10: Parameters for MU-MIMO Type II page 2
subbandAmplitude
  True
MIMO correlation
  XP Medium
Propagation condition
  Option 1: TDLC300-5
  Option 2: TDLA30-5
  Other options not precluded

## Slide 11: Parameters for MU-MIMO Type II page 3
Scheduling mode:
  Option 1: Zero-forcing (following slide)
  Other options not precluded
DCI value for antenna mapping (Table 7.3.1.2.2-2 from 38.212):
  DUT = 3 with DMRS seed=0, co-scheduled UE=5 with random DMRS seed (Rank 1, DMRS antenna port mapping 1000 for DUT, 1002 for co-scheduled UE)

## Slide 12: Parameters for MU-MIMO Type II page 4
Beam Steering Model
  Option 1: No beam steering model applied in MU-MIMO test set-up
  Option 2: Yes

## Slide 13: Parameters for MU-MIMO Type II page 5
,
  where is the orthogonalized and normalised and is the normalized projection of the co-scheduled PMI on the null space of
  Note: does not require matrix inversion to generate Xb
One TE vendor questions the feasibility of the proposed test setup

## Slide 14: Parameters for MU-MIMO Type II page 6
How to generate Xb (channel for co-scheduled UE)
  Option 1: Random PMI
    The PMI is selected at random, given the size of type II codebook set, the PMI used may with a very low probability be equal to the PMI reported from the DUT
  Option 2: Fixed PMI
    The PMI is generated once at the start of the simulation and kept in memory to be used in the ZF precoder algorithm when a new PMI from DUT is reported.

## Slide 15: Agreements
Make final agreements among SU-MIMO vs. MU-MIMO set-up in RAN4#97e
  Companies are encouraged to bring simulation results for both Type II and Type I codebook under the same simulation assumption for comparison purpose.