## Slide 1: WF for addition of new frequency separation classes
Qualcomm
R4-2016824
3GPP TSG-RAN WG4 #97-e
Nov, 2020
Electronic meeting

## Slide 2: Background
R4-2014290 proposed to add 200, 400 and 600 MHz as Frequency separation class for combination of inter- and intra-band CA for FR2 to limit the UE maximum supported BW
In the discussion companies questioned the proposal with comments on
  Necessity of 200 MHz
  Motivation is UE implementation driven only and spectrum allocations are not shown
  Applicability of the new Fs class should be for intra-band configurations involving inter-band CA

## Slide 3: WF
Addition of newly Fs values 200, 400, 600 MHz into Table 5.3A.4-2 of TS 38.101-2 is FFS
Applicability of new values will be discussed in next meeting further, considering the following two options :
  Option 1: Applicable only for configurations that are combinations of intra- and inter-band CA
  Option 2: Applicable to all CA configurations involving intra-band non-contiguous CA