## Slide 1: WF on MR-DC RRM requirements for Idle mode CA measurements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #97e
E-meeting, November 2nd – 13th, 2020
R4-2017118
Document for: Approval

## Slide 2: Background
During the RAN4#97e E-meeting the dicussion related to Multi-RAT Dual-Connectivity and Carrier Aggregation enhancements [LTE_NR_DC_CA_enh] continued.
This WF addresses Idle mode CA measurement RRM requirements.
Summary of the 1st round discussion during RAN4#97e meeting is captured in R4-2017009.
  Summary document additionally includes background for topics #1 and #2, based on the input from the companies.

## Slide 3: Topic #1: UE idle mode CA measurement requirements and s-NonIntraSearch
Sub-topic #1-1: UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are not configured:
  Issue 1-1-1: UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are not configured
    Agreement: UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are not configured, follow requirements in section 4.2.2.4 table 4.2.2.4-1

## Slide 4: Topic #1: UE idle mode CA measurement requirements and s-NonIntraSearch
Sub-topic #1-2: UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are configured
  Issue 1-2-1: Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ (high priority carrier not configured):
Agreement:
UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are configured, and when Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ follow requirements in section 4.2.2.4 table 4.2.2.4-1.
Same principles will apply for inter-RAT measurements
E-UTRAN measurements when UE is in NR IDLE or INACTIVE mode
NR measurements when UE is in LTE IDLE mode

## Slide 5: Topic #1: UE idle mode CA measurement requirements and s-NonIntraSearch
Sub-topic #1-2: UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are configured
  Issue 1-2-2: Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ (high priority carrier configured):
Agreement:
UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are configured, and when Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ follow requirements in section 4.2.2.4 table 4.2.2.4-1.
Same principles will apply for inter-RAT measurements
E-UTRAN measurements when UE is in NR IDLE or INACTIVE mode
NR measurements when UE is in LTE IDLE mode

## Slide 6: Topic #1: UE idle mode CA measurement requirements and s-NonIntraSearch
WF on Issue 1-2-3:
  Issue 1-2-3: Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ (high priority carrier configured):
    Candidate agreement (from GTW):
      UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are configured, when Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ, and the UE is configured with one or more higher priority carrier, at least follow requirements in section 4.2.2.7.
      Send LS to RAN2 to inform on the agreement and RAN4 observations that the measurement duration can exceed the maximum configurable duration of T331 timer but there is no consensus in RAN4 whether the timer value needs to be increased. It is up to RAN2 whether and how to resolve the issue.
Moderator Propose following (conclude based on 2nd round discussion):
  UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are configured, and (Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ), and the UE is configured with one or more higher priority carrier, at least follow requirements in section 4.2.2.7.
  Send LS to RAN2 to inform on the agreement and RAN4 the observation that the UE measurement duration can exceed the current maximum configurable duration of T331 timer.

## Slide 7: Topic #1: UE idle mode CA measurement requirements and s-NonIntraSearch
WF on Issue 1-2-4:
  Issue 1-2-4: Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ (high priority carrier not configured)
  Proposals
    Option 1: UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are configured, when Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ, and the UE is configured with one or more higher priority carrier, at least follow requirements in section 4.2.2.7.
    Option 2: UE measurement requirements for idle mode CA measurements, when SnonIntraSearchP/Q are configured, when Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ, and the UE is configured with one or more higher priority carrier, at least follow requirements in section 4.2.2.4 table 4.2.2.4-1.
Moderator Propose following:
  More discussion needed

## Slide 8: Topic #1: Summary of UE idle mode CA measurement requirements and s-NonIntraSearch
Agreements on UE measurement requirements for idle mode CA measurements:
  If SnonIntraSearchP/Q are not configured:
    Follow requirements in section 4.2.2.4 table 4.2.2.4-1.
  If SnonIntraSearchP/Q are configured:
    Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ (high priority carrier not configured):
      Follow requirements in section 4.2.2.4 table 4.2.2.4-1.
    Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ (high priority carrier configured)
      Follow requirements in section 4.2.2.4 table 4.2.2.4-1
Way Forward:
  If SnonIntraSearchP/Q are configured:
    Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ (high priority carrier configured):
      at least follow requirements in section 4.2.2.7
    Send LS to RAN2 to inform on the agreement and RAN4 the observation that the UE measurement duration can exceed the current maximum configurable duration of T331 timer
SnonIntraSearchP/Q configured |  |  |  | SnonIntraSearchP/Q not configured
Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ |  | Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ |  | N/A
High Priority carrier not configured | High Priority carrier configured | High Priority carrier not configured | High Priority carrier configured | N/A
4.2.2.4 | 4.2.2.4 | 4.2.2.x | 4.2.2.7 | 4.2.2.4

## Slide 9: Topic #2: Overlapping and non-overlapping carriers
Sub-topic 2-2: UE measurement requirements and scaling according to measured carriers
  Based on the comments from companies, moderator propose to agree on the following (conclude based on 2nd round discussion):
    RAN4 agree to scale the UE Idle mode CA measurement requirements based on the actual measured target carrier, regardless if the carrier is configured for Idle mode CA measurements only, mobility only or both idle mode CA and mobility measurements.
    A carrier shall only be counted once in the scaling if the carrier is configured for both idle mode CA measurement requirements and mobility measurements.

## Slide 10: Topic #2: Overlapping and non-overlapping carriers
Sub-topic 2-1: need for RAN4 define different UE idle mode CA measurement requirements depending on whether the EMR carrier is measured for mobility or not.
  Based on the comments received moderator propose following modified proposal for agreement (conclude based on 2nd round discussion):
    UE idle mode CA measurement requirements do not depend on whether the carrier configured for idle mode CA measurements is configured for mobility or not.
Next page captures the proposed agreements for sub-topics 2-1 and 2-2 in table format.

## Slide 11: Topic #2: Overlapping and non-overlapping carriers
SnonIntraSearchP/Q configured |  |  |  | SnonIntraSearchP/Q not configured
Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ |  | Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ |  | N/A
EMR measurement requirements when high Priority carrier not configured | EMR measurement requirements when high Priority carrier configured | EMR measurement requirements when high Priority carrier not configured | EMR measurement requirements when high Priority carrier configured | N/A
4.2.2.4 (Kcarrier * Tdetect,NR_Inter, Kcarrier * Tmeasure,NR_Inter)Note 1 | 4.2.2.4 (Kcarrier * Tdetect,NR_Inter, Kcarrier * Tmeasure,NR_Inter) Note 1 | 4.2.2.x | 4.2.2.7 (Thigher_priority_search = (60 * Klayers), Klayers * Tmeasure,NR_Inter) Note 1 | 4.2.2.4 (Kcarrier * Tdetect,NR_Inter, Kcarrier * Tmeasure,NR_Inter) Note 1
Note 1: UE idle mode CA measurement requirements apply for the carrier configured for idle mode CA measurement when the carrier configured for mobility and when the carrier is not configured for mobility. Note 2: Kcarrier is the total number of NR inter-frequency carriers indicated by the serving cell for mobility and idle mode CA measurements. If a carrier is configured for both idle mode CA measurements and mobility, the carrier is only counted once. Note 3: Nlayers is the total number of higher priority NR and E-UTRA carrier frequencies broadcasted in system information and carriers configured for idle mode CA measurement. |  |  |  | 
Overview of proposed agreements for sub-topics 2-1 and 2-2:

## Slide 12: Topic #2: Overlapping and non-overlapping carriers
Sub-topic 2-4: Is there a need for the definition of overlapping and non-overlapping carriers
  Moderator proposal is to discuss this Issue accounting the company view of Issue 2-11-3. Based on company view related to Issue 2-11-3, is there a need to discuss Issue 2-11-4 further?
    (conclude based on 2nd round discussion)

## Slide 13: Topic #2: Overlapping and non-overlapping carriers
Sub-topic 2-3: Can the EMR carrier dynamically change between overlapping and non-overlapping based on the UE conditions and the s-NonIntraSearch thresholds
  Moderator proposal is to discuss this Issue accounting the company views and input related to Issue 2-11-1- and 2-11-2. Hence, considering company proposals for Issues 2-11-1 and 2-11-2 - are there any technical reasons for RAN4 to define overlapping and non-overlapping carriers?
    (conclude based on 2nd round discussion)

## Slide 14: Topic #2: Overlapping and non-overlapping carriers
Sub-topic 2-12: Measurement requirement for UE who supports the beam level EMR reporting
  Issue 2-12-1: Value of X?
    (conclude based on 2nd round discussion)
  Issue 2-12-2: Can the same value of X apply for NR inter-RAT beam measurements
    (conclude based on 2nd round discussion)

## Slide 15: Topic #2: Overlapping and non-overlapping carriers
Sub-topic 2-13: Timer T331 length
  Issue 2-13-1: Whether to include in LS any RAN4 recommendations, e.g. increase the value range for timer T331?
    (conclude based on 2nd round discussion)
  Issue 2-13-2: Candidate values for timer T331 (if to be recommended to be increased in Issue 2-13-1)
    (conclude based on 2nd round discussion)

## Slide 16: Topic #2: Overlapping and non-overlapping carriers
Sub-topic 2-14: UE Idle mode CA measurement requirements and UE conditions
  Issue 2-14-1: Company view regarding whether having idle mode CA measurement requirements based on UE conditions (Srxlev and s-NonIntraSearch) could lead to uncertainty on network side concerning the reported results
    (conclude based on 2nd round discussion)

## Slide 17: Topic #2: Overlapping and non-overlapping carriers
Sub-topic 2-15: Cell detected status
  Issue 2-15-1: RAN4 to discuss and agree if the cell detected status condition needs to be updated or clarified to reflect the cell detected state condition of the cell at the time of and during the actual connection release
    (conclude based on 2nd round discussion)