## Slide 1: WF on test case for DL interruption due to Tx switching between two uplink carriers
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, 2-13 Nov., 2020
      R4-2017173
Document for: Approval

## Slide 2: Principle and general parameters for test case
How to verify the symbol-level DL interruption in test
    Triggering an aperiodic CSI-RS L1-RSRP reporting with CSI-RS resources (with boosted power) on the OFDM symbol right before the interruption and check UE’s aperiodic L1-RSRP report with corresponding measurement accuracy.

## Slide 3: Principle and general parameters for test case
No MRTD is set in the test
SRS configuration in the special slot
  SRS configuration refers to SRSConf.1 in Table A.4.4.1.1.1-3 in TS 38.133 except that:
  • resourceMappingstartPosition: 0
  • resourceMappingnrofSymbols: n2

## Slide 4: Specific parameters for DL Interruptions at UE switching between LTE 1Tx carrier and NR 2Tx carrier in inter-band ENDC
TDD configuration
    Carrier#2 TDD UL/DL pattern is 3D1S4U, S = 10DL: 2GP: 2UL
Which symbol to be verified?
    symbol#5 or symbol #8 on the special slot on NR TDD carrier depending on UE capability uplinkTxSwitchingPeriod (140us or 35us respectively)
    symbol level DL interruption can’t be verified in LTE

## Slide 5: Specific parameters for DL interruptions at switching between two uplink carriers in FDD-TDD CA (SA)
TDD configuration
    Carrier#2 TDD UL/DL pattern is 3D1S4U, S = 10DL: 2GP: 2UL
Which symbol to be verified?
    Symbol #8 or symbol #9 or symbol #10 in the slot overlapping with the special slot of the NR TDD carrier depending on UE capability uplinkTxSwitchingPeriod on NR FDD carrier (Cell 1)
    Symbol #4 or symbol #5 or symbol #8 on the special slot depending on UE capability uplinkTxSwitchingPeriod on NR TDD carrier (Cell 2)

## Slide 6: Specific parameters for DL interruptions at switching between two uplink carriers in TDD-TDD CA (SA)
TDD configuration
    Carrier#1 TDD UL/DL pattern is 3D1S4U, S = 10DL: 2GP: 2UL;
    Carrier#2 TDD UL/DL pattern is 1D1S2U, S = 10DL: 2GP: 2UL
Which symbol to be verified?
    symbol #4 or symbol #5 or symbol #8 on the special slot depending on UE capability uplinkTxSwitchingPeriod on NR TDD PCell (Cell 1)
    symbol #4 or symbol #5 or symbol #8 on the 2nd special slot of every 8 slots depending on UE capability uplinkTxSwitchingPeriod NR TDD SCell (Cell 2)
The test is applied assuming UE support simultaneous Rx-Tx.