## Slide 1: WF on remaining issues on CSI-RS based L3 measurement requirements (core part)
Apple
3GPP TSG-RAN WG4 Meeting #97e R4-2017223 Electronic Meeting, 2 – 13 Nov., 2020

## Slide 2: Core requirements based on CSI-RS resources and SSB overlapping in time domain
CSSF framework generally applies to both scenario 1 and 2
  Scenario 1 (CSI-RS resources and SSB are fully or partially overlapped in time domain)
  Scenario 2 (CSI-RS resources and SSB are non-overlapped in time domain)
  In both scenario 1 and 2
    CSI-RS and SSB measurements outside of the gap are subject to searcher limitation as defined in CSSF framework
    CSI-RS and SSB measurement inside the gap should follow the existing assumption that single frequency layer can be measured per MG
    CSI-RS and SSB for L3 measurement, including gap based and non-gap based, equally share the measurement opportunities.

## Slide 3: UL scheduling restriction for CSI-RS intra-frequency measurements
TDD
  Introduce a scheduling restriction for TDD band when UE performs CSI-RS intra-frequency measurements in a TDD band
    Option 1: When UE performs CSI-RS intra-frequency measurements in a TDD band, UE is not expected to transmit on data OFDM symbols overlapped by CSI-RS resource symbols to be measured, and 1 OFDM symbols before and after each consecutive CSI-RS symbols, where the serving cell is taken as the symbol level timing reference.
    Option 2: When UE performs CSI-RS intra-frequency measurements in a TDD band, UE is not expected to transmit on data OFDM symbols fully or partially overlapped by CSI-RS resource symbols to be measured, where the serving cell is taken as the symbol level timing reference.
    FFS whether the scheduling restrictions apply for all scenarios when UE performs CSI-RS measurements
FDD:
  No UL scheduling restriction for FR1 FDD.

## Slide 4: DL Scheduling restriction for mixed numerologies in FR1
It has been agreed in RAN4#89e to restrict the use case to the same numerology for intra-frequency CSI-RS and data of serving cell.
No DL scheduling restriction due to CSI-RS based intra-frequency L3 measurement is allowed for FR1
  Add this assumption to the applicability section in intra-frequency CSI-RS based L3 measurement specification.

## Slide 5: Time domain restriction for CSI-RS resource configuration
The CSI-RS measurement requirements apply provided that CSI-RS resources per frequency layers are always configured within 5 ms window
TBD: can it be assumed that all CSI-RS resources in the same MO have the same periodicity and offset?
  Option 1: all CSI-RS resources in the same MO have the same periodicity and offset
  Option 2: CSI-RS resources in the same MO can have different periodicities and/or offset

## Slide 6: On collision between SSB/CSI-RS based L1 and CSI-RS based L3 measurements
Do not define CSI-RS measurement requirements in Rel-16 for the collision between CSI-RS based L3 measurement of neighbor cell and serving cell measurement for SSB/CSI-RS based RLM/BFD or other SSB/CSI-RS based L1 measurements