## Slide 1: WF on 2-step RACH RRM test cases
ZTE Corporation
3GPP TSG-RAN WG4 #97-e
Electronic Meeting, 2-13 Nov., 2020
R4-2017254

## Slide 2: Principles to follow when defining test cases
There is no CSI-RS based non-contention based 2-step RA type random access.
In the tables for configurations, the PRACH configuration shall be changed to MsgA configurations.
RSRP-ThresholdSSB shall be replace with msgA-RSRP-ThresholdSSB.
If there is no RSRP-ThresholdSSB in the original configuration table, msgA-RSRP-ThresholdSSB shall be configured so that the TC can configure the UE correctly.
In the tests, PRACH transmissions shall be replaced with MsgA transmissions.
In some test cases, use MsgA PRACH and MsgA PUSCH transmission for clarity.

## Slide 3: PRACH transmission power
Specify 2-step RACH tests with first transmitted MsgA PRACH power with the same values as specified to the first transmitted preamble in 4-step RACH RRM performance tests.

## Slide 4: PUSCH transmission power
Define 2-step RACH RRM performance requirements with MsgA PUSCH power calculated with a shift of 3.μ + 2 dB in comparison to the MsgA PRACH power. Definition of μ should be clarified, e.g., μ = 0 for SCS = 15kHz.

## Slide 5: Test parameters
Define 2-step RACH RRM performance requirements with the parameters defined in the table below:
Parameter | Value
MsgA number of PRBs | 2
msgA-DeltaPreamble | 3 dB
msgA-Alpha | alpha1
deltaMCS | Disabled