## Slide 1: WF on NR UE Power Saving Enhancements (All agreements in RAN4#97e in email thread #233)
MediaTek inc.
3GPP TSG-RAN WG4 Meeting #97e R4-2017269
Electronic Meeting, 2-13 Nov., 2020
Agenda Items: 12.9

## Slide 2
Agreements

## Slide 3
Issue 2-1-1: Evaluation assumption for SLS on mobility impact
Evaluation assumptions are in section 2 of R4-2017306
  Note: Further updates in future meetings are not precluded.
Issue 2-1-2: Evaluation assumption for power consumption
Power consumption model in 38.840 is used as the starting point of evaluation assumption. Other options are not precluded, e.g.,
  LS R1-2007419
  VoIP traffic model as in TR 38.840
  Evaluation assumptions in section 3 of R4-2017306
    Note: Further updates in future meetings are not precluded.

## Slide 4: Issue 2-1-3: From configuration perspective, factors to be studied and evaluated for RLM/BFD relaxation
At least the following factors are prioritized for RLM/BM relaxation study,
  DRX cycle (option 1) for both 20ms and 40ms cycle length
The following factors can also be considered for evaluation. Companies are encouraged to evaluate the following factors and clarify the corresponding assumption.
  Option 2: RS configurations,
    2a: RLM/BFD-RS types
    2b: Periodicity of SSB or CSI-RS resource
    2c: BW of RLM/BFD-RS types
    2d: the relation to RSs for RRM
    2e: relation to RS for other L1 measurement
    2f: WUS is applied or not
  Option 3: N factor (# of RX beams for FR2)
  Option 4: P (scale factor with consideration of overlap with measurement gap and/or SMTC window)

## Slide 5
Issue 2-2-2: Evaluation metrics, system impact aspects
  Study the system impact of relaxed RLM/BFD measurements, taking in to account the following evaluation metrics:
    increased latency in RLF triggering (for RLM)
    increased latency in beam failure detection and the initiation of beam recovery procedure (for BFD)
    Delta SINR as one of the performance statistic to evaluate the RLM/BFD performance impact
  RAN4 to discuss the impact of RLM/BM relaxation on PDCCH monitoring.

## Slide 6: Issue 2-3-1: Scheme of RLM/BFD measurements relaxation
At least extending evaluation period of RLM/BFD measurement (Option 1) to be considered as the scheme of RLM/BFD measurements relaxation. FFS schemes as follows
  Option 1a: RAN4 to further discuss use of a scaling factor for defining the relaxed RLM/BM evaluation period and indication intervals.
  Option 2: Reducing the number of candidate beams when UE fulfilled relaxed criteria can be a feasible way to reduce power consuming.
  Option 3: Reducing the number reducing the sample number.

## Slide 7: Issue 2-3-2: Criteria which the UE is allowed to relax the RLM/BM requirements
RAN4 to further study the criteria which the UE is allowed to relax the RLM/BM requirements, according to UE mobility and/or serving cell’s quality.
Note: The options discussed in RAN4 97e meeting are listed below for information.
  Option 1: UE mobility
    1a: Low mobility criteria, e.g. R16 RRM relaxation criterion can be used as a starting point.
    1b: other solutions.
  Option 2: Serving cell’s quality (e.g. RSRP, SINR)
    2a: at-cell-center criteria, e.g. R16 RRM relaxation criterion can be used as a starting point.
    2b: the measured SINR is above one additional threshold (e.g. SINR > 2dB).
    2c: other solutions.

## Slide 8: Issue 2-3-3: Network or UE to determine if the criteria for relaxation is fulfilled
The following options are FFS
Option 1: Low mobility scenario under which the UE is allowed to relax the RLM/BM requirements is determined by the network.
Option 2: Low mobility scenario under which the UE is allowed to relax the RLM/BM requirements is determined by the UE.
Option 3: Low mobility scenario under which the UE is allowed to relax the RLM/BM requirements is determined by both the network and UE.

## Slide 9: Issue 2-4-1: Reverting to the normal RLM operation
The following options are FFS
Option 1: The UE while performing relaxed RLM upon detecting certain number of out-of-sync indications or upon triggering T310 reverts to the normal RLM operation (i.e. without relaxation).
Other options are not precluded

## Slide 10: Issue 2-4-2: Reverting to the normal BM operation
The following options are FFS
Option 1: The UE while performing relaxed BFD upon beam failure detection reverts to the normal BFD operation (i.e. without relaxation).
Other options are not precluded

## Slide 11: Issue 2-4-3: Relaxation of BM when not all serving cells in intra-band CA/DC meets relaxation criteria
RAN4 to further discuss the relaxation of BFD when not all serving cells in intra-band CA/DC meets relaxation criteria.
The following options are FFS
  Option 1A: relax on all serving cells when the relaxed criteria is fulfilled in one serving cell.
  Option 1B: relax only on serving cells where the relaxed criteria is fulfilled.
  Option 1C: Other solutions