## Slide 1: 3GPP TSG-RAN WG4 Meeting #97-e Electronic Meeting, 2– 13 Nov, 2020
Huawei, HiSilicon
WF on CSSF calculation for Inter-RAT MO
R4-2017331

## Slide 2: Open issue
This WF is about the inter-RAT measurement configured by LTE PCell on NR serving carriers when UE is in EN-DC
Base on existing requirements in 36.133 and 38.133, there is ambiguity on whether the inter-RAT measurement is assumed to be performed within MG or outside MG, and how the inter-RAT MO should be accounted in CSSF outside MG and CSSF within MG. There may be different UE implementations:
  Implementation#1: inter-RAT measurement is always performed within MG
  Implementation#2: inter-RAT measurement are performed in the same way as NR intra-frequency measurement, i.e. it can be within or outside MG depending on whether SSB is contained in the active BWP, and whether SMTC is fully overlapping with MG

## Slide 3: WF
FFS whether/how to update Rel-15 requirements on CSSF outside MG and CSSF within MG to account for both UE implementations in the previous page
  Option 1: no change to Rel-15 CSSF calculation
  Option 2: count the NR inter-RAT MO on NR serving CC configured by LTE MN that can be measured without MG in CSSF outside MG
    Option 2a: remove the inter-RAT MOs counted in CSSF outside MG from CSSF within MG, and further discuss allowing existing implementations not to meet the updated requirements
    Option 2b: do not remove the inter-RAT MOs counted in CSSF outside MG from CSSF within MG
  Other options not precluded

## Slide 4: WF
FFS for calculation of CSSF outside MG, whether to consider merging of intra-frequency MO configured by NR SN and inter-RAT MO configured by LTE MN on the same serving frequency that are measured without MG
  Option 1: yes
    Option 1a: MO merging condition is same as MO merging conditions in clause 9.1.3.2 of 38.133
    Option 1b: MO merging condition is different from MO merging conditions in clause 9.1.3.2 of 38.133
  Option 2: no
FFS for calculation of CSSF with MG, whether to consider merging of two MOs configured by LTE MN and NR SN on the same frequency that are measured within MG
  Option 1: yes
    Option 1a: MO merging condition is same as MO merging conditions in clause 9.1.3.2 of 38.133
    Option 1b: MO merging condition is different from MO merging conditions in clause 9.1.3.2 of 38.133
  Option 2: no