## Slide 1: WF on NR-U remaining BS RF core requirements
Nokia, Nokia Shanghai Bell
R4-2017461
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, November 2th – 13th 2020

## Slide 2: Background
This WF summarizes agreements from RAN4#97-e meeting on remaining BS RF core requirements. Following contributions were submitted for NR-U BS RF agenda:
[1] R4-2015372, On band n96 remaining issues, Nokia, Nokia Shanghai Bell
[2] R4-2016124, Discussions on remaining issue of NR-U BS RF requirements, ZTE Corporation
[3] R4-2015374, BS OBUE mask for NR-U, Nokia, Nokia Shanghai Bell
[4] R4-2015695, On remaining issues for BS TX, Huawei, HiSilicon
[5] R4-2015725, Discussion on remaining NR-U BS RF Requirements, Ericsson
[6] R4-2015373, On interfering signals for NR-U Rx requirements, Nokia, Nokia Shanghai Bell
[7] R4-2015696, On remaining issues for BS RX, Huawei, HiSilicon
[8] R4-2015371, CR to TS 38.104 with NR-U remaining open issues updates, Nokia, Nokia Shanghai Bell
[9] R4-2015698, CR for TS 38.104: Corrections for NR-U, Huawei, HiSilicon
[10] R4-2016125, CR to 38.104: Corrections on NR-U BS RF requirements, ZTE Corporation
[11] R4-2015726, CR to TS 38.104: Removal of ∆fOBUE for wider than 900 MHz, Ericsson
[12] R4-2016188, CR to 36.104: Introduction of n96 medium range requirements, Nokia, Nokia Shanghai Bell
[13] R4-2016189, CR to 37.104: Introduction of n96 medium range requirements, Nokia, Nokia Shanghai Bell
[14] R4-2016190, CR to 37.105: Introduction of n96 medium range requirements, Nokia, Nokia Shanghai Bell

## Slide 3: WF on LO leakage for NR-U puncture channels
Agreements:
  To remove LO leakage exception requirements for NR-U BS

## Slide 4: WF on ΔfOBUE for band n96
Agreements:
Option 1: (Nokia, Huawei)
  To define separate table in specification for NR-U n46 and n96 for ΔfOBUE
  50MHz as ΔfOBUE for 900 MHz < FDL,high – FDL,low £ 1200 MHz for BS type 1-C and BS type 1-H
  Option 2: Remove this requirements for band n96,with additional note in emission requirements. (Ericsson)
  Agreement: Option 1
Notes: E///: The boundary for CAT A and CAT B spurious emission. We have concern on the value also have concern on separate table.
Option 3: Remove this requirements for band n96,with additional note in emission requirements.
Nokia: This has discussed over many times, this new proposal not so clear. We are referring to 3GPP, we need to have clear definition for out of band and in-band, this should be generic approach.
Huawei： We prefer option 1, otherwise many clarification needed.
Nokia: What’s the proposal from E///?
ZTE： Have concern on the proposed value [50MHz] considering FCC requirements, for sake of progress, ZTE willing to comprise with [50MHz].

## Slide 5: WF On ΔfOOB for band n96
Agreements:
  To define separate table in specification for NR-U n46 and n96 for ΔfOOB
  70MHz as ΔfOOB for 900 MHz < FDL,high – FDL,low £ 1200 MHz for BS type 1-C and BS type 1-H

## Slide 6: WF on IBB interfering signal power level for band n96 for LA BS
Agreements:
  To define -35dBm for LA BS IBB interfering signal power level for band n96

## Slide 7: WF on IBB interfering signal power level for band n96 for MR BS
Agreements:
  To define -38dBm for MR BS IBB interfering signal power level for band n96

## Slide 8: WF on OOBB requirement for band n96
Agreements:
  To define -15dBm for band n96 OOBB requirement interfering signal power level and update the frequency offset aligned with LAA as:
Operating Band | Centre Frequency of Interfering Signal [MHz] |  |  | Wanted Signal mean power (dBm) | Interfering Signal mean power (dBm) | Type of Interfering Signal
n46, n96 | (FUL_low -500) (FUL_high +ΔfOOB) | to to | (FUL_low -ΔfOOB) (FUL_high +500) | PREFSENS +6dB | -35 | CW carrier
 | 1 (FUL_high +500) | to to | (FUL_low -500) 12750 | PREFSENS +6dB | -15 | CW carrier

## Slide 9: WF on Dynamic range interfering signal power level for band n96
Agreements:
  To align interfering signal levels for LA BS for band n96 and remove brackets from specification 38.104 in tables 7.3.2-3c (Dynamic range) considering 1dB difference due to NF change

## Slide 10: WF on ICS (in channel selectivity) interfering signal power level for band n96
Agreements:
  To align interfering signal levels for LA BS for band n96 and remove brackets from specification 38.104 in table 7.8.2-3c considering 1dB difference due to NF change