## Slide 1: WF on NR eMIMO PDSCH requirement
Intel Corporation
3GPP TSG-RAN WG4 Meeting #97-e
Electronic, 2nd – 13th November 2020 Agenda Item: 7.9.4.1
R4-2017529 Document for: Approval

## Slide 2: Background
      Agreed WFs for demodulation requirements for NR eMIMO WI in previous meetings
        R4-2002419 WF on demodulation and CSI requirement for NR eMIMO, RAN4 #94-e
        R4-2002420 WF on PDSCH demodulation requirements based on multi-TRP transmission for NR eMIMO, RAN4 #94-e
        R4-2005529 WF on PDSCH demodulation requirement and general aspects for NR eMIMO, RAN4 #94e-Bis
        R4-2008813 WF for general and PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes(eMBB), RAN4 #95-e
        R4-2008814 WF for PDSCH requirements with Single-DCI based multi-TRP/Panel transmission schemes (URLLC), RAN4 #95-e
        R4-2008815 Simulation assumption for PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes, RAN4 #95-e
        R4-2008816, WF on PMI Reporting Test Cases with Rel-16 Type II Codebook, RAN4 #95-e
        R4-2012662, WF for general and PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes (eMBB), RAN4 #96-e
        R4-2012663, WF for PDSCH requirements with Single-DCI based multi-TRP/Panel transmission schemes (URLLC), RAN4 #96-e
        R4-2012664, Simulation assumption for PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes, RAN4 #96-e
        R4-2012761, WF on PMI Reporting Requirement for NR eMIMO, RAN4 #96-e

## Slide 3: General

## Slide 4: Number of test cases for single-DCI/multi-DCI eMBB transmission schemes
3 test cases per duplex mode with test applicability rule (Agreement from GTW session)
Test 1a: Single-DCI with frequency offset and negative time offset and overlapping scheduling
Test 1b: Single-DCI with positive time offset, and overlapping scheduling
Test 2a: Multi- DCI with frequency offset and negative time offset and non-overlapping scheduling
Applicability rule:
  If UE only supports single-DCI based multi-TRP transmission for eMBB, it should be tested with test case 1a and test case 1b
  If UE can support both single-DCI and multi-DCI for eMBB, it should be tested test 2a and test 1b
  If UE only support multi-DCI transmission schemes for eMBB, it should be test 2a

## Slide 5: Test cases for URLLC Transmission schemes
Define performance requirement for URLLC transmission schemes with test applicability rule (Agreement from GTW session)
Only FDM scheme A for UE capable of supportFDM-SchemeA and inter-slot TDM scheme for UE capable of supportInter-slotTDM
Test applicability
  FDM scheme A is skipped if UE passes the multi-DCI based multi-TRP Tx requirements
  Inter-slot TDM scheme is skipped if UE passes URLLC slot aggregation requirements and anyone of the other multi-TRP Tx requirements

## Slide 6: PDSCH scheduling
Schedule PDSCH data in TDD special slots for multi-DCI based Tx scheme and single-DCI based schemes except inter-slot TDM scheme.
Schedule PDSCH data in DL slots which carries TRS Tx for single/multi-DCI based Tx schemes

## Slide 7: Precoding scheme
      Independent precoding generation is applied for both TRPs for both single-DCI/multi-DCI based multi-TRP transmission schemes.
      PDSCH & PDSCH DMRS precoding is configured with Single Panel Type I, with PRB bundling granularity and random precoder selection is updated per slot.

## Slide 8: Single/multi-DCI based SDM Tx schemes

## Slide 9: FRC for single/multi-DCI based SDM transmission
Introduce new FRC for Single/multi-DCI based SDM transmission requirements with
  Multi-DCI based SDM schemes
    FDD: 26PRB per codeword
    TDD: 53PRB per codeword
    Two TRS configurations every 20ms
  Single-DCI based SDM schemes
    Two TRS configurations every 20ms
  Reference channel
    R.PDSCH.1-3.2 FDD: single-DCI based SDM schemes in FDD
    R.PDSCH.1-3.3 FDD: multi-DCI based SDM schemes in FDD
    R.PDSCH.2-3.2 TDD: single-DCI based SDM schemes in TDD
    R.PDSCH.2-3.3 TDD: multi-DCI based SDM scheme in TDD

## Slide 10: Single-DCI based URLLC Tx schemes

## Slide 11: Number of test cases
Test 1a: Single-DCI based FDM scheme A with frequency offset and negative time offset
  Frequency offset
    FDD with 15 kHz SCS: 200Hz
    TDD with 30 kHz SCS: 300Hz
  Time offset
    FDD with 15 kHz SCS: - 0.5 us
    TDD with 30 kHz SCS: - 0.25 us
Test 1b: Single-DCI based inter-slot TDM scheme with frequency offset and positive time offset
  Frequency offset
    FDD with 15 kHz SCS: 200Hz
    TDD with 30 kHz SCS: 300Hz
  Time offset
    FDD with 15 kHz SCS: 2 us
    TDD with 30 kHz SCS: 1 us

## Slide 12: Simulation assumptions (1)
PRB precoding granularity
  Wideband precoding for single-DCI based FDM scheme A
  2 PRB precoding granularity for single-DCI based inter-slot TDM scheme
Antenna port indices and MIMO Rank
  FDM Scheme A
    Rank 2: {1000, 1002} DMRS antenna port with TCI state#1 and {1001, 1003} DMRS antenna port with TCI state#2
  Inter-slot TDM
    Rank 1: 1000 DMRS antenna port with TCI state#1 and 1001 DMRS antenna port with TCI state#2
Two Tx occasions for inter-slot TDM
Note: For more details please refer to R4-2017530.

## Slide 13: Simulation assumptions (2)
MCS
  FDM scheme A: MCS 19 from MCS table 3
  Inter-slot TDM scheme: MCS 19 from MCS table 3
Note: For more details please refer to R4-2017530.

## Slide 14: Test Metric
70% TP for FDM scheme A
1% BLER for inter-slot TDM scheme (BLER is calculated after all transmission)

## Slide 15: Requirements definition
Set the requirement (SNR) based on the simulation result collection, not from requirements for multi-DCI based Tx scheme.
Companies are encouraged to provide both alignment and impairment results to finalize the PDSCH requirement with single-DCI/multi-DCI based multi TRP transmission schemes based on agreed simulation assumption R4-2017530 in the and complete WI next meeting