## Slide 1: WF on RF requirements for Rel-17 Tx switching enhancement
3GPP TSG-RAN WG4 Meeting #97e
Electronic Meeting, 2-13 Nov., 2020
Agenda: 12.2.2.2, 12.2.2.3
R4-2017815
China Telecom

## Slide 2: Background
WID approved at RAN #89e
  RP-202088, New WID proposal: RF requirements enhancement for NR frequency range 1 (FR1) in Rel-17
  Two topics in the WID are covered in the WF
    Topic #1: 2Tx-2Tx switching between carrier 1 and carrier 2 for SUL and UL CA
    Topic #2: 1Tx-2Tx and 2Tx-2Tx switching between band A (carrier 1) and band B (carrier 2+3) for SUL and UL CA

## Slide 3: WF on 2Tx-2Tx switching between two carriers (1/3)
  Length of switching period
  Reuse Rel-16 values for UL CA and SUL, i.e., report {35us, 140 us, or 210us} per pair of UL bands per band combination, and apply the same set of values for switching between different cases in the WID
  Location of switching period
  Reuse Rel-16 agreement for UL CA and SUL, i.e., semi-statically configure the switching period on one of the two uplink carriers
  Transient period
  Reuse Rel-16 agreement for UL CA and SUL, i.e., 2x10 us transient period in addition to the switching period
  UL outage due to switching
  Reuse Rel-16 agreement for UL CA and SUL, i.e., UL outage due to switching is applicable to both carrier 1 and carrier 2

## Slide 4: WF on 2Tx-2Tx switching between two carriers (2/3)
  Applicability of DL interruption
  Reuse the Rel-16 agreement:
    For SUL+TDD and TDD+TDD CA with the same UL-DL pattern, DL interruption is not required.
    For the other duplex mode combinations, define different capabilities for UEs with and without DL interruption.
      UE capability is defined as per band per band combination for each band pair supporting UL Tx switching.

## Slide 5: WF on 2Tx-2Tx switching between two carriers (3/3)
2-layer MIMO support
  For 2Tx-2Tx switching, it is mandatory to support 2-layer PUSCH transmission in both carrier 1 and carrier 2 for UL CA and SUL.

## Slide 6: WF on 1Tx-2Tx and 2Tx-2Tx switching between band A and band B (1/2)
Switching time mask related requirements
  For switching time mask related requirements for inter-band SUL and CA (including the length of switching period, location of switching period, transient period and uplink outage due to switching), the same agreements are applied for the scenarios with either one carrier or two contiguous aggregated carriers on band B
Applicability of DL interruption
  The same agreements are applied for the scenarios with either one carrier or two contiguous aggregated carriers on band B
    For SUL+TDD and TDD+TDD CA with the same UL-DL pattern, DL interruption is not required.
    For the other duplex mode combinations, define different capabilities for UEs with and without DL interruption.
      UE capability is defined as per band per band combination for each band pair supporting UL Tx switching.

## Slide 7: WF on 1Tx-2Tx and 2Tx-2Tx switching between band A and band B (2/2)
2-layer MIMO support
  FFS whether to Mandate 2-layer PUSCH transmission in all the carriers supporting 2Tx, including the two carriers on band B in 1Tx-2Tx switching scenario and the three carriers on band A+B for 2Tx-2Tx switching scenario.

## Slide 8
Thanks!