## Slide 1
Agenda item: 4.4.1(BS RF, General)
Source: SoftBank Corp., KDDI Corporation, NEC Corporation
Title: Support of Japan regulation for 2.5GHz(BWA) in NR BS
Document for: Information
3GPP TSG-RAN WG4 Meeting #98-e R4-2101016
Electronic meeting, 25 Jan – 5 Feb, 2021

## Slide 2: 2.5GHz regulation in Japan
2.5GHz in Japan
  Designated as “BWA”(Broadband Wireless Access), accommodating various RATs
  Different from “Cellular” spectrum where the requirements are basically aligned with those of 3GPP
  In LTE, we have adapted B41 for the range with necessary regional requirements added
Updated regulations for NR
  CBW: 10/20/30/40/50MHz
  Tx max power limitation stays as it is : 20W/10MHz
  Unwanted emission : -22dBm or -30dBm/MHz regions are relaxed to -13dBm/MHz but -42dBm/MHz range stays as it is
  Other requirements can be treated as per LTE: no modification made when relevant 3GPP requirements are tighter or equivalent

## Slide 3: Unwanted Emission in Japan
Mask
  1) ”Mask” is only applied in 2535 – 2655MHz
    Within 1.5*CBW away from the center : no requirement
    Within 1.5*CBW to 2.5*CBW away from the center: -13dBm/MHz
      Same relaxation goes for LTE
      Further than 2.5*CBW from the center : Follow the ”spurious” below: so-called 250% rule
Spurious Emission
  2) “Spurious” is applied to ranges other than 2535-2655MHz, or 2535-2655MHz but further than 2.5*CBW away from the center
  -42dBm/MHz stays at 2505 – 2535MHz but -22dBm/MHz and -30dBm/MHz ranges are relaxed to -13dBm/MHz

## Slide 4: Issue(1)
Architectural mismatch (1)
  In 3GPP, antenna connector based definition has been applied while max power is not limited
  In BWA in Japan, requirements are based on ”cell” in 3GPP term, with a limitation on Max power per cell
  Mapping between possible flexibilities in 3GPP on a cell configuration and J-regulation should be addressed
    For 4Tx in a cell for example:
    In 1-H/1-O, there would be variations on how to configure 4Tx in a cell
    1-C allows 4x unwanted emission in 3GPP but not in Japan-BWA (but practically unwanted emission could be reduced due to the max power limitation per cell)
    In J-Reg, scaling is allowed in 1-H/1-O type of configurations but not allowed for 1-C type

## Slide 5: Issues
Architectural mismatch (2)
  It does not seem feasible to map straight-forward and stringent
  It is proposed to put a note of “per-cell definition” where necessary and not to go into detail in architectural descriptions

## Slide 6: Others
Other Notes
  Release: prefers to modify from REL-15
    We need to add n90 in REL-16
  Handling of 37 series: to be postponed in Apr. as we need extra-maintenance efforts
  n34 range is not enlisted as an NR frequency in the regulation: no need to add this time

## Slide 7: EOF