## Slide 1: WF on FR2 UEs that support inter-band DL CA with IBM
Sony
3GPP TSG-RAN WG4 Meeting # 98-e R4-2103111
Electronic Meeting, Jan. 25-Feb. 5, 2021

## Slide 2: Background
In RAN4#98-e, the applicability and requirement of IBM for DL CA configurations has been further discussed in email thread 139 [1], with the following issues:
  The definition of IBM
  The requirement framework
  IBM inter-band CA requirements
In addition, the following issue from email thread 138 [2] has also been captured in this WF:
  Whether define any default beam management type

## Slide 3: The definition of IBM
It is agreed that the standard would benefit from introduction of a definition.
  The definition of IBM will be introduced in 38.101-2
The IBM definition is agreed as:
  IBM (Independent Beam management): A UE that supports inter-band CA with IBM selects its DL Rx beam(s) for all CCs in each configured band based on DL reference signals measurements made in that band.
It is agreed that RAN4 will not label CBM or IBM as a default BM method for any band combination. Used beam management is based on UE capability. This issue is not discussed anymore in RAN4

## Slide 4: Framework of IBM inter-band CA requirement
It is agreed that IBM inter-CA requirement framework established for n260+n261 shall be at least applied to any requested CA band pair from different frequency groups (parameter values discussed separately)
Further discuss whether IBM inter-CA requirement framework established for n260+n261 shall be applied to any requested CA band pair from the same frequency group (parameter values discussed separately)

## Slide 5: IBM inter-band CA requirements
It is agreed that
  The FR2 inter-band DL CA, maximum input level, ACS, and in-band blocking requirement are band combination agnostic and shall be reused for any new FR2 inter-band combinations.
  Apply release independent approach from Rel-16 to inter-band CA including intra-band contiguous CA with maximum number of bands is 2 bands.
    Further discuss maximum number of CCs for such combinations.
      Option 1: no need to limit the maximum number of CCs
      Option 2: maximum number of CCs is FFS, but at least 12
Further discuss how to define the relaxation values of FR2 inter-band CA between the low band group (n257, n258 or n261) and high band group (n259 and n260) for IBM.
  Option 1: the same relaxation values as the ones for CA_n260-n261, i.e., 3.5 dB for all these band pair.
  Option 2: The relaxation values should be further discussed based on per band pair case by case.
  Option 3: The relaxation values for CA_n260-n261 are reused as the ones for CA_n258-n260 and CA_n257-n259. For other band pairs, we should be further discussed based on per band pair case by case.

## Slide 6: Reference
[1] R4-2102987 Email discussion summary for [98e][139] NR_RF_FR2_req_enh2_Part_2 Moderator (Qualcomm Incorporated)
[2] R4-2102986 Email discussion summary for [98e][139] NR_RF_FR2_req_enh2_Part_1 Moderator (Nokia)