## Slide 1: Way Forward on BCS reporting and support for intra-band EN-DC band combinations
T-Mobile USA
3GPP TSG RAN WG4 Meeting #98-e R4-2103115
Online, , 25th Jan 2021 - 5th Feb 2021

## Slide 2: LS from RAN To RAN4
To RAN WG4 group.
ACTION: RAN respectfully requests RAN4 to complete the following for RAN#91e:
  A) Clarify if higher order (i.e. those band combinations which the UE indicates support for explicitly in UE capability signalling) EN-DC band combinations with a common band on the LTE and NR side such as DC_2A-7A-7A-66A-n66A and DC_2A-71A_n71A need to report a BCS for intra-band EN-DC (as defined in 38.101-3, section 5.3B.1), even if the UE doesn’t support the intra-band UL configurations DC_66A_n66A or DC_71A_n71A respectively. If the UE does not report the EN-DC BCS for such a combination, what can the network assume about the configuration limitations for the common bands (e.g. LTE band 71 and NR band n71) in the combination?
  B) Resolve the general question of classification of intra-band EN-DC band combinations according to UL support. If the UE doesn't support UL on intra-band EN-DC part of a band combination, is band combination classified as "intra-band EN-DC band combination"?
  C) Indicate the RAN4 understanding on A) and B) to RAN2 by the end of the first meeting week of RAN4#98e (to allow RAN2 to finalize their work).
  D) Agree to necessary CRs taking the conclusions of A) and B) into account.

## Slide 3: Goal
The network need to know without a doubt what LTE and NR channel bandwidths the UE supports for “higher order (i.e. those band combinations which the UE indicates support for explicitly in UE capability signalling) EN-DC band combinations with a common band on the LTE and NR side such as DC_2A-7A-7A-66A-n66A and DC_2A-71A_n71A need to report a BCS for intra-band EN-DC (as defined in 38.101-3, section 5.3B.1), even if the UE doesn’t support the intra-band UL configurations DC_66A_n66A or DC_71A_n71A respectively.”

## Slide 4: Question A.1) from the LS
Q: Clarify if higher order (i.e. those band combinations which the UE indicates support for explicitly in UE capability signalling) EN-DC band combinations with a common band on the LTE and NR side such as DC_2A-7A-7A-66A-n66A and DC_2A-71A_n71A need to report a BCS for intra-band EN-DC (as defined in 38.101-3, section 5.3B.1), even if the UE doesn’t support the intra-band UL configurations DC_66A_n66A or DC_71A_n71A respectively?
Response:
Intel, MediaTek, Oppo, Nokia, T-Mobile, and CHTTL all supported Option 1 in Round 1, which was that the intra-band BCSs apply.
Other companies including Apple, Qualcomm, Samsung, Huawei and ZTE supported option 2 in Round 1, which was that the intra-band BCSs do not apply.
Because of this discrepancy and also hardware limitations there are some UEs on the market that support all of the channel bandwidths, and some that support the channel bandwidths based on BCS0 and the network can’t differentiate between them.

## Slide 5: Proposal for A.1)
Response to the LS: Yes, higher order (i.e. those band combinations which the UE indicates support for explicitly in UE capability signalling) EN-DC band combinations with a common band on the LTE and NR side such as DC_2A-7A-7A-66A-n66A and DC_2A-71A_n71A do need to report a BCS for intra-band EN-DC (as defined in 38.101-3, section 5.3B.1), even if the UE doesn’t support the intra-band UL configurations DC_66A_n66A or DC_71A_n71A respectively.

## Slide 6: Question A.2) from the LS
Q: If the UE does not report the EN-DC BCS for such a combination, what can the network assume about the configuration limitations for the common bands (e.g. LTE band 71 and NR band n71) in the combination?
Ericsson, Apple, Samsung, Huawei, Qualcomm and ZTE supported Option 1 in Round 1, that the E-UTRA and NR BCSs apply, all LTE and NR channel bandwiths are supported
T-Mobile USA, Nokia and CHTTL supported Option 2 in Round 1, where the Network has to assume BCS0.
Oppo and MediaTek supported Option 3, that it is mandatory for the UE to report an intra-band EN-DC BCS
Because of this discrepancy, the only safe assumption is that all UEs support BCS0 if the UE does not report a BCS for the combination

## Slide 7: Proposal for A.2)
If the UE does not report the intra-band EN-DC BCS for such a combination, the network can assume that the UE supports intra-band the default BCS for the common bands (e.g. LTE band 71 and NR band n71) in the combination.
(Note to RAN4: My RAN2 colleague suggested I use default BCS and then define the default BCS in the RAN4 specs rather than using BCS0 in the RAN2 specs.)

## Slide 8: Question B) from the LS
Resolve the general question of classification of intra-band EN-DC band combinations according to UL support. If the UE doesn't support UL on intra-band EN-DC part of a band combination, is band combination classified as "intra-band EN-DC band combination"?
Ericsson, T-Mobile USA, Intel and MediaTek supported Option 1, that it is.
Apple, Samsung, Huawei, Oppo, Qualcomm, ZTE and Nokia supported Option 2 or 2B or 2C.

## Slide 9: Discussion on B)
Since these combinations have both inter-band and intra-band on the downlink and inter-band on the uplink, the RAN4 specs do not currently clearly specify if they are intra-band combinations or not. Even combinations with both inter and intra band downlink and intra-band uplink EN-DC appear in the inter-band tables in 38.101-3.
This question is likely related to a previous LS from RAN4 to RAN2 that used this terminology, which has subsequently been used in 38.306.
Rather than spending a lot of debating a somewhat philosophical question, the simplest solution would be to tell RAN2 that the such a combination is still intra-band EN-DC. Then the RAN2 specs wouldn’t need to change, and BCSs would be reported for the combinations in question.

## Slide 10: Proposal for B
Proposal 2: If the UE doesn't support UL on the intra-band EN-DC part of a band combination that has intra-band and inter-band downlink, the band combination is still an “intra-band EN-DC band combination.”

## Slide 11: Question D
Agree (if necessary) CRs taking the conclusions of A) and B) into account.
Based on Proposal B, RAN4 should work on CRs that clarifies that which combinations are “intra-band EN-DC band combinations.” RAN4 should also document which BCS is the default BCS for legacy UEs that don’t report the a BCS.

## Slide 12: Proposals for approval
Proposal 1 (Response to the A.1): Yes, higher order (i.e. those band combinations which the UE indicates support for explicitly in UE capability signalling) EN-DC band combinations with a common band on the LTE and NR side such as DC_2A-7A-7A-66A-n66A and DC_2A-71A_n71A do need to report a BCS for intra-band EN-DC (as defined in 38.101-3, section 5.3B.1), even if the UE doesn’t support the intra-band UL configurations DC_66A_n66A or DC_71A_n71A respectively.
Proposal 2 (Response to A.2): If the UE does not report the intra-band EN-DC BCS for such a combination, the network can assume that the UE supports intra-band the default BCS for the common bands (e.g. LTE band 71 and NR band n71) in the combination.
Proposal 3 (Response to B): If the UE doesn't support UL on the intra-band EN-DC part of a band combination that has intra-band and inter-band downlink, the band combination is still an “intra-band EN-DC band combination.”
Proposal 4: Based on Proposal B, RAN4 should work on CRs that clarifies that which combinations are “intra-band EN-DC band combinations.” RAN4 should also document which BCS is the default BCS for legacy UEs that don’t report the a BCS.

## Slide 13: Additional discussion material

## Slide 14: Additional Discussion on A.1)
Need to differentiate between legacy and new UEs.
  Because of the disconnect between company’s views on this issue, for combinations like the ones described in the LS, some legacy UEs support only the bandwidth combination in the intra-band BCS0, and other UEs support all of the possible bandwidth channel bandwidths. Therefore, for exiting UEs it not possible for a network to know what downlink intra-band channel bandwidth combination a given UE supports, so the only safe assumption for existing UEs is the common set, which would be the intra-band BCS0.
  If RAN4 now decides that for downlink intra-band EN-DC the UE needs to support all LTE and NR channel bandwidths for the common LTE and NR bands, without modified signalling it would not be possible for the network to distinguish between a new or legacy UE that supports all channel bandwidths, and a legacy UE that does not.
  To resolve this problem for RAN4 to decided that the intra-band BCSs do apply for the combinations described in the LS. If future UEs do report an intra-band BCS for these combinations, then the network will be able to at least distinguish between a new UE that supports the reported BCS(s), and a legacy UE that supports BCS0 at a minimum.

## Slide 15: Additional Discussion on A.2)
As discussed in A.1, since some companies interpreted 38.101-3 such that all combinations of the LTE and NR channel bandwidths have to be supported and other companies assumed that the BCS determine the intra-band channel bandwidths for the combinations described in the LS, it is not possible to distinguish between legacy UEs that support all possible combinations of LTE and NR channel bandwidths, and ones that support only BCS0 or a different BCS if they don’t report a BCS. Therefore, the only safe assumption is that existing UEs only support the intra-band channel bandwidths in the intra-band EN-DC BCS0.

## Slide 16: Additional discussion 1
Q: Will the network be confused if a UE reports an intra-band EN-DC BCS, but the UE does not support uplink intra-band EN-DC?
A: Some companies commented that if a UE reports an intra-band EN-DC BCSs but does not support uplink intra-band EN-DC that the network might get confused, and maybe think that the UE supports uplink intra-band EN-DC. This is not the case because the UE capabilities report what downlink and what uplink combinations that the UE supports. If the UE does not support uplink intra-band EN-DC, it will not report the uplink intra-band combination as being supported in its UE capabilities. There will be no confusion cause by reporting an intra-band BCS for UEs that only support intra-band on the downlink for a higher order EN-DC combination. RAN specifically asked us if a BCS needs to be reported or not for these combinations, so we should decide and answer the question.

## Slide 17: Additional Discussion 2
Q: How can the network tell which combinations of channel bandwidths for common LTE and NR bands for downlink inter+intra-band EN-DC with inter-band uplink EN-DC?
As of today, for existing UEs there is no way for the network to tell if an existing UE supports all of the possible combinations of LTE and NR channel bandwidths for common LTE and NR bands in inter-band uplink and inter+intra-band downlink EN-DC band combinations. Since some companies have interpreted 38.101-3 to say that all combinations of LTE and NR channel bandwidth are supported for the common band LTE and NR carriers downlink intra-band EN-DC and other companies have interpreted 38.101-3 to say that all combinations of the LTE and NR common band channel bandwidths are supported, the common set of BCS0 is the only thing that we know for certain.
Future UEs could report the intra-band EN-DC BCS for “higher order (i.e. those band combinations which the UE indicates support for explicitly in UE capability signalling) EN-DC band combinations with a common band on the LTE and NR side such as DC_2A-7A-7A-66A-n66A and DC_2A-71A_n71A.”

## Slide 18: Additional Discussion 3
Q) Won’t UE and chipset vendors who did the work to ensure that they support all configurations of the intra-band downlink LTE and NR channel bandwidths be penalized if the network cannot utilize all of them, and are limited to using BCS0?
A) As it is now, the network cannot tell for sure what combinations of LTE and NR channel bandwidths that a legacy UE supports for the downlink intra-band components. If the network assumes that the UE supports all combinations of channel bandwidths and it does not, there is a risk of a configuration failure. Therefore, the network will be taking a risk if it configures a UE with an intra-band downlink configuration that is not included in BCS0, or a reported BCS. This problem will not improve until all of the UEs that don’t support all of the combinations of LTE and NR channel bandwidths are taken out of commission. So, if we don’t add BCS signalling, even in the future the only safe assumption will be that the UEs only support BCS0. This would be a bad outcome for everyone.