## Slide 1: WF on NR mobility enhancement maintenance
Apple
3GPP TSG-RAN WG4 Meeting #98-e R4-2103534
Electronic Meeting, 25th Jan. – 5th Feb. 2021

## Slide 2: Agreement on issue 1-1
Issue 1-1: Further clarification on DL-to-UL and UL-to-DL switching time
  Option 1: same as option 1 in R4-2017093: clarify that 13us switching time is allowed between source cell and target cell: (Apple)
    Note 2: For DAPS handover on a TDD band, a UE is not expected to transmit in the uplink to source or target cell earlier than NRX-TX after the end of the last received downlink symbol from source or target cell in the same TDD band where NRX-TX=25600Tc.
    Note 3: For DAPS handover on a TDD band, a UE is not expected to receive in the downlink from source or target cell earlier than NTX-RX after the end of the last transmitted uplink symbol toward source or target cell in the same TDD band where NTX-RX=25600Tc.

## Slide 3: Agreement on issue 1-1 (Cont.)
Issue 1-1: Further clarification on DL-to-UL and UL-to-DL switching time
  Option 2: Add conditions for not expected to transmit / not expected to receive covering both source and target cell. Autonomous interruption is allowed if these conditions are not met: (Ericsson)
    Note 2: For DAPS handover on a TDD band, a UE shall be capable to transmit in the uplink to source or target cell after NRX-TX from the end of the last received downlink symbol from source or target cell in the same TDD-band where NRX-TX=25600Tc. When this condition is not met, the UE may perfrom autonomous interruption as shown in Table 6.1.3.2-2.
    Note 3: For DAPS handover on a TDD band, a UE is shall be capable to receive in the downlink from source or target cell after NTX-RX after the end of the last transmitted uplink symbol towards sorce or target cell in the same TDD-band where NTX-RX=25600Tc. When this condition is not met, the UE mau perfrom autonomous interruption as shown in table 6.1.3.2-3.

## Slide 4: Agreement on issue 1-1 (Cont.)
Scenario | Allowed interruption
Target cell earlier than source cellNote 1, prior to start of random access | Not applicable
Target cell later than source cell Note 1, prior to start of random access | The UE may stop receiving the target DL up to 25600 Tc prior to the start of the source UL
Target cell earlier than source cell Note 1, after start of random access | The UE may stop receiving the source DL up to 25600 Tc prior to the start of the target UL
Target cell later than source cell Note 1, after start of random access | The UE may start transmitting the source UL up to 25600 Tc after the start of the source DL
Note 1: As observed by UE at antenna connector | 
Scenario | Allowed interruption
Target cell earlier than source cell Note 1, prior to start of random access | The UE may start receiving the target DL up to 25600 Tc after the end of the source UL
Target cell later than source cell Note 1 prior to start of random access | Not applicable
Target cell earlier than source cell Note 1, after start of random access | The UE may stop transmissions of the source UL up to 25600 Tc prior to the start of target DL reception.
Target cell later than source cell Note 1, after start of random access | The UE may start receiving the source DL up to 25600 Tc after the end of the target UL
Note 1: As observed by UE at antenna connector | 
Table 6.1.3.2-3: Autonomous interruptions related to UL to DL switching for syncrounous TDD DAPS handover in the same band
Table 6.1.3.2-2: Autonomous interruptions related to DL to UL switching for syncrounous TDD DAPS handover in the same band

## Slide 5: Agreement on issue 1-2
Issue 1-2: Tinterrupt2 of FR1 intra-freq DAPS hadover
Agreement: To separately define interruption time Tinterrupt2 of FR1 intra-freq DAPS hadover for sync and async cases, when the BWP of target cell is smaller than the BWP of source cell.