## Slide 1: WF on RRM requirements for FR2 Inter-band DL CA and UL CA
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #98e
E-meeting, January 25th – February 5th, 2020
R4-2104095
Document for: Approval

## Slide 2: Topic #1-1 Deployment and UE assumptions
Issue 1-1-1: Deployment scenarios assumption for CBM
  Agreements:
    Option2: Assumption of deployment and band pair for IBM UE and CBM UE should follow the RF session conclusions (Up to 2nd round discussion)
Issue 1-1-2: UE assumptions for CBM
  Agreements (in GTW):
    For CBM capable UE
      UE is assumed to make reception with one beam at a time, i.e. similar to Rel-15 baseline UE assumption
      FFS for number of panels UE can use for CBM and it is up to RF session conclusions. At least one active panel at a time can be assumed as baseline for RRM requirements definition.

## Slide 3: Topic #1-1 Deployment and UE assumptions
Issue 1-1-3: Deployment scenarios assumption for IBM
  Agreements: Follow the agreements in Rel16 i.e. there is no restriction on deployment scenario i.e. network assumes IBM UE supports both co-located and non-co-located deployments.
Issue 1-1-4: UE assumptions for IBM
  Agreements (in GTW):
    IBM capable UE is assumed to be capable of receiving signals for FR2 inter-band CA with different beam directions at the same time

## Slide 4: Topic # 1-2 MRTD for CBM
Issue 1-2-1: Can we assume symbol level alignment within CP length?
FFS:
  Option 1: Symbol level alignment should be with CP length (Apple, MTK, Xiaomi, OPPO)
  Option 2: We cannot assume symbol level alignment for common beam management (E///, Nokia).
  Option 3: RAN4 should focus on how to define MRTD requirements for CBM UE (Huawei, Intel)

## Slide 5: Topic # 1-2 MRTD for CBM
Issue 1-2-2: How to determine MRTD for FR2 inter-band CA?
  FFS:
    Option 1: Reuse FR2 intra-band MRTD i.e. 260ns (Apple, Intel, OPPO, MTK, LG, QC, Xiaomi)
    Option 2: 3us (NEC, Nokia, E///)
    Option 3: 3us MRTD requirements can be applied for co-located deployment and >3us MRTD requirements can be applied for non-co-located deployment (Huawei, E///)
      Option 3a: 4~5us (Huawei)
      Option 3b: 8us (Huawei)
  Tentative Agreements in GTW for further discussion:
    Inter-band MRTD is FFS
      MRTD requirements are derived under assumption of co-located deployments
        Note: this does not preclude using co-located or non-co-located deployments in the field
      MRTD value
        Option 1: 260ns (i.e. FR2 intra-band MRTD)
        Option 2: 3us
        Other options are not precluded
      Companies are encouraged to evaluate the impact on the performance in case of using MRTD larger than CP
      Session chair: No consensus reached. Continue the discussion.

## Slide 6: Topic # 1-2 MRTD for CBM
Issue 1-2-3: Performance impact due to Rx beam switching
FFS:
  Option 1: Demodulation performance degradation due to Rx beam switch should be noted in MRTD requirements for CBM UE if MRTD is larger than CP (LG, Xiaomi, Huawei, OPPO)
  Option 2: In worst case performance degradation of up to 1 OFDM symbol is allowed for UE operating in CBM during RX beam switch (NEC)
    Option 2a: The impact of Rx switch can be beyond 1 symbol. (Apple, Intel)
  Option 3: RAN4 should further study in Rel-17 to reduce the worst case (1 OFDM symbol or beyond) performance degradation (NEC, Intel)
  Option 4: UE could safely switch beams (E///)
  Option 5: Define different sets of requirements (260ns vs 3us) based on the UE capability and leave the degradation issue resolution to UE implementation. (Intel)
  Option 6: introduce a mechanism to allow UE to autonomously switch its beams, e.g. scheduling/measurement restriction (Qualcomm)

## Slide 7: Topic # 1-3 MRTD in case of IBM
Issue 1-3-1: How to determine MRTD in case of IBM?
  Agreement: For IBM capable UE, the Rel16 MRTD requirements for FR2 inter-band CA can be applied in Rel-17 and no additional discussion is required in Rel17.

## Slide 8: Topic # 1-4 MTTD for CBM
Issue 1-4-1: How to determine MTTD for CBM?
FFS:
  Option 1: 3.5 µs on condition of UE capability indication
  Option 2: If CBM based FR2 inter-band UL CA would be introduced in Rel-17, then RAN4 needs to study the MTTD requirement applicable for CBM based FR2 inter-band CA, and it is based on the conclusion of MRTD requirements for CBM UE.
Issue 1-4-2: Performance impact due to Tx beam switching
  Agreement: RAN4 needs to study how to handle impact on performance due to Tx beam switching.

## Slide 9: Topic # 1-5 MTTD for IBM
Issue 1-5-1: How to determine MTTD in case of IBM?
  Agreement: For IBM capable UE, the Rel16 MTTD requirements for FR2 inter-band CA can be applied in Rel-17 and no additional discussion is required in Rel17.

## Slide 10: Topic # 1-6 RRM Requirements for CBM UEs
Issue 1-6-1: Scope of the RRM requirements for FR2 inter-band DL CA ?
  Agreement: Scope of the RRM requirements for FR2 inter-band DL CA includes but not limited to MRTD, Scaling factor CSSFoutside_gap, interruption requirements, SCell activation requirements, Beam management requirements and scheduling/measurement restriction requirements
Issue 1-6-2: Interruption requirement
FFS:
  Option 1: The existing interruption requirements of intra-band CA can be applied (Intel, OPPO, MTK, LG, QC, OPPO, Intel, Nokia)
  Option2: The interruption requirements applied for CBM based FR2 inter-band CA need to be introduced in Rel-17, which need RF inputs on the RF architecture of CBM type UE (Huawei, MTK, Xiaomi, OPPO, Apple, NEC, E///)

## Slide 11: Topic # 1-6 RRM Requirements for CBM UEs
Issue 1-6-3: Scheduling restriction
FFS:
  Option 1: To apply an agreement from RAN4 #94-bis-e: (Intel, MTK, LG, QC, Huawei, Intel)
    “The scheduling availability requirements for FR2 inter-band CA scenario shall be introduced to clarify there is scheduling restriction on one FR2 band due to RLM/BFD/CBD/L1-RSRP measurements being performed on another FR2 band if UE uses common beam.
    The existing scheduling restriction requirements on FR2 shall be extended to serving cells in different bands.”
  Option 2: The existing scheduling/measurement restriction requirements applied for FR2 intra-band CA need to be extended to FR2 inter-band CA with CBM type UE. (Huawei, Xiaomi, E///, Nokia)
  Option 3: Need more discussion (Xiaomi, OPPO, Apple, NEC)

## Slide 12: Topic # 1-6 RRM Requirements for CBM UEs
Issue 1-6-4: Measurement restriction
FFS:
  Option 1: To apply an agreement from RAN4 #95-e: (Intel, LG, QC, Intel)
    “For CBM UEs in FR2 inter-band CA, the existing measurement restriction requirements for FR2 is applied for the RLM/BFD/CBD/L1-RSRP measurements being performed on different FR2 bands.”
  Option 2: For CBM UEs the measurement restriction applies when the SSB for RLM, BFD, CBD or L1- RSRP measurement on one band is in the same OFDM symbol as the CSI-RS for RLM, BFD, CBD or L1- RSRP measurement on another band (Intel)
  Option 2a: For CBM UEs the measurement restriction applies when the SSB for RLM, BFD, CBD or L1- RSRP measurement on one band is in the same OFDM symbols overlapping with the CSI-RS for RLM, BFD, CBD or L1- RSRP measurement on another band (MTK, LG)
  Option 3: The existing scheduling/measurement restriction requirements applied for FR2 intra-band CA need to be extended to FR2 inter-band CA with CBM type UE (Huawei, E///, Nokia)
  Option 4: More discussion is needed. (Xiaomi, OPPO, Apple, NEC)

## Slide 13: Topic # 1-6 RRM Requirements for CBM UEs
Issue 1-6-5: Scell activation delay requirements
Agreements:
  For Case 1: SCell being activated belongs to FR2 and if there is at least one active serving cell on that FR2 band, existing SCell activation delay requirements in Case 1 can be applied
FFS:
  Case 2: SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR2
    Option1 (Intel, MTK):
      If the target SCell is known, the existing known SCell requirement in Case 2 shall be applied. (E///, Nokia)
      In the case when SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR2 and the target SCell is unknown the existing SCell activation delay requirements for FR1+FR2 CA without L1-RSRP measurement delay can be reused.
    Option2: The SCell activation requirements in Case 2 applied for CBM type UE need to be defined. How to define the SCell activation requirements for CBM type UE depends on the RF architecture and MRTD requirements for CBM type UE (Huawei, MTK, QC, Xiaomi, OPPO)
    Option3: Scell activation delay would be reduced for the case if the PCell/PSCell and the target SCell are in a FR2 band pair with CBM, and the target SCell is unknown. (OPPO, E///)
    Option 4: Need further discussion (Apple, NEC)

## Slide 14: Topic # 1-6 RRM Requirements for CBM UEs
Issue 1-6-6: Scaling factor CSSFoutside_gap
FFS:
  Option 1: If FR2 inter-band CA with two bands are only considered in Rel-17, then the existing requirements on scaling factor CSSFoutside_gap in Rel-16 can be applied to Rel-17. The requirements on scaling factor CSSFoutside_gap need to be revised if FR2 inter-band CA with more than two bands will be introduced in Rel-17 (Huawei, QC, Xiaomi, OPPO, E///, Intel, LG)
  Option 2: Existing R15 requirements can be used as the baseline for CBM UE (Nokia).
  Option 3: Need further discussion (LG, Apple, NEC)
Issue 1-6-7: Beam management requirement
FFS:
  Option 1: The existing BFD/CBD requirements in Rel-16 can be applied for CBM type UE (Huawei, MTK, QC, Xiaomi, OPPO, E///, NEC, Nokia)
  Option 2: Need further discussion (LG, Intel)

## Slide 15: Topic # 2-1 RRM Requirements in inter-band UL CA
Issue 2-1-1: interruption requirements due to UL carrier RRC reconfiguration
FFS:
  Option 1: The existing interruption and delay requirements for UL carrier RRC reconfiguration can be applied when new inter-band UL CA configurations are introduced (Huawei, LG, QC, OPPO, E///)
  Option 2: More discussion is needed. (MTK, Apple, Intel)
  Option 3: RRM discussion should be hold until we have conclusion of FR2 inter-band UL CA in RF session. (Nokia, Apple)
Issue 2-1-2: DL interruption at UE switching between two uplink carriers
FFS:
  Option 1: The existing interruption requirements for UE switching between two uplink carriers are not applicable for FR2 inter-band UL CA (Huawei, MTK, LG, QC, E///, Intel)
  Option 2: More discussion is needed. (OPPO, Apple)
  Option 3: RRM discussion should be hold until we have conclusion of FR2 inter-band UL CA in RF session. (Nokia)

## Slide 16: Topic # 2-1 RRM Requirements in inter-band UL CA
Issue 2-1-3: DL interruption at NR SRS carrier based switching
FFS:
  Option 1: RAN4 investigates the interruption requirements for NR SRS carrier based switching applicable for inter-band SRS carrier switching in FR2. (Huawei, MTK, LG, QC, OPPO, E///, Intel)
  Option 2: More discussion is needed. (Apple)
  Option 3: RRM discussion should be hold until we have conclusion of FR2 inter-band UL CA in RF session. (Nokia)