## Slide 1: WF on R17 NR MG enhancements - Multiple concurrent and independent MG patterns
Mediatek Inc.
3GPP TSG-RAN WG4 #98-e Meeting
Electronic Meeting, 25th Jan. - 5th Feb. 2021
R4-2104096

## Slide 2: Work Plan
Rapporteurs are encouraged to reflect extended Rel-17 timelines in the WID in the next plenary. The work plan can be updated afterwards.
Before RAN4#100b (Q4’21), RAN4 focuses on the functionality and principles needed to support parallel MG patterns without considering pre-configured gap and NCSG.

## Slide 3: Definition(1)
Concurrent MG definition
  Concurrent MGs are multiple MGs that are configured for measurements during a common period of time
    Exact definition of common period of time is FFS
    UE behavior for non-overlapping, partially or fully overlapped cases is irrelevant to the definition and will be discussed separately.
    Note 1: current definition does not address pre-configured MG patterns and NCSG. FFS how to address pre-configured MG patterns and NCSG.
Concurrent MG patterns
  MG patterns are selected from Rel-16 gap patterns #0 to #25.

## Slide 4: Definition(2)
FFS definition of independent MG
  Option 1: (configuration perspective) gaps are considered as independent gaps if at least one of the configurations in MGL, MGRP, time offset is different.
  Option 2: (UE behavior perspective) gaps are considered as independent gaps if they can operate simultaneously without impacting the measurement performance requirements.
  Other option is not precluded
FFS whether to merge the definition of independent gap and concurrent gap.

## Slide 5: Applicability
The measurement purposes of concurrent gaps include:
  Different SMTC configurations
  Different RSs, e.g., SSB, CSI-RS, PRS, RSSI
  Different RATs
  FFS whether to extend to NCSG or pre-configured MG in the 2nd phase of the WI
  Other purposes not precluded
RAN4 to ensure both UE and NW have the same understanding on the usage of each measurement gap.
RAN4 shall further discuss on whether to define the framework of configuring gaps dedicated to specific purpose(s).

## Slide 6: Relation to per-UE gap and per-FR gap
RAN4 shall further discuss on the relation to per-UE gap and per-FR gap
  Option 1: All concurrent MGs are of the same type (per UE MG or per FR MG).
  Option 2: The parallel MG patterns can be any of
    all per-UE,
    all per-FR (for the same FR), or
    a combination of per-UE and per-FR MG patterns, with at least one per-UE and at least one per-FR
  Option 3:
    For a Per UE gap capable UE, multiple concurrent and independent MGPs applies per UE.
    For a Per FR gap capable UE, multiple concurrent and independent MGPs applies per FR
  Other option is not precluded
RAN4 shall further discuss on the max number of concurrent gap for per-UE gap FR1-gap and FR2-gap.
RAN4 shall further discuss whether a per FR gap and concurrent gap capable UE shall support multiple concurrent gaps on at least one FR.

## Slide 7: Overlapping
  RAN4 to work on at least non-overlapping concurrent gap as a start point.
  FFS whether to work on partially and fully-overlapped cases.

## Slide 8: Overhead
  Overhead for configuring multiple concurrent MG patterns.
    Option 1: RAN4 to specify a cap on aggregate fractional interruption time as applicability condition
    Option 2: Depends on NW configuration
    Other option is not precluded

## Slide 9: Measurement Requirement
  Measurement capability
    Keep Rel-16 UE measurement capability of number of layers to be monitored by gap(Section 9.1.3 of TS38.133) for UE configured with concurrent gaps.
  CSSF
    RAN4 to discuss how to define CSSF for concurrent gaps.
  Other requirements
    FFS: RAN4 to reuse the following existing MG related requirements for concurrent gaps: MG reference timing, effective MGRP, MG interruption and UE UL behaviour after MG.
    Other requirements can be further discussed in future meetings

## Slide 10: Others
No new gap pattern will be introduced in the scope of concurrent gaps objective in this WI.
Network configuration
    RAN4 to discuss whether to trigger LS to get RAN2 feedback for network configuration under DC mode.
    Do not introduce the concurrent gap in LTE SA mode.