## Slide 1: WF on the introduction of band n85
Ericsson
R4-210xxxx
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, 25 Jan - 5 Feb., 2021

## Slide 2: Band n85 - System parameters agreement
Band definition
Supported channel BWs
Channel arrangement
NR operating band | Uplink (UL) operating band BS receive / UE transmit FUL,low – FUL,high | Downlink (DL) operating band BS transmit / UE receive FDL,low – FDL,high | Duplex mode
n85 | 698 MHz – 716 MHz | 728 MHz – 746 MHz | FDD
NR band / SCS / BS channel bandwidth |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 70 MHz | 80 MHz | 90 MHz | 100 MHz
 | 15 | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 
n85 | 30 |  | Yes |  |  |  |  |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  |  |  | 
NR operating band | ΔFRaster (kHz) | Uplink Range of NREF (First – <Step size> – Last) | Downlink Range of NREF (First – <Step size> – Last)
n85 | 100 | 139600 – <20> – 143200 | 145600 – <20> – 149200
NR operating band | SS Block SCS | SS Block pattern1 | Range of GSCN (First – <Step size> – Last)
n85 | 15 kHz | Case A | 1826 – <1> – 1858

## Slide 3: Band n85 – BS Tx requirements agreement
OBUE
  n85 shall be added to the list of bands mentioned for Wide Area cat A and cat B option 1 limits for bands below 1GHz, in clauses 6.6.4.2.1 and 6.6.4.2.2
Spurious (coexistence)
  Spurious: Band n85 shall be added to the coexistence spurious emissions limits, table 6.6.5.2.3-1.
System type for NR to co-exist with | Frequency range for co-existence requirement | Basic limits | Measurement bandwidth | Note
UTRA FDD Band XII or | 729 – 746 MHz | -52 dBm | 1 MHz | This requirement does not apply to BS operating in band n12 or n85.
E-UTRA Band 12 or NR Band n12 | 699 – 716 MHz | -49 dBm | 1 MHz | This requirement does not apply to BS operating in band n12 or n85, since it is already covered by the requirement in clause 6.6.5.2.2. For NR BS operating in n29, it applies 1 MHz below the Band n29 downlink operating band (Note 5).
E-UTRA Band 29 or NR Band n29 | 717 – 728 MHz | -52 dBm | 1 MHz | This requirement does not apply to BS operating in Band n29 or n85.
E-UTRA Band 85 or NR band n85 | 728 - 746 MHz | -52 dBm | 1 MHz | This requirement does not apply to E-UTRA BS operating in band 12, 29 or 85.
 | 698 - 716 MHz | -49 dBm | 1 MHz | This requirement does not apply to E-UTRA BS operating in band n85, since it is already covered by the requirement in clause 6.6.4.2. For E‑UTRA BS operating in Band n29, it applies 1 MHz below the Band n29 downlink operating band.

## Slide 4: Band n85 – BS Tx requirements agreement
Spurious (co-location)
  Band n85 limits shall also be added to the colocation spurious emissions limits, table 6.6.5.2.4-1:
Type of co-located BS | Frequency range for | Basic limits |  |  | Measurement | Note
 | co-location requirement | WA BS | MR BS | LA BS | bandwidth | 
E-UTRA Band 85 or NR Band n85 | 699 – 716 MHz | -96 dBm | -91 dBm | -88 dBm | 100 kHz | 

## Slide 5: Band n85 – BS Rx requirements agreement
No impact on Rx requirements.

## Slide 6: Band n85 – UE Tx requirements agreement
Rx-Tx separation:
MOP: 23dBm shall be added to table 6.2.2-1 for n85
A-MPR:
  NS_06 information in table 6.2.3.1-1 shall be udpated:
Mapping of NS label table 6.2.31-1A:
NR operating band | TX – RX carrier centre frequency separation
n85 | 30 MHz
Network signalling label | Requirements (clause) | NR Band | Channel bandwidth (MHz) | Resources blocks (NRB) | A-MPR (dB)
NS_06 | 6.5.2.3.4 | n12 | 5, 10, 15 |  | N/A
 |  | n14, n85 | 5,10 |  | 
NR band | Value of additionalSpectrumEmission |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
n85 | NS_01 | NS_06 |  |  |  |  |  | 

## Slide 7: Band n85 – UE Tx requirements agreement
Spurious coexistence
  Band n85 shall be added to table 6.5.3.2-1:
NR Band | Spurious emission for UE co-existence |  |  |  |  |  | 
 | Protected band | Frequency range (MHz) |  |  | Maximum Level (dBm) | MBW (MHz) | NOTE
n85 | E-UTRA Band 2, 5, 13, 14, 17, 24, 25, 26, 27, 30, 41, 53, 71, 74, | FDL_low | - | FDL_high | -50 | 1 | 
 | E-UTRA Band 4, 10, 48, 51, 66, 70 NR Band n77, n78 | FDL_low | - | FDL_high | -50 | 1 | 2
 | E-UTRA Band 12, 85 | FDL_low | - | FDL_high | -50 | 1 | 15

## Slide 8: Band n85 – UE Rx requirements agreement
REFSENS
n85 shall also be added in table 7.3.2-4, with NS_06.
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 70 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n85 | 15 | -97.0 | -93.8 |  |  |  |  |  |  |  |  |  |  |  | FDD
 | 30 |  | -94.1 |  |  |  |  |  |  |  |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 70 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n85 | 15 | 20 | 20 |  |  |  |  |  |  |  |  |  |  |  | FDD
 | 30 |  | 10 |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 9: Band n85 – UE Rx requirements agreement
In-band blocking:
  n85 shall be added in table 7.6.2-2.
Out of band blocking:
  n85 shall be added in table 7.6.3-2.
Narrow band blocking:
  n85 shall be added in table 7.6.4-1.