## Slide 1: WF on remaining BS and UE parameters for 6.425-7.125 and 10.0-10.5 GHz
Ericsson
R4-2103103
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, 25 Jan - 5 Feb., 2021

## Slide 2: Minimum channel BW / OBUE for 10.0-10.5GHz
OPTION 1 OPTION 2
OBUE for cat B
OBUE for cat A
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | /100kHz
50 MHz  f < min(100 MHz, fmax) | -14 dBm/100kHz
100 MHz  f  fmax | -15 dBm/1MHz
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | 
50 MHz  f < min(100 MHz, fmax) | -14 dBm/100kHz
100 MHz  f  fmax | -15 dBm/1MHz
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | /100kHz
50 MHz  f < min(100 MHz, fmax) | -14dBm/100kHz
100 MHz  f  fmax | -13 dBm/1MHz
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | 
50 MHz  f < min(100 MHz, fmax) | -14dBm/100kHz
100 MHz  f  fmax | -13 dBm/1MHz
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | /100kHz
50 MHz  f < min(100 MHz, fmax) | -13 dBm/100kHz
100 MHz  f  fmax | -15 dBm/1MHz
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | 
50 MHz  f < min(100 MHz, fmax) | -13 dBm/100kHz
100 MHz  f  fmax | -15 dBm/1MHz
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | /100kHz
50 MHz  f < min(100 MHz, fmax) | -13dBm/100kHz
100 MHz  f  fmax | -13 dBm/1MHz
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | 
50 MHz  f < min(100 MHz, fmax) | -13dBm/100kHz
100 MHz  f  fmax | -13 dBm/1MHz

## Slide 3: Out of band blocking – 6.425-7.125GHz
3 options:
  Option 1:
    (TS 38.104)
  Option 2:
  Option 3:
    (n96)
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
(FUL_low - 500) to (FUL_low -ΔfOOB) (FUL_high +ΔfOOB) to (FUL_high +500) | -35 dBm CW
1 to (FUL_low -500) (FUL_high +500) to 12750 | -15 dBm CW
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
1 to (FUL_low -200) (FUL_high +200) to 12750 | -15 dBm CW
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
1 to (FUL_low -ΔfOOB) (FUL_high +ΔfOOB) to 12750 | -15 dBm CW

## Slide 4: Out of band blocking –10.0-10.5GHz
2 options:
  Option 1:
    (TS 38.104)
  Option 2:
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
1 to (FUL_low -200) (FUL_high +200) to 12750 | -15 dBm CW
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
1 to (FUL_low -ΔfOOB) (FUL_high +ΔfOOB) to 12750 | -15 dBm CW

## Slide 5: UE SEM
Agreement (to take into account new UE ACLR):
  Relax by 3 dB at the FOOB edge ± 0-1 and ± 1-5 (blue)
Should that relaxation be extended to the all OOB frequency range (yellow), excluding the frequency ranges with emission of -13dBm/1MHz?
ΔfOOB(MHz) | 20 MHz | 25 MHz | … | 50 MHz | … | MBW
± 0-1 | -10 | -10 | -10 |  |  | 1% CBW
± 0-1 |  |  |  | -21 | -21 | 30kHz
± 1-5 | -7 | -7 | -7 | -7 | … | 1MHz
± 5-6 | -13 | -13 | -13 | -13 | -13 | 
… |  |  |  |  |  | 
± 15-20 |  |  |  |  |  | 
± 20-25 | [-25 or -22] |  |  |  |  | 
… |  | [-25 or -22] |  |  |  | 
± 45-50 |  |  | ... |  |  | 
± 50-55 |  |  | ... | [-25 or -22] |  | 
 |  |  |  |  | ... | 
… |  |  | ... | … | ... | 

## Slide 6: BS ACS requirement (if time allows)
Agreed values:
  6.425-7.125GHz: 42dB
  10.0-10.5GHz: 40dB
To be agreed:
  Interferer type.
  Interferer power level.

## Slide 7: Agreements are captured in following slides

## Slide 8: Minimum channel BW / OBUE for 6.425-7.125 GHz
It does not mean that 50MHz will be the min. CBW when RAN4 specifies the CBW and emission requirements
Frequency offset of measurement filter ‑3dB point, f
0 MHz  f < 50MHz
50MHz  f < min(100MHz, fmax)
100MHz  f  fmax

## Slide 9: ΔfOBUE / ΔfOOB
For 10.0-10.5GHz:
For 6.425-7.125GHz - Option 2 is provisionally agreed pending checking by the end of this meeting.
Option 1 |  | Option 2 | 
ΔfOBUE | ΔfOOB | ΔfOBUE | ΔfOOB
50MHz | 70MHz | 100MHz | 100MHz
ΔfOBUE | ΔfOOB
100MHz | 100MHz

## Slide 10: BS antenna type for indoor
BS antenna type for indoor, 2 options:
  Option 1: AAS BS only
  Option 2: AAS BS and BS with omni antenna.
Agreement:
  ITU-R LS Reply: provide parameters for AAS BS only
  Capture in the TR that it’s not precluded to have BS with omni antenna for indoor.