## Slide 1: WF on FR2 UEs that support inter-band UL CA
MediaTek Inc.
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25 January – 5 February, 2021
Agenda Item: 11.3.1, 11.3.2, 11.3.3
R4-2103113

## Slide 2: Background
Current FR2 inter-band DL CA & UL CA status overview for reference. This WF focus on inter-band UL CA.
DL CA | Different Frequency Group (ex: 28+39) | Same Frequency Group (ex: 28+28)
IBM | requirement discussion stage | feasibility study stage
CBM | feasibility study stage | requirement discussion stage
UL CA | Different Frequency Group (ex: 28+39) | Same Frequency Group (ex: 28+28)
IBM | requirement discussion stage | feasibility study stage
CBM | feasibility study stage | feasibility study stage

## Slide 3: Work flow and WID objective
About “Feasibility stage UL CA work flow”
  Agreement: FR2 inter-band UL CA feasibility studies are put on hold until FR2 inter-band DL CA feasibility studies have progressed.

## Slide 4: Max EIRP & Max TRP of CA_n257A-n259A based on IBM
Worldwide regulator requirement study are encouraged
Focus on CA_n257A-n259A based on IBM discussion as first step, that is requested and non-overlapping bands type
Max EIRP
  Option 1: Specify max EIRP as per band
    PC1: max EIRP of each band set to 55 dBm
    PC3/4: max EIRP of each band set to 43 dBm
  Option 2: Specify max EIRP as per UE
    FFS on how “per UE” concept work, and the exact corresponding requirements
Max TRP (subject to revisit pending the final agreement on Max EIRP)
  PC1: Specify max TRP as per band, with max TRP of each band set to 35 dBm
  PC3/4: Specify max TRP as per band, with max TRP of each band set to 23 dBm

## Slide 5: Min Peak EIRP of CA_n257A-n259A based on IBM
Min Peak EIRP
  Option 1: Specify min peak EIRP as per band
    Option 1a: Same requirement as single-CC
      i.e. n257=22.4 dBm, n259=18.7 dBm
    Option 1b: FFS relaxed requirement compared to single-CC
      i.e. n257=22.4-FFS dBm, n259=18.7-FFS dBm
    Option 1c: 3dB relaxed requirement compared to single-CC
      i.e. n257=19.4 dBm, n259=15.7 dBm
  Option 2: Specify min peak EIRP as per UE
    FFS on how “per UE” concept work, and the exact corresponding requirements
  Option 3: Others
    Others are not precluded