## Slide 1: WF on FR2 enhancement part 3: UL gap
Apple, …
3GPP TSG-RAN WG4#98-e Meeting R4-2103114
Electronic Meeting, 25th Jan – 5th Feb., 2021 Document for: Approval
Agenda item: 11.3.4

## Slide 2: Way forward - UL gap related performance gain
On UL gap related performance gain:
  UL gap-based UE power/UL coverage gain with proximity sensing has been shown.
    Metric of the performance gain include P-MPR/power control accuracy/UL power.
    Observations:
      In R4-2100218, it has been shown that
        higher UL Tx power will provide better coverage of around 3dB and/or higher UL throughput, particularly for UE with high peak EIRP and operating at high duty cycle at cell edge.
        SLS result shows that 5-precentile UL throughput is reduced by 52% at P-MPR of 6dB.
        Up to 33% coverage reduction with P-MPR of 6dB, using UMa NLOS path loss model defined in 38.901.
    Inputs from interested companies are welcome.
  It is FFS if PA and transceiver calibration can be used as metric/use cases for performance gain.
    Observations:
      In R4-2100217, it has been shown that for transceiver calibration, end to end simulation shows that
        about 0.5dB higher Tx power is achieved when 3dB IQ imbalance and LO leakage EVM loss is compensated.
        About 3.5dB higher Tx power is achieved when 6dB IQ imbalance and LO leakage EVM loss is compensated.
        The gain depends on different UE implementations in terms of uplink performance to different EVM targets, RF exposure constraints and other implementation considerations.
      Concerns from companies if PA and transceiver calibration can be used as metric/use cases to justify the performance gain
Agreement:
  UL gap-based UE power/UL coverage gain with proximity sensing has been shown with respect to R16 amount of P-MPR for UEs without the use of such gaps. However, how to show the gain in the test is FFS
  For PA and transceiver calibration use cases, the metrics for performance gain can be UE TX power increase and DL throughput increase.
    FFS: additional metrics for consideration can be IBE reduction.

## Slide 3: Way Forward - Network impact analysis
To facilitate network impact analysis, the follow evaluation assumptions are defined to facilitate the related study,
  Gap configuration:
    A range of 0.25% - 5% UL gap overhead is considered for evaluation purpose. The UL gap overhead is defined as the duration UL gap over its periodicity.
    The values of x and y are to be decided in RAN4#98e
  Tx power gain in dB
    A range of 2-6dB (in case of 26dBm peak EIRP and 20% duty cycle without the presence of target in proximity) Tx power gain is considered for evaluation purpose.
    The values of m and n are to be decided in RAN4#98e
  Scheduling constraint modeling
    Company inputs on how to model scheduling constraint in network analysis are welcome
Interested companies are encouraged to provide NW impact related analysis in RAN4#99e from at least the follow two aspects
  System impact due to UL gap overhead
  NW impact due to scheduling restriction
Agreement:
  Companies are encouraged to provide network impact analysis with the above evaluation assumptions

## Slide 4: Way Forward – Requirement and testability associated with UL gap
Agreement: Requirements associated with UL gap:
  All the UE RF requirements should be applicable if any type of gaps is defined and allowed for the UE.
  New requirements if identified can be discussed in phase II
    UE TX power and DL throughput

## Slide 5: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2100144 | FR2 UL gaps for self-calibration and monitoring | Nokia, Nokia Shanghai Bell
R4-2100217 | UL gaps for tranceiver calibration | Apple
R4-2100218 | UL gaps for Tx power management | Apple
R4-2100599 | UL calibration gap continuation | Qualcomm Incorporated
R4-2100825 | Performance evaluation for calibration | CMCC
R4-2101129 | Discussion on the UL Gap | LG Electronics Finland
R4-2101467 | Discussion on UL gap for self-calibration and monitoring | vivo
R4-2102623 | on gaps for self-calibration and monitoring | Huawei, HiSilicon
R4-2102680 | Power calibration gap UE improvement requirements | Ericsson, Sony

## Slide 6: Reference
[1] R4-2102988, “Email discussion summary for [98e][140] NR_RF_FR2_req_enh2_Part_3”, Apple
[2] RAN4#98_[140]_GTW discussion on UL gap in FR2_GTW.pptx