## Slide 1: Way Forward on LTE CA MPR and CA_NS_04 A-MPR for UL 256 QAM PC2
Huawei, HiSilicon, T-mobile USA, Qualcomm Inc
R4-2103131
3GPP TSG-RAN WG4 #98-e
Jan 25th ‒ Feb 5th, 2020
Electronic Meeting

## Slide 2: Background
The MPR for PC2 CA 256QAM and the A-MPR for PC2 CA_NS_04 256QAM are still FFS in the current spec.
There’re simulation results in [1] and A-MPR values have been proposed in [1][2].
There have been discussions [3] on whether the A-MPR values should include the EVM effect or not.
References:
[1] R4-2102437 A-MPR for CA_NS_04 256QAM, Huawei, HiSilicon
[2] R4-2016426 LTE CA_NS_04 PC2 256QAM AMPR, QualComm
[3] R4-2102953 Round 1 Email discussion summary for [98e][105]LTE_Maintenance

## Slide 3: Way Forward
The A-MPR values for 256QAM (and 64QAM) should not include the EVM effect. Instead, the EVM effect is included in the MPR values.
The following A-MPR values were proposed for 256 QAM PC2 CA_NS_04 based on the simulation results in [1], other companies are encouraged to provide non-EVM based A-MPR simulation/measurement results
As stated in the spec, UL CA EVM requirement applies only when one CC is allocated. With this clarification, companies are encouraged to provide MPR simulation/measurement results for 256 QAM PC2 CA
Aim to agree the final A-MPR and MPR values in the next meeting (RAN4#98bis-e)
A-MPR for lower region of Rbstart | 5.5 dB
A-MPR for middle region of Rbstart | 5 dB
A-MPR for upper region of RBstart | 4.5 dB