## Slide 1: WF on requirements for Type 2 UEs supporting inter-band MRDC with overlapping DL
Ericsson
3GPP TSG-RAN WG4 Meeting #98-e
Electronic meeting, 25 January – 5 February 2021
R4-2103166

## Slide 2: Background
For inter-band EN-DC combinations with overlapping DL, e.g. DC_42-n77, the requirements in the current 38.101-3 are according to those for intra-band EN-DC
The 38.306 Rel-16 contains a new capability for indication of support of inter-band EN-DC requirements for FDD-FDD and TDD-TDD combinations with overlapping DL
  e.g. for support DC_42-n77 with non-collocation and inter-band EN-DC performance
How to facilitate implementation of UEs supporting the said capability (Type 2)?
Relevant RF requirements to ensure performance of Type 2 UEs in a non-collocated scenario?

## Slide 3: WF for faciliating Type 2 implementation
RAN4 to consider
Waiving requirements on the applicability of 2Rx/4Rx requirements for UE implementations with separate RX chains
  e.g. for TDD-TDD: for UEs indicating interBandMRDC-WithOverlapDL-Bands-r16: the requirements for each cell group shall be according to the SA requirements defined for two RX antennas for all DL bands above [2490] MHz (i.e. the requirements for four Rx ports do not apply when the UE is configured with EN-DC)
  for FDD-FDD a similar provisions could be considered (FFS)
Other provisions not precluded

## Slide 4: WF on RF requirements for Type 2 relevant for a non-collocated scenario
Scenario for which the current intra-band EN-DC requirements do not ensure RF performance
RAN4 to consider
requirements to ensure performance with larger received power differences (than 6 dB for Type 1) between cell groups
e.g. a provision that the minimum requirements apply for an input power of the anchor signal up to [30 dB] greater than the input power of the wanted NR except for the minimum requirement on the maximum input power (consistent with ACS requirements)

## Slide 5: WF on release
RAN4 to specify RF requirements for Type 2 UEs in the Rel-16 version of 38.101-3 in accordance with the 38.306

## Slide 6: References
R4-2101725, ”Requirements [for] Type 2 UEs supporting inter-band MRDC with overlapping DL”, Ericsson