## Slide 1: WF on increasing maximum output power for UE equipped with two PAs
Qualcomm Incorporated, [Nokia], Verizon, ZTE, Apple, [Skyworks], [vivo], [Ericsson]
R4-2103174
3GPP TSG-RAN WG4 #98-e
Jan 25th ‒ Feb 5th, 2020
Electronic Meeting

## Slide 2: Background
Increasing UE maximum output power has been seen as beneficial
  Proliferation of PC2 bands(even for FDD bands), band combinations, DC configurations
  Introduction of PC 1.5 in Band n41 and ongoing work item for n77 and n78
UE’s with two PA’s for the same band are more common now
  UL MIMO, TxD
  Configurations such as 23+23, 23+26, 26+23, 26+26 have been discussed
For a UE with two Tx paths capable of delivering 23 dBm (antenna port referred) and 26 dBm, the UE is potentially able to reach a maximum output power of 27.8 dBm. Generalizing, a UE with X dBm and Y dBm Tx paths can potentially deliver 10log(10X/10+ 10Y/10) dBm total maximum output power.
Two options have been discussed (R4-2102414)
  Option 1: Remove PPowerClass constraint in the maximum configured output power
  Option 2: Define a new power class

## Slide 3: Way Forward
Compare the two options for the next meeting
  Study the impact to regulations for each option. If possible, identify specific regulatory requirements that are impacted.
  Study the impact to 3GPP specifications of each option
    Identify which specifications are impacted
    Identify the impact to other ancillary requirements such as CA, DC
  Study the need for signaling
  Study the impact to SAR
  Study the impact on RAN4 requirements, such as MPR, emissions, coexistence
RAN4 should strive to address operator demand for HPUE implementations, and in the event that no consensus is achieved on related to the options above, the ”new power class” method is adopted
Alternatives to the two options are not precluded