## Slide 1: WF on adding 90 and 100MHz channel BW for UE in band n40
Huawei, HiSilicon, CMCC[…]
3GPP TSG-RAN WG4 Meeting #98-e R4-2103181 Electronic Meeting, Jan. 25-Feb. 5, 2021

## Slide 2: Status summary for 1st round discussion[3]
Candidate options: There are still very strong concerns on introducing 90 and 100MHz channel BW for UE in band n40, companies asking for more time to further analyze the analysis given by Huawei.
Recommendations for 2nd round: Opponents are encouraged to review the given inputs from Huawei and if needed further detail any remaining concern/questions. In the meantime, Huawei might want to provide additional analysis and proposals to address the raised concerns.
A Way Forward would be helpful to capture the next steps.

## Slide 3: Discussion
The filter rejection assumption and spurious emission requirements for co-existence with band n41 will be discussed in thread [113].

## Slide 4: Discussion
Co-existence with ISM band
  As discussed in R4-2101521, no new issue is introduced for the case 100 MHz CBW. The co-existence are guaranteed by implementation measures in frequency domain, time domain, power domain or their combinations.
    E.g. due to band 40 and 2.4GHz ISM band are adjacent, TDMed approach has to be used for all channel bandwidths.
      the whole n40 band will suffer large blocking from WIFI or BT TX in the frequency range 2400~2418.
      the WIFI or BT will suffer blocking from n40 max TX in upper edge frequency 2380~2400

## Slide 5: Discussion
Spurious emissions for UE co-existence with the bands 1, 38, 65 and 69 due to IMD5
  In general the spurious emission is defined as -30 dBm/MHz without filter rejection assumed. With larger than 20 dB filter rejection, -50 dBm/MHz co-existence can be met.
  We have checked several commercial band 40 filters, 30~35 dB rejection is achievable.
min Attenuation |  | Filter 1 |  |  | Filter 2 |  | 
 |  | min | type | max | min | type | max
2010 | 2170 | 30 | 33 |  | 35 | 40 | 
2481 | 2690 | 40 | 46 |  | 44 | 47 | 

## Slide 6: WF
  The filter rejection assumption and spurious emission requirements for co-existence with band n41 will follow the decision made in thread [113].
  To further investigate
    delta MPR for 90 and 100 MHz
    The need of AMPR for n41 coexistence
  For co-existence with ISM band, companies are encouraged to further study whether there is new coexistence issue introduced for 90 and 100 MHz channel BWs.
  For UE co-existence with the bands 1, 38, 65 and 69 due to IMD5, the -50 dBm/MHz spurious emissions can be met.
  To further investigate the impact on increasing n40 UL CBW as an aggressor to close band proximity MSD

## Slide 7: Reference
[1] R4-2101521, Adding 90 and 100MHz bandwidth for band n40, Huawei, HiSilicon
[2] R4-2102929, UE-UE Coexistence for Asynchronous n40 n41, Networks Skyworks Solutions Inc.
[3] R4-2102968, Email discussion summary for [98e][120] NR_bands_R17_BWs, Moderator (Ericsson)