## Slide 1: Way forward on the introduction of 25, 30 and 40MHz in band n2
AT&T
­­­3GPP TSG-RAN WG4 Meeting # 98-e R4-2103184
Electronic Meeting, 25th Jan. – 5th Feb., 2021

## Slide 2: Background
Huawei and Ericsson provided contributions with A-MPR and REFSENS proposals for 25, 30, and 40 MHz channel bandwidths for n2
Agreements can be made for A-MPR for n2
Agreements can be made for REFSENS for n2 25MHz
Further analysis and discussion required for REFSENS for n2 30 and 40MHz

## Slide 3: WF on A-MPR
Issue 4-1: A-MPR for 25, 30 and 40MHz channel BW.
  Option 1: No update needed (Huawei, Ericsson)
Observations:
  NS_03 is considered to be CBW agnostic
  Companies supported Option 1 with no dissenting views
WF
  No update for A-MPR (NS_03) needed when introducing the new channel BWs in n2

## Slide 4: Way Forward on REFSENS
Issue 4-2: UE REFSENS
  Option 1: Reuse n25 REFSENS limits and corresponding RB allocation (Huawei)
  Option 2: Specify following REFSENS limits and corresponding RB allocation (Ericsson)
Observations:
  Both options utilize identical UL configs for 25 MHz
  MSD=0 for 25 MHz
  REFSENS for 25 MHz derived by scaling existing values
WF
  Agree to UL config and REFSENS values above for n2 25MHz
  MSD for n2 30 and 40MHz to be finalized in next meeting
  Companies encouraged to bring UL config proposal and analysis for REFSENS at next meeting for 30 and 40MHz
Operating Band | SCS kHz | 25 MHz (dBm)
n2 | 15 | 501
 | 30 | 241
 | 60 | 101
Operating Band | SCS kHz | 25 MHz (dBm)
n2 | 15 | -90.8
 | 30 | -91.0
 | 60 | -91.1

## Slide 5: References
R4-2101815, “Discussion on the larger channel bandwidth for band n2”, Huawei, 3GPP TSG-RAN WG4 #98-e
R4-2102166, “Additional channel bandwidths in bands n2, n5 and n48 – A-MPR impacts”, Ericsson, 3GPP TSG-RAN WG4 Meeting # 98-e
R4-2102167, “Additional channel bandwidths in bands n2, n5 and n48 – REFSENS”, Ericsson, 3GPP TSG-RAN WG4 #98-e