## Slide 1: WF on spectrum utilization for 35 MHz and 45 MHz
Huawei, HiSilicon, […]
3GPP TSG-RAN WG4 Meeting #98-e R4-2103186 Electronic Meeting, Jan. 25-Feb. 5, 2021

## Slide 2: Background on channel raster and PRB grid alignment
Status summary for 1st round discussion
  Based on 1st round discussion, option 1 have more supporting companies. And companies are still checking whether there are NBC issues to legacy UE for option 2~4.
    Option 1: adjust the number of PRBs for 45 MHz， e.g. NRB=242.
      Ericsson, Qualcomm, Huawei, MediaTek
    Option 2: configure NRB=215 for 40 MHz CBW for the legacy UE
      ZTE
    Option 3: Apply a 5 kHz channel raster for FR1 bands with 100 KHz channel raster
      Nokia
    Option 4: two sub-options depend on whether legacy UEs are scheduled
      Apple
  Recommendation for 2nd round: further check whether option 1 is acceptable and capture the potential agreements in the WF1

## Slide 3: Discussion
In R4-1811905, the dedicated channel bandwidth has to be from the set of channel bandwidths defined in 38.101-1 or 38.101-2. Hence option 2 and 4 may cause confusion. And option 3 introduce a new 5 KHz channel raster which may cause NBC issue for legacy UEs. Hence Option 1 is preferred.
  For UEs to be able to operate in a regulatory compliant way, a UE channel bandwidth has to be explicitly configured such that UE is aware of which channel bandwidth it should operate in without ambiguity. Also, this channel bandwidth has to be from the set of channel bandwidths defined in 38.101-1 or 38.101-2 for the band in which the UE is operating.[R4-1811905]

## Slide 4: WF
  It is proposed to adopt option 1 and the spectrum utilization for 35MHz and 45MHz is defined as below.
SCS (kHz) | 35MHz | 45MHz
 | NRB | NRB
15 | 188 | 242
30 | 92 | 119
60 | 44 | 58