## Slide 1: WF on REFSENS for 35MHz and 45MHz
Qualcomm, Skyworks, […]
­­­3GPP TSG-RAN WG4 Meeting # 98-e R4-2103187
Electronic Meeting, 25 Jan – 5 Feb, 2021

## Slide 2: Background
Various companies brought contributions for REFSENS for 35MHz and 45MHz channel bandwidths
Agreement was made for n1 45MHz UL configuration and REFSENS
Agreement was made for n3 35MHz and 45MHz UL configuration
Agreement can be made for UL configuration for n8 and n71 20MHz UL for 35MHz REFSENS
Agreement can be made for UL configuration for n25 40MHz UL for 45MHz REFSENS
No agreements made for REFSENS on channel location for n8, n71, and n25 REFESNS

## Slide 3: Background: Comparison of REFSENS
UL configuration can be agreed as shown in table
REFSENS for n1 45MHz can be agreed
REFSENS (15 KHz SCS) |  |  |  |  |  |  |  |  |  |  |  |  | 
Company | n1 | n2 | n3 |  | n8 |  |  | n25 |  |  | n71 |  | 
 | 45 | 35 | 35 | 45 | 35 |  |  | 35 | 45 |  | 35 |  | 
 |  |  |  |  | worst | Mid | Best |  | worst | Best | worst | Mid | Best
Murata |  |  | -86 | -84.2 | -64 |  | -85.2 | -85.4 | -77.4 |  | -69.1 |  | -87.7
Mediatek |  |  |  |  | -67.6 |  | -87.8 |  |  |  | -67.6 |  | -88
Qualcomm |  |  | -85.2 | -80.2 | -69.9 | -78.5 | -84.8 | -81.7 | -76.4 |  | -69.9 | -82.7 | -84.9
Huawei | -90.1 |  | -86.1 | -82 | -71.5 |  |  |  |  |  | -71 |  | 
Apple |  |  |  |  |  | -76.7 |  |  |  |  |  | -77 | 
Skyworks | -90.1 | -87.1 | -87.5 | -85 | -70.6 |  | -85.1 | -86.1 | -81 | -84.4 | -71.6 |  | -85.5
Average | -90.1 |  | -86.2 | -82.9 | -68.7 | -77.6 | -86 | -84.4 | -78.3 |  | -69.8 | -79.9 | -87
UL Config (15 KHz SCS) |  |  |  |  |  |  |  | 
Company | n1 | n2 | n3 |  | n8 | n25 |  | n71
 | 45 | 35 | 35 | 45 | 35 | 35 | 45 | 35
Murata |  |  | 50 |  | 20 | 40 | 40 | 20
Mediatek |  |  |  |  | 20 |  |  | 20
Qualcomm |  |  | 50 |  | [20] | 45 | 40 | [20]
Huawei | 128 |  | 50 | 50 | 20 |  |  | 20
Apple |  |  |  |  | 20 |  |  | 20
Skyworks | 128 | 40 | 50 | 50 | 25 | 40 |  | 25
Agreement | 128 | 40 | 50 | 50 | 20 | 40 |  | 20

## Slide 4: WF
Agreement on UL configuration for all bands with 35MHz and 45MHz CBW as shown on last row in 2nd table on slide 3.
Agreement on n1 REFSENS
Further work to deduce n3 and 25 REFSENS.
  Simple average value of company contributions will not work
  35MHz REFSENS cannot be lower than the 30MHz REFSENS (ie. n25)
  45MHz REFSENS cannot be lower than the 40MHz REFSENS (ie. n3)
  Apply an MSD offset ([TBD] dB ) to deduce 35M, 45M REFENS using 30MHz and 40MHz baseline respectively to take into the effect of CIM5 overlap.
For n8, n71, and n25 where UL BW < DL BW. Choose 1 of 3 options for the next meeting while considering test time, complexity, and coverage
  Option 1: Worst case; UL BW closest to DL
  Option 2: Middle case; keep existing duplex offset between center of RX and TX channel BWs
  Option 3: Best case; UL BW furthest from DL

## Slide 5: References
R4-2100703, “REFSENS of n8 and n71 for 35MHz channel bandwidth”, Murata Manufacturing Co Ltd, 3GPP TSG-RAN WG4 #98-e,
R4-2100705, “REFSENS of n25 for 45MHz channel bandwidth”, Murata Manufacturing Co Ltd., 3GPP TSG-RAN WG4 Meeting # 98-e
R4-2101159, “REFSENS evaluation of n8 and n71 for 35MHz channel bandwidth ”, MediaTek Inc., 3GPP TSG-RAN WG4 #98-e
R4-2101177, “35MHz 45MHz AMPR, MPR, REFSENS for n8, n71, and n25.”, Qualcomm Incorporated, 3GPP TSG-RAN WG4 #98-e
R4-2101502, “UE REFSENS for 35 MHz and 45 MHz”, Huawei HiSilicon, 3GPP TSG-RAN WG4 #98-e
R4-2102592, “MSD considering asymmetric UL/DL for bands n8 and n71”, Apple Inc., 3GPP TSG-RAN WG4 #98-e
R4-2102927, “35MHz 45MHz REFSENS”, Skyworks Solutions Inc., 3GPP TSG-RAN WG4 #98-e