## Slide 1: WF on A-MPR for 35MHz and 45MHz
Apple, […]
3GPP TSG-RAN WG4 Meeting #98-e R4-2103188
Electronic meeting, 25 Jan – 5 Feb, 2021

## Slide 2: Background
WID NR_FR1_35MHz_45MHz_BW was updated in RP-202607 to include n1 and n2. Topics of interest:
  n1 with 45MHz CBW
  n2 with 35MHz CBW
  n25 with 35MHz and 45MHz CBW
A-MPR and filter assumptions need to be checked for the individual bands

## Slide 3: A-MPR for n1 with 45MHz CBW
Simulation assumptions:
  Power Class 3
  Calibration: 1dB MPR: DFT-s-OFDM QPSK 20MHz, 100RB
  Carrier Leakage: 28dBc
  Image: 28dBc
  CIM3: 60dBc
  Filter rejection at B3 Rx: 50dB
  Filter rejection at B34 Rx: 11dB
Sources on simulations assumptions: R4-2000108 (Qualcomm), R4-2000825 (Huawei), R4-2004692 (Apple)
A-MPR Proposal for n1 45MHz CBW: R4-2100516 (Apple)
WF: Use provided simulations assumptions for 45MHz and propose A-MPR next meeting

## Slide 4: A-MPR for n2 and n25
n2: highest CBW is increased from 20MHz to 35MHz
n25 45MHz: asymmetric UL/DL with maximum 40MHz UL
NS_03 is considered to be CBW agnostic
WF: Increased NS_03 A-MPR is not considered to be required