## Slide 1: Way forward on Deployment Scenario and UE RF Requirement for FR2 HST
Samsung
3GPP TSG-RAN WG4#98-e Meeting R4-2103240
Electronic Meeting, Jan. 25 - Feb. 5, 2021

## Slide 2: Way Forward – Transmission Schemes for FR2 HST
Transmission Scheme Clarification:
  Clarification for different transmission schemes:
    Joint Transmission (JT) for all channels (SSB, TRS, PDCCH/PDSCH) – Full SFN;
    Dynamic Point Selection (DPS) – based on Rel-15 beam management;
    Multi-DCI based Multi-TRP Transmission – based on Rel-16 eMIMO.
  For transmission scheme to be discussed in FR2 HST:
    FR2 HST transmission schemes which are not compatible with Rel-15/16 NR shall be precluded in FR2 HST WI discussion.
    For Joint transmission (JT) used for FR2 HST, only full SFN (i.e., Joint Transmission (JT) for all channels (SSB, TRS, PDCCH/PDSCH, etc.)) is considered in Rel-17 FR2 HST WI.
    Multi-DCI based multi-TRP transmission is precluded from Rel-17 FR2 HST.

## Slide 3: Way Forward – FR2 HST Deployment Scenario (1/3)
RAN4 primarily consider HST FR2 deployment with
  One train moving over one railway track in one direction;
  RRHs are located on one side of the track;
  FFS the impact from having two trains with two directions and other RRH location option on deployment aspects, if issues identified.
Agreements (achieved in GTW session):
  Replace scenario 4 with the new scenarios Ds = 700m and Dmin = 150m. For this new scenario, channel model is FFS.
  For scenario 2, change Ds from 650m to 700m
  No need to consider the grouping proposal
Scenario | Ds (meter) | Dmin (meter) | Prioritization | Note
A | 700 | 10 | Prioritised | Changed from Original Scenario-2
B | 700 | 150 | Prioritised | New Scenario (same as FR1 deployment)

## Slide 4: Way Forward – FR2 HST Deployment Scenario (2/3)
  If DPS is adopted as transmission scheme, SSB index to Beam Mapping:
  Option-1: Shared SSBs for beams from different panels, as following illustrative example:
  Option-2: RRHs under the same cell use the different sets of SSB indexes, e.g., RRH-1 uses SSB-0 to SSB-3, RRH-2 uses SSB-4 to SSB-7, etc.
  Option-3: SSB index to beam mapping can be left to implementation.
  Agreement (achieved in GTW session): Option 2 is agreed.
  Number of panels per CPE and Bi-directional Operation for Two Panels (if any):
  FFS if there is better term for CPE for Rel-17 FR2 HST.
  Number of panels per CPE:
    2 panels (both for TX and RX) for two opposite directions
    FFS CPE only has one panel pointing to upside and have analog beam directed to forward and backward by adjusting phase-shifter array.
  Bi-directional operation for two panels (if any):
    Follow Rel-15/16 principle of “only one panel to TX/RX at a time”.
    FFS signaling is needed.

## Slide 5: Way Forward – FR2 HST Deployment Scenario (3/3)
  Number of CPE devices per train/carriage:
  FFS the impact if more than 1 CPE devices per train, in terms of:
    System capacity;
    Inter-UE interference.
  FFS whether or not RAN4 requirement can be defined based on the baseline of 1 CPE devices per train.
  FR2 RRH Beamforming Modeling Revisit:
  RAN4 perform further evaluation based on the following antenna parameters:
  Antenna array configuration:
    Option-1: [Mg, Ng, M, N, P]=[1, 1, 4, 8, 2]
    Option-2: [Mg, Ng, M, N, P]=[1, 1, 8, 8, 2]
    Option-3: [Mg, Ng, M, N, P]=[1, 1, 8, 16, 2]
  Tunnel Deployment Scenario:
  RAN4 need to study tunnel deployment scenario:
    Different deployment parameters expected:
      Take [Ds = 300m and Dmin = 2m] as starting point.
    FFS channel model for tunnel deployment
    FFS other implementation issues.
    Requirement enhancement of tunnel scenario is studied only when both the legacy and the enhanced requirement from prioritized scenario doesn’t apply.
  Agreement (achieved in GTW session):
    To study tunnel scenario after the prioritized scenarios
Parameter | Urban macro 30 GHz
Am | 30
SLAv | 30
j3dB | 90
q3dB | 90
GE,max | 5.5
LE | 1.8
P | 2
dv | 0.5l
dh | 0.5l

## Slide 6: Way Forward – Uni-directional Deployment (1/2)
General:
  In uni-directional deployment, when UE is switching serving beam, source and target beams have very different propagation delays, and the change in timing may exceed a cyclic prefix.
    FFS on the impact of such timing change and resolution, if system impact is identified.
JT for all channels (full SFN) for Uni-directional Deployment
  If JT for all channels (full SFN) adopted for uni-directional RRH deployment, RAN4 only consider
    the setting with only one TCI state transmission.
If DPS adopted for uni-directional RRH deployment, RAN4 only consider
  The number of TCI states per RRH panel: 1, or 2
    FFS only 1 TCI state per RRH panel is enough or not.

## Slide 7: Way Forward – Uni-directional Deployment (2/2)
RAN4 further study the following uni-directional deployment scenario with priority:
  Uni-directional deployment with Ds = 300m and Dmin = 50m, and 1 or 2 analog beams can be FFS with low priority.
  NOTE1: For JT for all channels, only consider 1 beam per RRH panel. For DPS, 1 or 2 analog beams per RRH panel can be considered, if benefit is identified.
  NOTE2: RAN4 focus on 1 direction 1 train, but be aware of the fact that another panel to serve train towards the other direction is needed. If this opposite direction is completely symmetric, the 1 direction study can apply directly.
Parameter | Value
Ds and Dmin | Scenario-A: Ds = 700m and Dmin = 10m Scenario-B: Ds = 700m and Dmin = 150m
RRH height | 15 m
Number of RRH sites per BBU | 4
Number of RRH panels per RRH sites | 1 (i.e., uni-directional) NOTE2
Number of Analog Beams per RRH panel | 1 or 2 Note1
RRH panel orientation | Option-1: RRH panel boresight pointed to the railway at the distance of Ds (projection of the neighboring RRH on the railway) Other Options are not precluded
Analog beam orientation | Based on companies’ selection for better performance

## Slide 8: Way Forward – Bi-directional Deployment (1/2)
For bi-directional RRH deployment, FFS the necessity of joint transmission (JT) for all channels (SSB, TRS, PDCCH/PDSCH), by
  FFS the benefits of PDSCH combining for this case;
  CPE’s architecture and panel orientation’s impact needs to be considered.
For bi-directional RRH deployment, DPS transmission scheme shall be considered to reduce the multi-path delay spread, reduce ICI and achieve good coverage.
  FFS:
    the coverage performance by study the signal strength in the area around each RRH site.
    the number of beams (i.e., TCI states) per RRH penal.

## Slide 9: Way Forward – Bi-directional Deployment (2/2)
RAN4 further study the following bi-directional deployment:
Parameter | Value
Ds and Dmin | Scenario-A: Ds = 700m and Dmin = 10m Scenario-B: Ds = 700m and Dmin = 150m
RRH height | 15 m
Number of RRH sites per BBU | 4
Number of RRH panels per RRH sites | 2 (i.e., bi-directional)
Number of Analog Beams per RRH panel | 1, 2, 4
RRH panel orientation | Option-1: RRH panel boresight pointed to the railway in the middle point between 2 RRHs) Option-2: RRH panel boresight pointed to the railway at the distance of Ds (projection of the neighboring RRH on the railway) Other Options are not precluded
Analog beam orientation | Based on companies’ selection for better performance

## Slide 10: Way Forward – Channel Modeling
  Pathloss model used for link budget evaluation:
  RAN4 choose TS38.901 RMa LoS pathloss model to be used for link budget evaluation at least for Scenario-A:
    FFS pathloss model for tunnel deployment scenario.
    FFS channel model for Scenario-B.
  Channel modelling for performance requirements:
  For channel modelling for performance requirement evaluation:
    The single-tap can be assumed for a single TX-RX link at least for Scenario-A.
    FFS multi-tap models are needed for SFN and other scenarios.
    FFS channel model for Scenario-B.

## Slide 11: Way Forward – Maximum Supported Speed (1/3)
Numerology considered for maximum supported speed:
  For FR2 HST evaluations and possible performance requirements definition:
    Only consider 120kHz SCS as baseline assumption.
FFS the maximum supported speed from DL demodulation perspective:
  Reference signal(s) to be used for frequency offset tracking:
    Option-1: TRS (4 symbol interval)
    Option-2: DMRS (1+1+1)
    Option-3: TRS + PT-RS (1 and 2 symbol interval)
FFS the maximum supported speed from UL demodulation perspective:
  Reference signal(s) to be used for frequency offset tracking:
    Option-1: DM-RS (1+1+1) only
    Option-2: PT-RS (1 or 2 or 4) + DMRS
    Option-3: PT-RS (1 or 2 or 4)
FFS under bi- and uni-directional deployment.
FFS the possible higher supported speed for uni-directional deployment.
FFS Frequency error of +/-0.1ppm should be taken into consideration for both UL and DL.

## Slide 12: Way Forward – Maximum Supported Speed (2/3)
RAN4 shall check the maximum supportable speed from demodulation perspective and accordingly the possible enhancement:
  Candidate maximum speed values to be evaluated:
    260kmph
    350kmph
    Other options if identified.
PUSCH demodulation parameter:
Parameter |  |  | Value
Transform precoding |  |  | Disabled
Default TDD UL-DL pattern (Note 1) |  |  | 60 kHz and 120kHz SCS: 3D1S1U, S=10D:2G:2U
Antenna layout |  |  | 1T2R, ULA Low Correlation
HARQ | Maximum number of HARQ transmissions |  | 4
 | RV sequence |  | 0, 2, 3, 1
DM-RS | DM-RS configuration type |  | 1
 | DM-RS duration |  | single-symbol DM-RS
 | Additional DM-RS symbols |  | TBD
 | Number of DM-RS CDM group(s) without data |  | 2
 | Ratio of PUSCH EPRE to DM-RS EPRE |  | -3 dB
 | DM-RS port(s) |  | 0
 | DM-RS sequence generation |  | NID=0, nSCID =0
Time domain resource | PUSCH mapping type |  | B
 | Start symbol index |  | 0
 | Allocation length |  | 8 or 9
Frequency domain resource | RB assignment |  | Full applicable test bandwidth
 | Frequency hopping |  | Disabled
 | Bandwidth |  | 100 MHz
Code block group based PUSCH transmission |  |  | Disabled
PT-RS configuration |  | Frequency density (KPT-RS) | Disabled, or KPT-RS=2 if PT-RS is enabled
 |  | Time density (LPT-RS) | Disabled, or LPT-RS = 1 or 2 or 4 if PT-RS is enabled
MCS |  |  | MCS16
Propagation channel |  |  | Uni-directional: Derived based on agreed deployment scenario. Bi-directional: Single-Tap channel in TS38.101-4 B.3 but updated parameters

## Slide 13: Way Forward – Maximum Supported Speed (3/3)
PDSCH demodulation parameter:
Parameter |  | Unit | Value
CBW and SCS |  |  | 120kHz, 100MHz (66PRB)
Duplex mode |  |  | TDD
TDD pattern |  |  | 3D1S1U (FR2.120-1) S=10D:2G:2U
Active DL BWP index |  |  | 1
CSI-RS for tracking | First OFDM symbol in the PRB used for CSI-RS (l0) |  | 6 for CSI-RS resource 1 and 3 10 for CSI-RS resource 2 and 4
 | CSI-RS offset | Slots | 1 for CSI-RS resource 1 and 2 2 for CSI-RS resource 3 and 4
 | CSI-RS periodicity | Slots | 80 (10ms)
PDCCH configuration | Number of PDCCH candidates and aggregation levels |  | 1/AL8
PDSCH configuration | Mapping type |  | Type A
 | k0 |  | 0
 | Starting symbol (S) |  | 1
 | Length (L) |  | 13
 | PDSCH aggregation factor |  | 1
 | PRB bundling type |  | Static
 | PRB bundling size |  | 2
 | Resource allocation type |  | Type 0
 | RBG size |  | Config2
 | VRB-to-PRB mapping type |  | Non-interleaved
 | VRB-to-PRB mapping interleaver bundle size |  | N/A
PDSCH DMRS configuration | DMRS Type |  | Type 1
 | Number of additional DMRS |  | Option 1: 1 Option 2: 2
 | Maximum number of OFDM symbols for DL front loaded DMRS |  | 1
Propagation channel |  |  | Uni-directional: Derived based on agreed deployment scenario. Bi-directional: Single-Tap channel in TS38.101-4 B.3 but updated parameters.
Antenna configuration |  |  | 2x2 ULA Low Correlation
Number of MIMO layers |  |  | 1
MCS |  |  | Option 1: 16QAM 0.5 (MCS 13 with Table 1) Other options are not excluded

## Slide 14: Way Forward – UE RF Requirement
Baseline power class and UE RF requirement for FR2 HST:
  FFS FR2 HST UE (roof-mounted UE type) RF requirement,
    Follow Rel-15/16 principle of “only one panel to TX/RX at a time”
    Take FR2 PC4 requirement as baseline for discussion:
      FFS spherical coverage requirement and min peak EIRP requirement, based on implementation limitation
Beam correspondence:
  For FR2 HST UE (roof-mounted UE type), Beam Correspondence requirement is FFS, following aspect can be considered:
    how to handle the RF requirements on beam correspondence bit 1 and bit 0 UE capability, based on deployment scenario study;
    FFS the side condition for Beam Correspondence requirement for FR2 HST UE.

## Slide 15: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2102103 | HST FR2 general aspects | Ericsson
R4-2102266 | NR support for high speed train scenario in frequency range 2 (FR2) | Nokia, Nokia Shanghai Bell, Samsung
R4-2100631 | FR2 HST general discussion | Qualcomm, Inc.
R4-2100915 | Further discussion on high speed train deployment scenario in FR2 | Samsung
R4-2100916 | Simulation results and analysis on HST deployment scenario in FR2 | Samsung
R4-2101267 | Discussion on deployment scenarios for NR HST in FR2 | Intel Corporation
R4-2101368 | Discussion on deployment scenarios for FR2 HST | Huawei, HiSilicon
R4-2101856 | Deployment scenarios for HST FR2 | ZTE Wistron Telecom AB
R4-2102093 | Simulation results for HST in FR2 | Nokia, Nokia Shanghai Bell
R4-2102099 | On high-speed train deployment scenario in FR2 | Nokia, Nokia Shanghai Bell
R4-2102104 | HST FR2 deployment aspects | Ericsson
R4-2100632 | FR2 HST RRM discussion | Qualcomm, Inc.
R4-2100918 | Discussion on UE RF requirement for FR2 HST | Samsung
R4-2102561 | Power Class 4 for HST | Nokia, Nokia Shanghai Bell
R4-2102679 | Consideration on UE requirements for FR2 HST | Ericsson

## Slide 16: Reference
[1] R4-2103328, “Email discussion summary for [98e][141] NR_HST_FR2_enh”, Samsung