## Slide 1: WF on coexistence evaluation for NR SL enh. in Rel-17
LG Electronics
­­­3GPP TSG-RAN WG4 Meeting # 98-e R4-2103241
Electronic Meeting, 25th Jan. – 05th Feb., 2021

## Slide 2: Background
In RAN4 #98-e meeting, following coexistence issues are discussed.
  1.2.3 Sub-topic #1-3
  Sub-topic description: Coexistence evaluation for public safety
    Issue 1-3-1: FDD band coexistence evaluation for public safety
    Proposals
      Option 1: RAN4 need coexistence evaluation in FDD band regardless of operator proposal in FDD band for SL operation
      Option 2: RAN4 can consider the coexistence evaluation in FDD band based on operator proposal in FDD band for SL operation.
    Issue 1-3-2: Whether study for coexistence evaluation in n14 or not
    Proposals
      Option 1: RAN4 need coexistence evaluation in n14
      Option 2: No, RAN4 do not need coexistence evaluation for both PC1 and PC3 since NR SL operation in n14 is only allowed in out-of-coverage based in AT&T operating scenarios.

## Slide 3: Background
In RAN4 #97-e meeting, work plan [2] was approved in FR2 as follow
  RAN4 # 98-e (2021 Jan.)
    Discussion
      General scope to introduce NR SL enhancement for RF requirements at FR1
      n79 partial used SL operation with NR n79 Uu
      High power UE for SL enhancements
        Single antenna High power UE and UL-MIMO high power UE
      Other RF issues
    Agreement
      If FR2 operating bands are identified, related work plan will be updated, otherwise, FR2 discussion will be closed.

## Slide 4: WF on coexistence evaluation in FR1
  Issue 1-3-1: FDD band coexistence evaluation
    In WID [1], RAN4 need to study on coexistence evaluation in the exact band request for both FR1 and FR2 as follow
      4. Support of new sidelink frequency bands for single-carrier operations [RAN4]
        Support of new sidelink frequency bands should ensure coexistence between sidelink and Uu interface in the same and adjacent channels in licensed spectrum.
        The exact frequency bands are to be determined based on company input during the WI, considering both licensed and ITS-dedicated spectrum in both FR1 and FR2.
    Currently, only n14 was requested to specify the new SL enh. Operating band in Rel-17.
      The Public safety UE in n14, only operated in the out-of-coverage. RAN4 expect to not to coexistence evaluation in n14.
    Based on current status and recommendation in WID, RAN4 can decide as follow
      WF:
      RAN4 can consider the coexistence evaluation in FDD band based on operator proposal in FDD band in Rel-17.
      The new FR1 SL enh. operating bands should be requested until May 2021 to evaluate the FDD coexistence evaluation in Rel-17, otherwise, RAN4 can close discussion on new FDD band in Rel-17.

## Slide 5: WF on coexistence evaluation in FR1
  Issue 1-3-2: Whether study for coexistence evaluation in n14 or not
    In AT&T operating scenario paper [3], they propose to specify PC1 and PC3 SL enh. UE in n14.
    AT&T will operate the SL enh. UE in n14 as same Prose UE in Band 14 with PC1 and PC3 UE.
      However, the use case for sidelink operation in NR Band n14 is for emergency situations where the UE is out of network coverage for NR and LTE and Uu operation is not possible.
    Based on e-mail discussion, RAN4 can decide as follow
      WF:
      Based on interesting operator’s operating scenarios [3], there is no Uu service for the whole band in out-of-coverage scenario. Hence, RAN4 conclude that the co-existence evaluation in n14 for out-of-coverage scenario is not needed.

## Slide 6: WF on coexistence evaluation in FR2
  New SL operating band request in FR2
    In this meeting, any operator did not request to study the coexistence evaluations in FR2 for NR SL enhancement in Rel-17.
    Based on approved work plan [2], RAN4 can close FR2 NR SL enh. operations request.
      WF:
      RAN4 do not need to update the work plan to add FR2 SL enh. operation. Also RAN4 close FR2 discussion in NR SL enhancement.

## Slide 7: References
RP-202846, “WID revision: NR sidelink enhancement”, LG Electronics, 3GPP TSG-RAN Meeting # 90-e
R4-2016924, “Work plan for NR sidelink enhancement in Rel-17”, LG Electronics, 3GPP TSG-RAN WG4 #97-e
R4-2103005, “Additional Information for SL Operation in NR Band n14, AT&T, 3GPP TSG-RAN WG4 #98-e