## Slide 1: WF on MPR&AMPR simulation assumption for NR V2X intra-band con-current operation
LG Electronics
R4-2103246
3GPP TSG-RAN WG4 Meeting #98-e
Electronic meeting, 25th Jan. – 05th Feb., 2021

## Slide 2: Background on architecture
Issue 1-3-1: Whether the RF architecture of 2UL intra-band CA could apply to V2X intra-band con-current operation in band n79
  Tentative agreements:
    Option 2: No. The RF architecture of 2UL intra-band CA could not simply apply to V2X intra-band con-current operation in band n79
  Recommendations for 2nd round:
    The initial consideration on RF architecture for TDM operation and FDM operation can be discussed in the 2nd round based on the corresponding WF if possible
Issue 1-3-3: Shared RF architecture or separate RF architecture
  Tentative agreements: None.
  Candidate options:
    Option 2: Separate RF architecture.
    Option 3: Decision of shared or separate RF architecture should be left to UE vendors.
  Recommendations for 2nd round:
    Make final decision between option 2 and option 3 in the 2nd round.
1st round discussion results for RF architecture
  Separate RF architecture: LGE, Xiaomi, CATT, Huawei, Hi silicon, vivo
  UE implementation: Qualcomm, Ericsson

## Slide 3: WF on Scope
To derive MPR/A-MPR requirements for NR V2X intra-band con-current operation in a licensed band, both shared and separate RF architectures will be considered
  But some operations (e.g individual power control or different waveforms) will be restricted.
The basic simulation assumptions for intra-band con-current operation in a licensed band can reuse the simulation assumptions in TR38.886 in Rel-16.
The example operating NR V2X band is n79.
Firstly, RAN4 can specify the intra-band contiguous con-current operation with adjacent channel.
  In here, do not allow simultaneous NR UL Transmission and NR SL reception within adjacent channel.
  Target is CA bandwidth class B (2CCs, 20 MHz ≤ aggregated BW ≤ 100 MHz) for NR V2X intra-band contiguous con-current operation.
  For the intra-band non-contiguous con-current operation, RAN4 need further discussion to allow FDM operation and study the frequency gap between NR SL CC and NR Uu CC.

## Slide 4: WF on allocations and waveforms
Define each PSSCH/PSCCH transmission, simultaneous multiple PSFCH transmission and S-SSB transmission for PC3 NR V2X intra-band con-current operation
Inner/outer contiguous allocations definition for PC3 is used to evaluate MPR
Focus on only CP-OFDM waveform in NR SL UE is used.
For NR UE, both CP-OFDM and DFT-S-OFDM waveforms are considered.
To derive A-MPR requirements, RAN4 need to study the regulatory requirements in n79 and other NR V2X operating band, then RAN4 can further discuss the A-MPR requirements to comply the regional regulation requirements.
Channel BW configurations for class B should be evaluated
  Class B: RAN4 evaluate following CBW combinations
    At least 10MHz (NR SL, 30kHz SCS)+10MHz (NR Uu, 30kHz SCS)
    10MHz (NR SL, 30kHz SCS) +20/40/60/80MHz (NR Uu, 30kHz SCS)
    20MHz (NR SL, 30kHz SCS) + 20/40/80MHz (NR Uu, 30kHz SCS)
  Other CBW combinations are not precluded

## Slide 5: WF on assumptions for MPR/A-MPR evaluation
parameter | Assumption
center frequency | 4.5GHz (n79)
Each Bandwidth | 10/20/30/40MHz for NR SL 10/20/40/60/80MHz for NR Uu
Maximum total output power | 23dBm
numerology | 15KHz, 30kHz and 60kHz
Modulation | QPSK/16QAM/64QAM/256QAM
Waveform | CP-OFDM for NR SL CP-OFDM or DFT-S-OFDM for NR Uu
Carrier leakage | 25dBc
IQ image | 25dBc
CIM3 | 45~60dBc
PA calibration | PA calibrated per CC to deliver -30dBc ACLR for a fully allocated RBs in 20MHz QPSK DFT-S-OFDM waveform at 1dB MPR.

## Slide 6: WF on assumptions for MPR A-MPR evaluation
Items | Assumption
Allowed sub-channel sizes for NR SL | Support {10, 12, 15, 20, 25, 50, 75, 100} PRBs for NR SL. No restriction of size of RB for NR Uu.
Allowed LCRB allocation for NR SL | 10,12,15,20, 24, 25,30,36, 40,45,48,50,60,70,72, 75,80,84, 90,96,100,105,108,110,120,130,132,135,140,144,150,156,160,165,168,170,175,180,190,192,195,200,204,210, 216. No restriction of LCRB for NR Uu.
Regarding PSCCH / PSSCH multiplexing for NR SL | 
PSCCH size for NR SL | 10RB*3 Symbols
PSD offset of X dB between PSCCH and PSSCH for NR SL | 0dB
* If there is not indicate the detail parameters, then follow TR38.886 for NR SL operation. Also follow TS38.211/TS38.212/TS38.101-1 for NR Uu operation

## Slide 7: References
R4-2102991, “Email discussion summary for [98e][143] NRSL_enh_Part_2, CATT, 3GPP TSG-RAN WG4 #98-e
R4-2100283, “Consideration on partial usage operation with PC5 and Uu in a licensed band, LGE, 3GPP TSG-RAN WG4 #98-e
R4-2101877, “Synchronous operation between NR Uu and NR SL in an operating band, Xiaomi, 3GPP TSG-RAN WG4 #98-e