## Slide 1: WF on NR BCS4 RAN4 #98e
Ericsson
R4-2103271
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25 January – 5 February 2021

## Slide 2: Sub-topic 1-1: BCS4 for all combinations or only requested combinations
There is no agreement on sub-topic 1-1 so this remains to be discussed at next meeting:
  Discuss and agree if BSC4 should be introduced for all combinations or if only for requested combinations
  One way suggested is to have BCS4 applied for all combinations, but there are considerations that some BW combination cases may not have a concrete deployment scenario and that therefore there also must be possibilities for specific (traditional) BCS’s on a case-by-case basis.
  Above suggestions, and possible others, need to be discussed further.

## Slide 3: Sub-topic 1-2: Configuration tables
There are no agreements on sub-topic 1-2 so these remain to be discussed at the next meeting:
  Proposal 1. Using the R4-2102187 templates in Table 1-3 and Table 1-4, Table 1-5 and Table 1-6 for xUL/2DL and 1UL/3DL&/2UL/3DL NR CA/DC BCS4 band combination configurations requesting, respectively –
  Proposal 2. When BCS4 is requested, direct CR approach is precluded. BCS4 request shall first analyse impact on specifications in TP. Once TP/draft CR are approved for BCS4, BCS0/1/2/3 combinations are completed by default for the same band combination.
  Proposal 3. It is needed to include BCS4 configurations in configurations tables in the 38.101-1 (clause 5.5A.3.1) and TS38.101-3(clause 5.5A.1). The templates in Table 1-4 and Table 1-6 without SCS column can be applied

## Slide 4: Sub-topic 2.1: MSD requirements
There is one agreement reached:
  MSD due to UL harmonics to be used suggested as in the draft CR R4-2102150 for below parts
    Only DL victim CBW change needs to be considered,
    In case of full harmonic overlap of DL victim, calculation method proposed by [Bill-excel] is applicable,
  Note: a revision of R4-2102150 is needed and to be sent for email approval
For below bullet points there are no agreements reached need to be further discussed at the next coming meeting:
  For the case of MSD due to UL Harmonics:
    In case of near-miss, or partial victim overlap, MSD needs to be re-assessed,
  For the case of MSD due to cross-band isolation:
    MSD needs to be revisited to account for both the changes in UL aggressor CBW and DL victim CBW,
    Consider general principles proposed in [R4-2102928], other guidelines are not precluded,
  When BCS4 is not applied some MSD test points may not be configured for certain markets,
  Discuss if to change MSD method and representation or whether to use existing MSD tables and fill in the gaps
  BCS4 impact on MSD specifications should always be first studied in discussion paper.

## Slide 5: Sub-topic 3.1: Signalling
There are no conclusions on signaling. All four options remain to be discussed further at next meeting:
Option 1
  R4-2101371 by Xiaomi, introduce a new UE signalling with BCS4 in IE FeatureSetDownlinkPerCC, i.e., channelBWs-UL-ca/channelBWs-DL-ca. The signalling allows UE report the channel bandwidths it supports by bitmap on one carrier of a band of a band combination, and absence of the signalling for a CC means that the UE supports all channel bandwidths in this CC as single carrier operation. Send LS to RAN2 to ask for introduction of such signalling.
Option 2
  R4-2102188 by ZTE and R4-2101817 by Huawei, Signalling of BCS4 support per band combination
Option 3
  R4-2102502 by Qualcomm, RAN4 to agree to use the method of BCS4 signalling with additional minimum channel bandwidth supporting on each CC for the band combination reporting via multiple feature sets. Send an LS to RAN2 to inform above RAN4 agreement. RAN2 to introduce the signalling for minimum channel bandwidth supporting on each CC for the band combination and to allow UE signalling maximum and minimum channel bandwidth supporting on each CC for the same band combination via multiple feature sets
Option 4
  R4-2100088 by Nokia, introduce a new capability for a UE to indicate the supported minimum CBW per SCS per CC per NR band within a band configuration and allow the UE to indicate supported CBW combinations for a CA configuration via Feature Sets. Send an LS to inform RAN2 of a necessity of the new capability mentioned in Proposal 1 and a relevant feature set(s) to have an equivalent functionality that the traditional BCS has