## Slide 1: WF on frequency bands for testing of A-GNSS Sensitivity requirements in NR and LTE
Apple, Xiaomi
3GPP TSG-RAN WG4#98-e Meeting R4-2103287
Electronic Meeting, Jan. 25 – Feb. 5, 2021

## Slide 2: Background
At this meeting, there are two contributions submitted in response to RAN5 LS (R4-2100021).
  [1] R4-2100196 Analysis of RF interferences to A-GNSS Sensitivity requirements in NR and LTE, Apple
  [2] R4-2101923 Frequency Bands for testing of A-GNSS Sensitivity in EN-DC, Qualcomm

## Slide 3: Way Forward – LTE and NR bands for testing
In [1], there are 4 LTE bands (13, 14, 24, 44) and 5 NR bands (n13, n14, n24, n79 and n96 ) identified that may have interference to A-GNSS operating in the RNSS band 1559-1610MHz.
There are three options discussed:
  Option 1: Repeat the test in all UE supported bands (Spirent)
  Option 2: Repeat the test in a subset of UE supported bands (Apple, Xiaomi, Qualcomm’s 2nd preference)
  Option 3: Perform the test in any bearer band supported by the UE (i.e., only 1 (any) band is enough) (Qualcomm’s 1st preference).
Agreements:
  TBD

## Slide 4: Way Forward –EN-DC combinations for testing
In [1], a number of EN-DC band combinations are identified that may have IMD interference to A-GNSS operating in the RNSS band 1559-1610MHz.
  111 combinations if up to 5th IMDs are considered
  50 combinations if up to 3rd IMDs are considered
In [2], it is proposed to:
  Focus on "high-risk UL band combinations" that can cause impacts to A-GNSS sensitivity.
  The "high-risk UL band combinations" should be those UL band combinations that can generate second or third order intermodulation (IM) products falling into the GNSS bands.
Agreements:
  It is agreed to focus the testing on “high-risk UL band combinations” that generate 2nd or 3rd IMDs falling into the GNSS bands.

## Slide 5: Way Forward
Regarding GNSS band(s) to be considered in RAN4 analysis when identifying LTE/NR bands or high-risk UL band combinations for testing, two options:
  Option 1:
    1559-1610MHz
    1164-1300MHz
  Option 2:
    1559-1610MHz
As RAN4 continues to introduce new bands or new EN-DC band combinations, the list of bands or band combinations needs to updated as well:
  Option 1: the list is documented in TS 38.171, i.e. maintained by RAN4
  Option 2: the list is documented in TS 37.571-1, i.e. maintained by RAN5

## Slide 6: Plan for Next Meeting
Interested companied are requested to provide more analysis to the next meeting to decide among options in previous slides which one to pick
  A list of high-risk UL band combinations will be decided based on companies’ IMD analysis at next meeting
A reply LS to RAN5 is expected to be agreed at the next meeting