## Slide 1: WF on bands plans for further study and duplex filter options
Nokia
R4-2103372
3GPP TSG-RAN WG4 #98-e
Jan 25 – Feb 05, 2021
Electronic meeting

## Slide 2: Unresolved Issues
Band plans to be studied
Duplex filter bandwidths
Center band gap
Single or dual duplexers

## Slide 3: Agreements
Band plan
  Option B1 and B2 is further studied as baseline to respond to the request of APT/AWG.
  Other options can be studied as well, if such options are considered to better address the device performance, cost and ecosystem issues, etc.
  Companies are encouraged to study how to benefit from band n71 ecosystem with these options.

## Slide 4: Agreements
Duplex filter options
  Companies are encouraged to provide further analysis whether single duplexer more than 35 MHz pass band can be ruled out.
  Companies are encouraged to provide further analysis whether the following split duplexer assumptions can be used.
    One of the duplexers supports band n71, another duplexer covers (at least) the extended frequency range for APT.
    Other split-duplexer arrangements that facilitate support of 71/n71 (and hence the requirements for 71/n71)
  Companies are encouraged to further analyze the feasibility of duplexers w.r.t.
    Insertion loss and isolation for different center gap and pass band sizes.
    Coexistence with own band, band 28, DTV, RAS etc., e.g., by means of filter isolation, uplink RB restriction, or A-MPR, etc.
    Compatibility with band n71