## Slide 1: WF on test configurations for NR-U RRM performance requirements all agreements in RAN4#98-e from: [98e][206] NR_unlic_RRM_2, topic #2
Ericsson
3GPP TSG-RAN WG4 Meeting #98-e R4-2103520
Electronic Meeting, Jan. 25-Feb. 5, 2021
Agenda Items: 7.1.6

## Slide 2
Agreements from the 1st GTW session
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: Test Cases for Cell Re-Selection (sub-topic 2-2)
Issue 2-2-1:
  Test configurations for NR-U -> NR-U:
    1: Cells with CCA: NR 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
  Test configurations for NR-U -> NR and NR-> NR-U
    1:
      Cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 15 kHz SSB SCS, 10 MHz bandwidth, FDD duplex mode
    2:
      Cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 15 kHz SSB SCS, 10 MHz bandwidth, FDD duplex mode
    3:
      Cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
Issue 2-2-3:
  Reselection test shall verify that maximum allowed CCA failures for Md, Mm and Me

## Slide 4: Test Cases for HO (sub-topic 2-3)
Issue 2-3-1:
  Test configurations for NR-U -> NR-U:
    1: Cells with CCA: NR 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
  Test configurations for NR-U -> NR and NR-> NR-U
    1:
      Cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 15 kHz SSB SCS, 10 MHz bandwidth, FDD duplex mode
    2:
      Cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 15 kHz SSB SCS, 10 MHz bandwidth, FDD duplex mode
    3:
      Cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
  Test configuration for E-UTRAN -> NR-U
    1: LTE FDD, NR with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
    2: LTE TDD, NR with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
Issue 2-3-3: Handover delay verified in test requirements is expressed using a formula containing L1, L1’, L2 and L3 depending on the type of test case, and the total delay is limited by T304 timer

## Slide 5: Test Cases for RRC Re-Establishment (sub-topic 2-4)
Issue 2-4-1:
  At least the following NR-U to NR-U RRC re-establishment tests to verify core requirements in clause 6.2.1A, TS 38.133, are defined:
    TC1: Intra-frequency RRC Re-establishment in FR1 with known target cell subject to CCA
    TC2: Inter-frequency RRC Re-establishment in FR1 with unknown target cell subject to CCA
    TC3: Intra-frequency RRC Re-establishment in FR1 with unknown target cell subject to CCA
Issue 2-4-2: Test configurations for NR-U -> NR-U
  1: Cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
FFS: Issue 2-4-3: NR-U to NR-U RRC re-establishment tests are defined for the following LBT configuration/setting:
    Option 1:
      Serving cell: PCCA_UL=1 and PCCA_DL=1 in all test times
      Target cell: PCCA_UL=1 and PCCA_DL< 1 (e.g. 0.5) in all test times

## Slide 6: Test Cases for RRC Connection Release with Re-Direction (sub-topic 2-5)
Issue 2-5-2: Test configurations for NR-U to NR-U RRC connection release with redirection tests defined for both serving and target cells:
  1: Cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
FFS: Issue 2-5-3:
  NR-U to NR-U RRC connection release with redirection test is defined for the following LBT configuration/setting:
    Option 1:
      Serving cell: PCCA_UL=1 and PCCA_DL=1 in all test times
      Target cell: PCCA_UL=1 and PCCA_DL< 1 (e.g. 0.75) in all test times

## Slide 7: Test Cases for RRC Connection Release with Re-Direction (sub-topic 2-5)
Issue 2-5-2: Test configurations for NR-U to NR-U RRC connection release with redirection tests defined for both serving and target cells:
  1: Cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
FFS: Issue 2-5-3:
  NR-U to NR-U RRC connection release with redirection test is defined for the following LBT configuration/setting:
    Option 1:
      Serving cell: PCCA_UL=1 and PCCA_DL=1 in all test times
      Target cell: PCCA_UL=1 and PCCA_DL< 1 (e.g. 0.75) in all test times

## Slide 8: Test Cases for Transmit Timing (sub-topic 2-6, partly)
Issue 2-6-1:
  Test configurations for SA:
    1: NR cells with CCA: NR TDD, SSB SCS 30 kHz, data SCS 30 kHz, BW 40 MHz
  Test configuration for EN-DC:
    1: LTE FDD; NR cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
    2: LTE TDD, NR cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
FFS: Issue 2-6-2: UE transmit timing tests are defined for the following LBT configuration/setting in SpCell:
    Option 1:
      PCCA_UL=1 and PCCA_DL < 1 depending on SSB periodicity (e.g. 0.5% for TSSB=20 ms) in all test times

## Slide 9: Test Cases for Timing Advance (sub-topic 2-6, partly)
Issue 2-6-3:
  Test configurations for EN-DC:
    Same as for transmit timing
  Test configuration for SA:
    Same as for transmit timing
FFS: Issue 2-6-4: UE timing advance adjustment accuracy tests are defined for the following LBT configuration/setting in SpCell:
    Option 1:
      PCCA_UL=1 and PCCA_DL =1 in all test times

## Slide 10: Test Cases for BWP switching (sub-topic 2-7)
Issue 2-7-1:
  Test configurations for SA:
    1: NR cells with CCA: NR TDD, SSB SCS 30 kHz, data SCS 30 kHz, BW 40 MHz
  Test configuration for EN-DC:
    1: LTE FDD; NR cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
    2: LTE TDD, NR cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
Issue 2-7-2:
  FFS: Periodic SRS is configured in the SpCell to enable the UE to detect consistent UL LBT failure in the SpCell.
  FFS: The tests on BWP switching under consistent UL failure are defined for the following LBT configuration/setting in SpCell:
    Option 1:
Active BWP in SpCell | PCCA_UL | PCCA_DL
UL active BWP before active BWP switching (UL BWP-1) | 0 | 1
UL active BWP after active BWP switching (UL BWP-2) | 1 | 1
DL active BWP before active BWP switching (DL BWP-1) | 1 | 1
DL active BWP after active BWP switching (DL BWP-2) | 1 | 1

## Slide 11: Test Cases for Active TCI State Switching (sub-topic 2-8)
Issue 2-8-1:
  In Rel-16 NR-U, test cases for active TCI state switching are introduced for the following cases:
    EN-DC, NR PSCell under CCA, known TCI state, MAC-based triggering
    EN-DC, NR PSCell under CCA, known TCI state, RRC-based triggering
    NR SA, PCell under CCA, known TCI state, MAC-based triggering
    NR SA, PCell under CCA, known TCI state, RRC-based triggering
    NR SA, SCell under CCA, known TCI state, MAC-based triggering
    NR SA, SCell under CCA, known TCI state, RRC-based triggering

## Slide 12: Test Cases for Interruptions (sub-topic 2-9)
Issue 2-9-1:
  During interruption tests, a deactivated SCell measurement cycle of 160ms is used
Issue 2-9-3:
  The interruption requirements are verified in tests with the following phases
    T1 : UE is configured with PCell and PSCell if applicable, and measures/reports candidate SCell such that it will be known in T2
    T2 : SCell is added, interruption requirement verified
    T3 : SCell is activated, interruption requirement verified
    T4 : SCell is deactivated, interruption requirement verified
    T5 : Deactivated SCell measurement interruption requirement is verified
    T6 : SCell is released, interruption requirement verified

## Slide 13: Test Cases for SCell Activation Delay (sub-topic 2-10)
Issue 2-10-1:
  Define test cases for SCell (de)activation of known SCell in NR-U for both measurement cycles 160 and 320ms
Issue 2-10-3:
  FFS: Test cases for SCell (de)activation testing with NR PCC in FR1 with SCC under CCA are modelled with
    Option 1: only DL CCA in SCell
  FFS: Test cases for SCell (de)activation testing with NR PCC under CCA with SCC under CCA are modeled with
    Option 1: DL CCA in SCell and UL CCA in PCell
  FFS: Test cases for SCell (de)activation testing with NR PSCC under CCA with SCC under CCA are modeled with
    Option 1: DL CCA in SCell and UL CCA in PSCell

## Slide 14: Test Cases for RLM (sub-topic 2-11)
Issue 2-11-1: The following sections are added for RLM test cases:
  For PSCell in Scenario B:
    A.10.3.1.2 Radio link monitoring out-of-sync test for PSCell configured with SSB-based RLM RS in non-DRX mode
    A.10.3.1.3 Radio link monitoring in-sync test for PSCell configured with SSB-based RLM RS in non-DRX mode
    A.10.3.1.4 Radio link monitoring out-of-sync test for PSCell configured with SSB-based RLM RS in DRX mode
    A.10.3.1.5 Radio link monitoring in-sync test for PSCell configured with SSB-based RLM RS in DRX mode
  For PCell in Scenario C:
    A.11.4.1.2 Radio link monitoring out-of-sync test for PCell configured with SSB-based RLM RS in non-DRX mode
    A.11.4.1.3 Radio link monitoring in-sync test for PCell configured with SSB-based RLM RS in non-DRX mode
    A.11.4.1.4 Radio link monitoring out-of-sync test for PCell configured with SSB-based RLM RS in DRX mode
    A.11.4.1.5 Radio link monitoring in-sync test for PCell configured with SSB-based RLM RS in DRX mode
Issue 2-11-2:
  RAN4 develops test cases to verify both sets of RLM out-of-sync requirements:
    For RLM-RS SSB Es/Iot ≥-7 dB, and
    For RLM-RS SSB Es/Iot <-7 dB
  Both requirements are verified in different tests (e.g., Test 1 and Test 2) of the same test case
Issue 2-11-3:
  Test configurations for EN-DC:
    1: LTE FDD; NR cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
    2: LTE TDD, NR cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
  Test configuration for SA:
    1: NR cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode

## Slide 15: Test Cases for BM: BFD and LR (sub-topic 2-12, partly)
Issue 2-12-1: Define the following BFD and LR test cases for NR-U:
  A.10.3.4.1 EN-DC Beam Failure Detection and Link Recovery Test for FR1 PSCell configured with SSB-based BFD and LR in non-DRX mode
  A.10.3.4.2 EN-DC Beam Failure Detection and Link Recovery Test for FR1 PSCell configured with SSB-based BFD and LR in DRX mode
  A.11.4.4.1 Beam Failure Detection and Link Recovery Test for FR1 PCell configured with SSB-based BFD and LR in non-DRX mode
  A.11.4.4.2 Beam Failure Detection and Link Recovery Test for FR1 PCell configured with SSB-based BFD and LR in DRX mode
Issue 2-12-2:
  To verify the different evaluation period (for BFD-RS SSB Es/Iot ≥ -7 dB and (BFD-RS SSB Es/Iot < -7 dB) in Table 8.5A.2.2-1, define the test cases with
    1) BFD-RS SSB Es/Iot ≥ -7 dB and
    2) BFD-RS SSB Es/Iot < -7 dB to verify the different evaluation period.

## Slide 16: Test Cases for BM: L1-RSRP (sub-topic 2-12, partly)
Issue 2-12-4:
  A.9.3.3.1 SSB based L1-RSRP measurement when DRX is not used (SA SCell with NR PCell)
  A.9.3.3.2 SSB based L1-RSRP measurement when DRX is used (SA SCell with NR PCell)
  A.10.4.3.1 SSB based L1-RSRP measurement on PSCC when DRX is not used (EN-DC PSCell)
  A.10.4.3.2 SSB based L1-RSRP measurement on PSCC when DRX is used (EN-DC PSCell)
  A.10.4.3.3 SSB based L1-RSRP measurement on SCC when DRX is not used (EN-DC SCell with LTE PCell and NR-U PSCell)
  A.10.4.3.4 SSB based L1-RSRP measurement on SCC when DRX is used (EN-DC SCell with LTE PCell and NR-U PSCell)
  A.11.5.4.1 SSB based L1-RSRP measurement when DRX is not used (SA PCell)
  A.11.5.4.2 SSB based L1-RSRP measurement when DRX is used (SA PCell)
  A.11.5.4.3 SSB based L1-RSRP measurement on SCC when DRX is not used (SA SCell with NR-U PCell)
  A.11.5.4.4 SSB based L1-RSRP measurement on SCC when DRX is used (SA SCell with NR-U PCell)
Issue 2-12-5:
  For L1-RSRP measurement procedure tests with CCA, reuse the same Es/Ioc as Rel-15 tests
  For NR-U L1-RSRP measurement procedure tests with DRX and non-DRX cases, RAN4 sets the same T1/T2 and reporting timing requirements as Rel-15 test, that is,
    T1=5s, T2=1s.
    TReport=80 slots (Periodic L1-RSRP reporting with PUCCH)
    The UE shall send L1-RSRP report every 80 slots. No later than 640ms plus 80 slots from the beginning of time period T2, UE shall send L1-RSRP report including results of both SSB0 and SSB1 while meeting the absolute accuracy requirement.

## Slide 17: Test Cases for RRM measurements (sub-topic 2-13)
Issue 2-13-1:
  The following test cases are defined for NR-U intra-frequency RRM measurements for PCC, SCC, and PSCC:
    SA event triggered reporting test without gaps under non-DRX,
    SA event triggered reporting test without gaps under DRX,
    SA event triggered reporting test with per-UE gaps under non-DRX,
    SA event triggered reporting test with per-UE gaps under DRX.
  Each test case is conducted for three A3 measurement quantities: SS-RSRP, SS-RSRQ, SS-SINR
Issue 2-13-2:
  For L1-RSRP measurement procedure tests with CCA, reuse the same Es/Ioc as Rel-15 tests
  For NR-U L1-RSRP measurement procedure tests with DRX and non-DRX cases, RAN4 sets the same T1/T2 and reporting timing requirements as Rel-15 test, that is,
    T1=5s, T2=1s.
    TReport=80 slots (Periodic L1-RSRP reporting with PUCCH)
    The UE shall send L1-RSRP report every 80 slots. No later than 640ms plus 80 slots from the beginning of time period T2, UE shall send L1-RSRP report including results of both SSB0 and SSB1 while meeting the absolute accuracy requirement.

## Slide 18: Test Cases for RRM measurements, cont. (sub-topic 2-13)
Issue 2-13-2: Test configurations
  Scenario A:
    1:
      Cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 15 kHz SSB SCS, 10 MHz bandwidth, FDD duplex mode
    2:
      Cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 15 kHz SSB SCS, 10 MHz bandwidth, FDD duplex mode
    3:
      Cell with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
      Cell without CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
  Scenario B:
    1: LTE FDD; NR with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
    2: LTE TDD; NR with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
  Scenario C:
    1: Cells with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
  Inter-RAT E-UTRAN-NR-U:
    1: LTE FDD; NR with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
    2: LTE TDD; NR with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode

## Slide 19: Test Cases for RSSI/CO measurements (sub-topic 2-14)
Issue 2-14-1: Test configurations
  The same as for RRM measurements, for all scenarios including inter-RAT E-UTRA-NR-U
Issue 2-14-3: number of cells
  Scenario A:
    Intra-frequency RSSI/CO: 2 cells (PCell, SCell)
    Inter-frequency RSSI/CO: 2 cells (PCell, SCell) and 1 inter-frequency for RSSI/CO
  Scenario B:
    Intra-frequency RSSI/CO: 2 cells (E-UTRAN PCell, NR PSCell)
    Inter-frequency RSSI/CO: 2 cells (E-UTRAN PCell, NR PSCell) and 1 inter-frequency for RSSI/CO
  Scenario C:
    Intra-frequency RSSI/CO: 1 cell (PCell)
    Inter-frequency RSSI/CO: 1 cell (PCell) and 1 inter-frequency for RSSI/CO
  Standalone Inter-RAT E-UTRAN-NR-U:
    Inter-RAT RSSI/CO: 1 cell (E-UTRAN PCell) and 1 inter-RAT frequency for RSSI/CO

## Slide 20: Test Cases for SFTD measurements (sub-topic 2-15)
Issue 2-15-1: Test configurations for inter-RAT SFTD reporting delay with NR target under CCA
  1: LTE FDD; NR with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
  2: LTE TDD; NR with CCA: 30 kHz SSB SCS, 40 MHz bandwidth, TDD duplex mode
Issue 2-15-2:
  Inter-RAT reporting delay test cases are based on SFTD reporting only, i.e. no additional SS-RSRP reporting
Issue 2-15-3:
  FFS: Test case for inter-RAT SFTD reporting delay for SFTD between EUTRA PCell and NR neighbour cell on NR carrier under CCA is modelled with
    Option 1: DL CCA on the NR carrier

## Slide 21: Test Cases for SFTD measurement accuracy (sub-topic 2-16)
Issue 2-16-1: Test configurations for inter-RAT SFTD accuracy
  Same as for inter-RAT SFTD reporting delay

## Slide 22: Other: Test Cases Applicability for 4RX UEs (issue 2-11-6)
For NR-U, all relevant test cases (e.g., RLM, BM, …) have to also cover 4 RX UEs (similar to legacy Rel-16 NR)
  SNR test points for RLM, BFD, and LR tests with CCA should be adjusted for UEs capable of 4Rx, i.e., set lower SNR test point than the tests for 2Rx UEs