## Slide 1: WF on remaining issues for power saving RRM
Agenda Item: 7.6.1
Document for: Approval
Source: CATT
3GPP TSG-RAN WG4 #98e R4-2103573
Electronic Meeting, 25 Jan. - 05 Feb., 2021

## Slide 2: WF on RRM core requirements maintenance
When Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ and the UE is configured with highPriorityMeasRelax [2] then the UE shall search for inter-frequency layers (E-UTRA inter-RAT frequency layers) of higher priority at least every K2*Thigher_priority_search seconds where Thigher_priority_search is described in clause 4.2.2.7 and, K2 = 60. Whether to change “K2* Thigher_priority_search” to “1 hour” directly?
  Option 1: Yes. Accept the proposal in R4-2101383. Change it to “1 hour” (vivo, Qualcomm, Huawei)
  Option 2: No. still use current K2* Thigher_priority_search , Thigher_priority_search = 60 * Nlayers, The difference from option 1 is 1 hour * Nlayers (CATT, Apple, Xiaomi, Ericsson, MTK)

## Slide 3: WF on RRM test case maintenance
Whether to consider UE gain G for two test cases of FR2 inter-frequency measurement?
  Option 1: No. Use the same principle as legacy R15 FR2 inter-frequency measurement.
  Option 2: Yes. FFS: considering UE gain G for FR2 inter-frequency measurement is not precluded.
    Why and how to reflect to the test parameters including thresholds?
    Further check whether similar issue exists in corresponding test cases in R15.

## Slide 4: References
[1] R4-2101383 CR for removing K2 for R16 UE power saving
[2] R4-2103572 Correction to relexed cell reselection requirements R16
[3] R4-2100473 Discussion on remaining issues for UE power saving test case
[4] R4-2102246 Changes to cell reselection tests under power saving